## Slide 1
Results on Weighted Prediction in 3D Video Coding (JCT3V-B0134)
10. 13. 2012
Jiwook Jung, Hongbin Liu, Jaewon Sung , Jie Jia, Sehoon Yea (LG)

## Slide 2
Weighted Prediction (WP)
  - useful for coding fading sequences (normative tool in HEVC)
HTM computes the WP parameters independently for each view
  - Currently non-CTC, the current implementation buggy
In principle, the fading in/out effect apply to all views simultaneously with the same magnitude
  - predominantly a temporal effect
Backdrop

## Slide 3
Provides a SW bug-fix that would make the WP in the HTM work
Propose to inherit WP parameters for a dependent view
  by inheriting from the base view when available
  by setting to default values (weight 1, offset 0) when unavailable
Results
- BD-Rate savings: -7.1%, -7.4%, -2.6% for V1, V2, video only
- Anchor: HTM (with the proposed bug-fix) without inheritance
Contribution
WP Parameters
WP Parameters
Base view
Dependent view

## Slide 4
weighted_pred_flag = 1
Contribution
Y=W*X+O
Set by the encoder per slice
as per RD-consideration
W & O saved in a table for
each ref_pic candidate
Current reference scheme not good & buggy for interview
yes
Copy, if available, from the base-view
Contribution 1
Contribution 2

## Slide 5
Bug Fix on Weighted Prediction in HTM4.0.1
TComRdCostWeightPrediction::xGetSADw( DistParam* pcDtParam) in TComRdCostWeightPrediction.cpp,
pcDtParam->pUsed represents whether the tool InterViewSkip is on or off.
(default setting : InterViewSkip is off in CTC)
Original code
Bug fixed code

## Slide 6
Inheritance of WP parameters for a dependent view
For each temporal reference picture of the dependent view, refPic with refIdx,
A reference picture of the base view picture, refPicBase, having the same POC with refPic is searched
If the refPicBase is found,
  WP_Param( refIdx ) = WP_Param_Base( RefIdx(refPicBase ) )
otherwise,
  WP_Param( refIdx ) = default values (weight 1, offset 0)
The WP parameters for inter-view reference pictures are set equal to default values: 1.0 for weight, 0.0 for offset.
Proposal
LumaWeightL0 parameters of
base view picture
refIdx | 0 | 1
POC | 2 | 0
LumaWeightL0[refIdx] | 1 | 0.5
LumaWeightL0 parameters of
dependent view picture
refIdx | 0 | 1 | 2
POC | 2 | 0 | V0
LumaWeightL0[refIdx] | 1 | 0.5 | 1

## Slide 7
Syntax change
slice_header( ) { | Descriptor
first_slice_in_pic_flag | u(1)
… | 
if( !entropy_slice_flag ) { | 
… | …
if( ( weighted_pred_flag && slice_type = = P) ¦ ¦ ( weighted_bipred_flag = = 1 && slice_type = = B ) ) { | 
if(ViewIdx>0 && !DepthFlag) { | 
base_pred_weight_table_flag | u(1)
if( base_pred_weight_table_flag== 0 ) | 
pred_weight_table() | 
} | 
… | 
} | 
base_pred_weight_table_flag equals to 1 specifies that the weighted prediction parameter
for the texture of dependent view are inherited from the texture picture of base view.
When the base_pred_weight_table_flag is not present, it is inferred to be 0.

## Slide 8
Decoding process for WD

## Slide 9
Decoding process for WD

## Slide 10
Test Sequences
Fading sequences
  The fading tool used in HEVC (JCTVC-E041) applied to 3DV Sequences
  A linear fade in/out on each of the Y, U, V components
  First 2-seconds of texture videos
  : linear fade-out for 0 ~ 1 sec interval
  : linear fade-in for 1~2 sec interval
  : fading in/out strength [0.25,1]

## Slide 11
Simulation result 1
Anchor : WP Off
Test : WP On (weight and offset for inter-view ref. pic are set to 1.0, 0.0 by Enc)
 | video 0 | video 1 | video 2 | video only | enc time | dec time
Balloons | -36.0% | -19.5% | -17.5% | -29.6% | 158.0% | 100.0%
Kendo | -18.6% | -3.6% | -2.5% | -13.1% | 192.6% | 102.0%
Newspapercc | -33.0% | -22.5% | -23.9% | -29.3% | 140.7% | 93.7%
GhostTownFly | -29.6% | -2.5% | -5.0% | -24.8% | 162.1% | 105.0%
PoznanHall2 | -32.1% | -11.4% | -12.1% | -24.2% | 166.7% | 100.5%
PoznanStreet | -27.5% | -15.4% | -14.3% | -24.4% | 136.9% | 102.6%
UndoDancer | -37.2% | -19.9% | -23.8% | -33.2% | 156.2% | 102.1%
1024x768 | -29.2% | -15.2% | -14.6% | -24.0% | 162.4% | 98.5%
1920x1088 | -31.6% | -12.3% | -13.8% | -26.7% | 155.0% | 102.5%
average | -30.6% | -13.6% | -14.2% | -25.5% | 158.1% | 100.8%

## Slide 12
Simulation result 2
Anchor : WP Off
Test : WP On, WP parameter inheritance
 | video 0 | video 1 | video 2 | video only | enc time | dec time
Balloons | -36.0% | -26.3% | -25.1% | -32.0% | 161.1% | 101.5%
Kendo | -18.6% | -12.9% | -11.9% | -16.4% | 193.4% | 102.3%
Newspapercc | -33.0% | -28.2% | -29.2% | -31.3% | 143.9% | 94.8%
GhostTownFly | -29.6% | -11.6% | -12.2% | -26.2% | 164.0% | 104.0%
PoznanHall2 | -32.1% | -18.6% | -19.9% | -27.0% | 168.7% | 98.6%
PoznanStreet | -27.5% | -19.1% | -19.4% | -25.5% | 141.8% | 101.1%
UndoDancer | -37.2% | -23.8% | -26.7% | -33.9% | 158.4% | 102.2%
1024x768 | -29.2% | -22.5% | -22.1% | -26.6% | 164.9% | 99.5%
1920x1088 | -31.6% | -18.3% | -19.6% | -28.2% | 157.9% | 101.5%
average | -30.6% | -20.1% | -20.7% | -27.5% | 160.9% | 100.6%

## Slide 13
Simulation result 3
Anchor : WP on (weight and offset for inter-view ref. pic are set to 1.0, 0.0 by Enc)
Test : WP on WP parameter inheritance
 | video 0 | video 1 | video 2 | video only | enc time | dec time
Balloons | 0.0% | -8.2% | -9.1% | -3.4% | 102.0% | 101.5%
Kendo | 0.0% | -9.9% | -9.7% | -3.9% | 100.4% | 100.2%
Newspapercc | 0.0% | -7.3% | -6.8% | -2.8% | 102.3% | 101.2%
GhostTownFly | 0.0% | -9.2% | -8.1% | -1.9% | 101.2% | 99.0%
PoznanHall2 | 0.0% | -8.1% | -8.6% | -3.6% | 101.2% | 98.1%
PoznanStreet | 0.0% | -4.3% | -6.0% | -1.4% | 103.6% | 98.5%
UndoDancer | 0.0% | -4.7% | -3.6% | -1.1% | 101.4% | 100.1%
1024x768 | 0.0% | -8.4% | -8.5% | -3.4% | 101.6% | 101.0%
1920x1088 | 0.0% | -6.6% | -6.6% | -2.0% | 101.8% | 98.9%
average | 0.0% | -7.4% | -7.4% | -2.6% | 101.7% | 99.8%

## Slide 14
Simulation result 4
Anchor : WP On
Test : WP On, WP parameter inheritance
 | video 0 | video 1 | video 2 | video only | enc time | dec time
Balloons | 0.0% | -8.1% | -8.9% | -3.3% | 102.7% | 98.2%
Kendo | 0.0% | -8.6% | -9.1% | -3.5% | 100.4% | 98.9%
Newspapercc | 0.0% | -7.3% | -6.6% | -2.7% | 102.9% | 97.8%
GhostTownFly | 0.0% | -8.6% | -9.6% | -1.9% | 101.1% | 98.0%
PoznanHall2 | 0.0% | -8.6% | -4.9% | -2.6% | 101.4% | 96.1%
PoznanStreet | 0.0% | -4.0% | -5.2% | -1.2% | 104.3% | 95.5%
UndoDancer | 0.0% | -4.5% | -3.1% | -0.9% | 101.5% | 96.9%
1024x768 | 0.0% | -8.0% | -8.2% | -3.2% | 102.0% | 98.3%
1920x1088 | 0.0% | -6.5% | -5.7% | -1.7% | 102.1% | 96.6%
average | 0.0% | -7.1% | -6.8% | -2.3% | 102.1% | 97.3%

## Slide 15
Conclusion
This contribution proposed the inheritance of WP parameters for dependent views from the base view.
BD-rate gains are -7.1%, -6.8%, -2.3% for V1, V2, video only
We recommend to adopt the proposal.