## Slide 1
3D-CE5.h Modified disparity vector derivation process
for memory reduction
(JCT2-B0135)
LG Electronics
Convergence Lab.
Jaewon Sung, Moonmo Koo, Sehoon Yea

## Slide 2: DV-MCP Block
Motion compensated prediction block whose MV is predicted by inter-view predicted temporal motion
To indicate it’s a DVMCP block,
  a flag is set to true,
  the correspondence vector is saved..
VID 0
VID1
DvMcpFlag
CorrespondenceVector
POC
MCP
Correspondence Vector

## Slide 3: Memory increase by using the DV-MCP blocks
Disparity derivation process,
  step1) Search DCP blocks in the neighbor blocks, if not found goto step 2). Otherwise stop.
  step2) Search DV-MCP blocks in the neighbor blocks until one with DvMcpFlag =1 is found.
For step2), additional DV-MCP information is saved for each 4x4 partition
  - motion vector, reference index, ... + (DvMcpFlag, CorrespondenceVector)
B2
Current
PU
B1
B0
A0
A1
DvMcpFlag
CorrespondenceVector
DvMcpFlag
CorrespondenceVector
DvMcpFlag
CorrespondenceVector

## Slide 4: Proposed algorithm
Disparity derivation process,
  step1) Search DCP blocks in the neighbor blocks, if not found goto step 2). Otherwise stop.
  step2)
    if above blocks (B0, B1, B2) belong to different LCU,
      Search DV-MCP blocks in the neighbor blocks except for the above blocks
    Else,
      Search DV-MCP blocks in the neighbor blocks
No additional information need to be saved for the above LCUs
B2
Current
PU
B1
B0
A0
A1
DvMcpFlag
CorrespondenceVector

## Slide 5: Results
Anchor: HTM 4.0.1 with CTC
Performance of the proposed algorithm:
  For V1 and V2, 0.0%, 0.2% BD rate losses, respectively.
  Did not affect the overall coding gains for video only, synthesize, and coded & synthesized.
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | Enc time | Dec time | Ren time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.1% | 98.6% | 93.4%
Kendo | 0.0% | 0.0% | 0.2% | 0.1% | 0.0% | 0.0% | 99.8% | 96.4% | 91.3%
Newspapercc | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 99.3% | 98.9% | 91.6%
GhostTownFly | 0.0% | -0.1% | 0.2% | 0.0% | 0.0% | 0.0% | 100.4% | 98.9% | 110.9%
PoznanHall2 | 0.0% | 0.4% | 0.5% | 0.2% | 0.2% | 0.2% | 100.2% | 98.3% | 102.1%
PoznanStreet | 0.0% | -0.3% | 0.0% | 0.0% | 0.0% | 0.0% | 99.8% | 100.9% | 97.5%
UndoDancer | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 100.5% | 100.5% | 108.9%
1024x768 | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 99.7% | 98.0% | 92.1%
1920x1088 | 0.0% | 0.0% | 0.2% | 0.1% | 0.0% | 0.0% | 100.2% | 99.6% | 104.7%
average | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 0.0% | 100.0% | 98.9% | 99.1%

## Slide 6: Conclusion
Proposed algorithm reduced the amount of memory needed for DV-MCP
BD-rate changes
  0.0%, 0.2%, 0.0%, 0.0%, 0.0% for V1, V2, video only, synthesize, coded & synthesized
We recommend to adopt the proposed simplification.