## Slide 1
1. Summary
2. Proposed Method
3. Experimental Results
4. Conclusion
Contents
CE 6 related: Applying Depth Look-up Table to Intra Modes of Depth Map (JCT3V-E0157)
China TV Lab. / Media Part
Hongbin Liu, Jie Jia
(LG Electronics)

## Slide 2: Summary
Proposed Method
  Apply DLT to all intra modes of depth map.
Performance
  CTC: -0.29% coding gain for synthesized view, and -0.50% coding gain for sequences using DLT.
  AI: -0.54% coding gain for synthesized view, and -0.94% coding gain for sequences using DLT.
  When combined with JCT3V-Exxxx, -0.94% coding gain for synthesized view
Crosscheck
  JCT3V-Exxxx (by Qualcomm)
JCT3V-E0157

## Slide 3: Proposed Method
Basic idea
  Generate residual as the difference of DLT index of original pixel value and prediction pixel value.
  Encoder
  resi[x] = DepthValue2Idx [org[x]] – DepthValue2Idx[pred[x]] (1)
  Rate distortion optimized selection between proposed method and method in 3D-HEVC is performed, and 1 flag is encoded for each intra coded (excluding SDC) depth CU to indicate which method is used.
  Decoder
  rec[x] = Idx2DepthValue [DepthValue2Idx[pred[x]] + resi[x] ] (2)
  Complexity increase: 2 look up table operation for each pixel.
JCT3V-E0157

## Slide 4: Compare with HTM-7.0r1 (CTC)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.00% | 0.02% | -0.04% | -0.02% | -0.33% | -0.30% | 87.5% | 98.9%
Kendo | 0.00% | 0.16% | -0.05% | 0.03% | -0.50% | -0.61% | 108.0% | 98.9%
Newspaper_CC | 0.00% | 0.05% | -0.09% | 0.00% | -0.70% | -0.93% | 90.1% | 99.1%
GT_Fly | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 107.7% | 98.7%
Poznan_Hall2 | 0.00% | 0.01% | 0.21% | 0.01% | -0.14% | -0.17% | 88.5% | 98.8%
Poznan_Street | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 86.7% | 98.5%
Undo_Dancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 107.7% | 98.7%
1024x768 | 0.00% | 0.08% | -0.06% | 0.00% | -0.51% | -0.61% | 95.2% | 99.0%
1920x1088 | 0.00% | 0.00% | 0.05% | 0.00% | -0.04% | -0.04% | 97.6% | 98.7%
average | 0.00% | 0.03% | 0.00% | 0.00% | -0.24% | -0.29% | 96.6% | 98.8%
JCT3V-E0157

## Slide 5: Compare with HTM-7.0r1 (AI)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.00% | 0.00% | 0.00% | 0.00% | -0.79% | -0.96% | 185.0% | 106.7%
Kendo | 0.00% | 0.00% | 0.00% | 0.00% | -0.92% | -1.07% | 189.7% | 105.9%
Newspaper_CC | 0.00% | 0.00% | 0.00% | 0.00% | -0.94% | -1.15% | 180.2% | 110.0%
GT_Fly | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 100.2% | 99.6%
Poznan_Hall2 | 0.00% | 0.00% | 0.00% | 0.00% | -0.37% | -0.61% | 190.9% | 104.0%
Poznan_Street | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 102.6% | 99.6%
Undo_Dancer | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | 100.4% | 99.9%
1024x768 | 0.00% | 0.00% | 0.00% | 0.00% | -0.88% | -1.06% | 185.0% | 107.6%
1920x1088 | 0.00% | 0.00% | 0.00% | 0.00% | -0.09% | -0.15% | 123.5% | 100.8%
average | 0.00% | 0.00% | 0.00% | 0.00% | -0.43% | -0.54% | 149.9% | 103.7%
JCT3V-E0157

## Slide 6: Compare JCT3V-E0157 + JCT3V-E0156 with HTM-7.0r1 (CTC)
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time
Balloons | 0.00% | 0.00% | -0.07% | -0.02% | -0.23% | -0.71% | 86.9% | 101.7%
Kendo | 0.00% | 0.15% | -0.27% | -0.03% | -0.38% | -1.16% | 115.1% | 100.9%
Newspaper_CC | 0.00% | -0.02% | 0.03% | 0.01% | -0.37% | -1.33% | 87.0% | 101.6%
GT_Fly | 0.00% | -0.98% | -1.06% | -0.25% | 0.06% | -1.10% | 105.4% | 102.1%
Poznan_Hall2 | 0.00% | -0.22% | 0.20% | -0.02% | 0.19% | -1.14% | 89.8% | 101.5%
Poznan_Street | 0.00% | -0.19% | -0.08% | -0.04% | 0.06% | -0.26% | 88.1% | 102.0%
Undo_Dancer | 0.00% | -0.42% | -0.40% | -0.09% | 0.15% | -0.86% | 105.1% | 101.8%
1024x768 | 0.00% | 0.04% | -0.10% | -0.02% | -0.33% | -1.07% | 96.3% | 101.4%
1920x1088 | 0.00% | -0.45% | -0.33% | -0.10% | 0.12% | -0.84% | 97.1% | 101.9%
average | 0.00% | -0.24% | -0.24% | -0.07% | -0.07% | -0.94% | 96.7% | 101.7%
JCT3V-E0157

## Slide 7: Conclusion
Propose method
  Apply DLT to all intra modes of depth map.
Performance
  -0.29% coding gain for synthesized view
  When combined with JCT3V-E0156, -0.94% coding gain for synthesized view
It is recommended to adopt proposed method into 3D-HEVC
JCT3V-E0157