## Slide 1: JCT3V-E0180 3D-CE5.h related: A simplified method on DMM mode coding in 3D-HEVC
Kai Zhang, Jicheng An, Jian-Liang Lin, Yu-Lin Chang, Shawmin Lei

## Slide 2: Overall Summary
The Problem
  The table index in DMM1 is binarizied as a fixed-length code.
    All bins in the code share one context model.
    These bins can hardly obey the same distribution.
    Two other syntax elements in DMM are coded similarly.
Proposed
  Code these bins in the by-pass way
  Two context models can be removed.
Results
  Cause no BD-rate loss in the common test condition

## Slide 3: The problem
The table index in DMM1 is binarizied as a fixed-length code, all bins in which share one context model.
  It may be inefficient to code them according to a single context model since these bins can hardly obey the same distribution.
The table index in DMM3 and delta_end_abs_minus1 in DMM2 are coded in the similar way.

## Slide 4: Proposed
  Code bins of the table index in DMM1/DMM3 and delta_end_abs_minus1 in DMM 2 in the by-pass mode.
  Two context models can be removed
    The context model for the table index in DMM1 can be removed.
    The context model for the table index in DMM3 can be removed.
    The context model for delta_end_abs_minus1 cannot be removed since it is shared by dmm_delta_end_flag.

## Slide 5: Results
The simplification does not cause a BD-rate loss.
Cross-checked by JCT3V-Exxxx (Thank Hisilicon)
CTC

## Slide 6: Results (Cont.)
AI

## Slide 7: Conclusion
Three syntax elements in DMM is proposed to be coded in the by-pass mode.
Two context models can be removed.
No BD-rate loss in CTC/AI
Suggest to be adopted

## Slide 8: Thank you for your attention!