## Slide 1: JCT3V-E0181 3D-CE6.h: Results on direct simplified depth coding in 3D-HEVC
Kai Zhang, Jicheng An, Jian-Liang Lin, Yi-Wen Chen, Shawmin Lei

## Slide 2: Overall Summary
The Problem
  A two-step ( intra prediction and averaging ) approach is applied to obtain the prediction values in SDC segments
    The two-step method introduces a high complexity
Proposed
  Remove the two-step method
  Instead, the prediction values are calculated from the neighbouring reconstructed samples directly by a simple rule
Results
  0.1% BD-rate saving for the synthesized view in CTC

## Slide 3: The problem
There is a prediction value for each SDC segment
A two-step approach is applied to obtain the prediction values
  First, the normal intra-prediction procedure using neighboring reconstructed samples is invoked to get all the prediction samples in the coded block. DC, Planar and DMM-1 are possible prediction modes.
  Second, the average value of the prediction samples in a segment is calculated as the prediction value for this segment

## Slide 4: Proposed
  What we really want is the final SDC prediction value
    The prediction-averaging process is not necessary
  Direct SDC (dSDC) is proposed to simplify SDC prediction
    The prediction values are calculated from the neighbouring reconstructed samples directly

## Slide 5: Proposed (Cont.)
Initialize: neighbouring reconstructed samples are initialized as before the normal intra-prediction
For mode DMM-1.
  P0 and P1 are derived following the same method in DMM-1.
  P0 and P1 are treated as the final prediction values directly, without filling each prediction samples and calculating the average values
For mode DC.
  P=(A+B+1)>>1
For mode Planar.
  P= (X+Y+1) >> 1.

## Slide 6: Benefits
dSDC simplifies the SDC prediction procedure without changing the reconstruction procedure
The table shows the numbers of operations for an NxN SDC block in the prediction procedure at decoder.
  The number of additions are reduced from O(N2) to only 1 or 2, and all division operations are removed.
 | Anchor |  | dSDC | 
 | Addition | Division | Addition | Division
DC | O(N2) | 1 | 1 | 0
DMM | O(N2) | 2 | 2 | 0
Planar | O(N2) | 1 | 1 | 0

## Slide 7: Results
The simplification does not cause a BD-rate loss.
  Even achieve 0.1% BD-rate saving for the synthesized view in CTC
Cross-checked by JCT3V-Exxxx (Thank Hisilicon)
CTC

## Slide 8: Results (Cont.)
AI

## Slide 9: Conclusion
Propose to calculate prediction values from the neighbouring samples directly by a simple rule
  Reduce the complexity of SDC prediction process
  0.1% BD-rate saving for the synthesized view in CTC
Suggest to be adopted

## Slide 10: Thank you for your attention!