## Slide 1: JCT3V-G0114 AHG 10: Complexity Assessment on Illumination Compensation (IC)
Gwo Giun (Chris) Lee, Bo-Syun Li, Chun-Fu Chen, Zheng-Han Yu, Chun-Hsi Huang
National Cheng Kung University (NCKU)

## Slide 2: Abstract
Complexity assessment on IC
  Number of operations
  Data storage requirement
  Data transfer rate
Complexity at 6464 block with various PU sizes
Coding performance when IC is OFF at HTM-9.0r1
  Video PSNR vs. video bitrate: 0.6% coding loss.
  Video PSNR vs. total bitrate: 0.6% coding loss.
  Synth PSNR vs. total bitrate: 0.4% coding loss.
Notes: video vs. video rate: BD-rate is calculated from the texture PSNR and texture bit-rate
video vs. total rate: BD-rate is calculated from the texture PSNR and total bit-rate (video+depth)
synth vs. total rate: BD-rate is calculated from the synthesized PSNR and total bit-rate (video+depth)

## Slide 3: Outline
Abstract
Introduction to IC
Complexity assessment at PU level
  Number of operations
  Data storage requirement
  Data transfer rate
Overall complexity of IC at 6464 block level
Coding performance without IC
Conclusion

## Slide 4: Introduction to IC
Dependent view
Independent view
Reference block
Current block
Disparity vector
Prediction block generation
Pred =   Ref + 
Prediction block
Parameter  and  derivation
Disparity vectors could be derived from neighboring block based disparity vector (NBDV) or Depth-oriented NBDV (DoNBDV)
Pixels used for deriving parameter α and β

## Slide 5: Introduction to IC
Flowchart of IC
Left and above pixels of current block Left and above pixels of reference block Reference block
Compensation model derivation, α and β
Prediction block generation
Reconstructed block
Left and above pixels of current block Left and above pixels of reference block
α and β
Reference block

## Slide 6: Number of operations (1/4)
Uni-Prediction
  Compensation model, derivation, α and β
    Luma : 4(N-1) additions + 3 subtractions = 4N – 1 additions/subtractions, 2N+3 multiplications, 1 division LUT.
    Chroma: 4((N/2)-1) additions + 3 subtractions = 2N – 1 additions/subtractions, 2(N/2)+3 multiplications, 1 division LUT.
  Prediction block generation:
    Luma : N2 additions, N2 multiplications.
    Chroma: (N/2)2 additions, (N/2)2 multiplications.
N: PU size
Curr(i): left and above pixels of current block, i is the index of one-dimension array pixels
Ref(i): left and above pixels of reference block, i is the index of one-dimension array pixels
Notes: The variable avgShift and avgOffset are derived as follows:
  avgShift = Log2( numSamples / 2) (H‑202)
  avgOffset = 1 << ( avgShift − 1 ) (H‑203)
The variables numerDiv and denomDiv are derived as follows:
  denomDiv= ( ( sumRefSquare + ( sumRefSquare >> 7 ) ) << avgShift ) – ( sumRef * sumRef ) >> precShift (H‑204)
  numerDiv= Clip3( 0, 2 * denomDiv, ( ( sumProdRefCur + ( sumRefSquare >> 7 ) ) << avgShift ) – ( sumRef * sumCur ) >> precShift ) (H‑205)
The variables shiftNumer and shiftDenom are derived as follows:
  shiftDenom = Max( 0, Floor( Log2( Abs( denomDiv ) ) ) − 5 ) (H‑206)
  shiftNumer = Max( 0, shiftDenom − 12 ) (H‑207)
The variables sNumerDiv and sDenomDiv are derived as follows:
  sDenomDiv = denomDiv >> shiftDenom (H‑208)
  sNumerDiv = numerDiv >> shiftNumer (H‑209)

## Slide 7: Number of operations (2/4)
Bi-Prediction
  The number of operations included in uni-prediction should be counted twice.
  Prediction block averaging:
    Luma : N2 additions, N2 shifts.
    Chroma: (N/2)2 additions, (N/2)2 shifts.
PredSamplesX: Prediction samples by Xth uni-prediction

## Slide 8: Number of operations (3/4)
Algebraic expressions of number of operations
  Uni-Prediction
Type of operations | Number of operations per PU | 
 | Luma | Chroma
Add./Sub. | Compensation model derivation: 4(N-1)+3 Pred. block generation: N2 Total: N2+4N-1 | Compensation model derivation: (4(N/2-1)+3)2 Pred. block generation: ((N/2)2)2 Total: ((N/2)2+4(N/2)-1)2
Mul. | Compensation model derivation: 2N+3 Pred. block generation: N2 Total: N2+2N+3 | Compensation model derivation: (2(N/2)+3)2 Pred. block generation: ((N/2)2)2 Total: ((N/2)2+2(N/2)+3)2
Div. LUT | 1 | 12
Numbers colored in orange present two components of chrominance
N: PU size

## Slide 9: Number of operations (4/4)
Algebraic expressions of number of operations
  Bi-Prediction
Type of operations | Number of operations per PU | 
 | Luma | Chroma
Add./Sub. | Two uni-predictions: (N2+4N-1)2 Pred. block averaging: N2 Total: (N2+4N-1)2+N2 | Two uni-prediction: (((N/2)2+4(N/2)-1)2)2 Pred. block averaging: ((N/2)2)2 Total: (((N/2)2+4(N/2)-1)2)2+((N/2)2)2
Shift | Pred. block averaging: N2 | Pred. block averaging: ((N/2)2)2
Mul. | Two uni-predictions: (N2+2N+3)2 Total: (N2+2N+3)2 | Two uni-predictions: (((N/2)2+2(N/2)+3)2)2 Total: (((N/2)2+2(N/2)+3)2)2
Div. LUT | 12 | 122
N: PU size
Numbers colored in orange present two components of chrominance Numbers colored in red present bi-prediction

## Slide 10: Data storage requirement
Algebraic expressions of data storage requirement
  Only Luma component is considered since the storage could be reused.
Data | Data storage requirement | 
 | Uni-Prediction | Bi-Prediction
Left and above pixels of current block | Left neighboring pixels: (N/2) Above neighboring pixels: (N/2) Total: (N/2)+(N/2) | Left neighboring pixels: (N/2) Above neighboring pixels: (N/2) Total: (N/2)+(N/2)
Left and above pixels of reference block | Left neighboring pixels: (N/2) Above neighboring pixels: (N/2) Total: (N/2)+(N/2) | Left neighboring pixels: ((N/2))2 Above neighboring pixels: ((N/2))2 Total: ((N/2)+(N/2))2
Reference block* | Total: N2 | Total: (N2)2
Total | N2+2N | 2N2+3N
*: The storage of reference block could be reused to save the first prediction block due to the fact that the reference is no longer required upon generating the prediction block. Therefore, one N2 is counted.
N: PU size
Numbers colored in red present bi-prediction

## Slide 11: Data transfer rate (1/2)
Algebraic expressions of data transfer rate
  Uni-Prediction
Data | Data storage requirement | 
 | Luma | Chroma
Left and above pixels of current block | Left neighboring pixels: (N/2) Above neighboring pixels: (N/2) Total: (N/2)+(N/2) | Left neighboring pixels: (((N/2)/2))2 Above neighboring pixels: (((N/2)/2))2 Total: (((N/2)/2))2+(((N/2)/2))2
Left and above pixels of reference block | Left neighboring pixels: (N/2) Above neighboring pixels: (N/2) Total: (N/2)+(N/2) | Left neighboring pixels: (((N/2)/2))2 Above neighboring pixels: (((N/2)/2))2 Total: (((N/2)/2))2+(((N/2)/2))2
Reference block | Total: N2 | Total: ((N/2)2)2
Prediction block | Total: N2 | Total: ((N/2)2)2
Total | 2N2+2N | (2(N/2)2+2(N/2))2
N: PU size
Numbers colored in orange present two components of chrominance

## Slide 12: Data transfer rate (2/2)
Algebraic expressions of data transfer rate
  Bi-Prediction
Data | Data storage requirement | 
 | Luma | Chroma
Left and above pixels of current block | Left neighboring pixels: (N/2) Above neighboring pixels: (N/2) Total: (N/2)+(N/2) | Left neighboring pixels: (((N/2)/2))2 Above neighboring pixels: (((N/2)/2))2 Total: (((N/2)/2))2+(((N/2)/2))2
Left and above pixels of reference block | Left neighboring pixels: ((N/2))2 Above neighboring pixels: ((N/2))2 Total: ((N/2)+(N/2))2 | Left neighboring pixels: ((((N/2)/2))2)2 Above neighboring pixels: ((((N/2)/2))2)2 Total: ((((N/2)/2))2+(((N/2)/2))2)2
Reference block | Total: (N2)2 | Total: (((N/2)2)2)2
Prediction block | Total: N2 | Total: ((N/2)2)2
Total | 3N2+3N | (3(N/2)2+3(N/2))2
N: PU size
Numbers colored in orange present two components of chrominance Numbers colored in red present bi-prediction

## Slide 13: Complexity at 6464 block level with various PU sizes
 | Number of operations |  |  |  |  | 
 | Uni-Prediction |  |  | Bi-Prediction |  | 
PU_size | Add./Sub. | Mul. | Div. LUT | Add./Sub. | Mul. | Div. LUT
6464 | 6,650 | 6,409 | 3 | 19,444 | 12,818 | 6
3232 | 7,144 | 6,692 | 12 | 20,432 | 13,384 | 24
1616 | 8,096 | 7,312 | 48 | 22,336 | 14,624 | 96
88 | 6,080 | 5,312 | 64 | 16,256 | 10,624 | 128
 | Data storage requirement (bits) | 
PU_size | Uni-Prediction | Bi-Prediction
6464 | 33,792 | 67,072
3232 | 8,704 | 17,152
1616 | 2,304 | 4,480
88 | 640 | 1,216
 | Data transfer rate (bits per 6464 block) | 
PU_size | Uni-Prediction | Bi-Prediction
6464 | 100,352 | 150,528
3232 | 102,400 | 153,600
1616 | 106,496 | 159,744
88 | 73,728 | 110,592

## Slide 14: Overall complexity of IC at 6464 block
Complexity Metric | Worst case | 
 | Uni-Prediction | Bi-Prediction
Number of operations (Add/Sub) | 8,096 | 22,336
Number of operations (Mul.) | 7,312 | 14,624
Number of operations (Div. LUT) | 64 | 128
Data storage requirement (bits) | 33,792 | 67,072
Data transfer rate (bits per 6464 block) | 106,496 | 159,744

## Slide 15: Coding results without IC
Anchor: HTM-9.0r1
Tested: HTM-9.0r1 without IC and IC is turned off via configuration file
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Balloons | 0.0% | 2.6% | 2.2% | 0.9% | 0.9% | 0.6% | 90.8% | 100.2% | 99.9%
Kendo | 0.0% | 4.6% | 6.0% | 2.0% | 1.8% | 1.5% | 91.4% | 100.4% | 101.0%
Newspaper_CC | 0.0% | 1.2% | 2.5% | 0.8% | 0.7% | 0.6% | 92.0% | 100.9% | 99.5%
GT_Fly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.4% | 95.7% | 96.9%
Poznan_Hall2 | 0.0% | 1.4% | 4.0% | 1.2% | 1.1% | 0.7% | 93.3% | 95.7% | 100.1%
Poznan_Street | 0.0% | -0.1% | 1.2% | 0.2% | 0.2% | 0.1% | 92.2% | 97.0% | 96.9%
Undo_Dancer | 0.0% | -0.2% | -0.1% | 0.0% | 0.0% | 0.0% | 94.3% | 101.9% | 103.0%
Shark | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.3% | 101.7% | 102.9%
1024x768 | 0.0% | 2.8% | 3.6% | 1.2% | 1.1% | 0.9% | 91.4% | 100.5% | 100.1%
1920x1088 | 0.0% | 0.2% | 1.0% | 0.3% | 0.3% | 0.2% | 95.7% | 98.4% | 100.0%
average | 0.0% | 1.2% | 2.0% | 0.6% | 0.6% | 0.4% | 94.1% | 99.2% | 100.0%
Notes: The positive value in this table presents coding loss.
The row of 1024x768 denotes the average coding loss over Balloons, Kendo, and Newspaper_CC. (The resolutions of the three sequences are 1024x768.)
The row of 1920x1088 denotes the average coding loss over GT_Fly, Poznan_Hall2, Poznan_Street, Undo_Dancer, and Shark. (The resolutions of the five sequences are 1920x1088.)

## Slide 16: Conclusion
Coding results when IC is OFF
  The coding loss is 0.6%, 0.6%, and 0.4% for video PSNR vs. video bitrate, video PSNR vs. total bitrate, and synth PSNR vs. total bitrate, respectively, at HTM-9.0r1 configuration without IC.
The intrinsic complexity of IC is presented to be anchor complexity to evaluate IC tools.

## Slide 17: Appendix – MC+IC
Motion Compensation
Illumination Compensation
Reference Picture
IC Flag
Motion Vector
Current Position
IC Flag
Reference Block
Prediction Block
MC + IC
Left and above pixels of current block
Left and above pixels of reference block