## Slide 1: Centralized Color-Depth Packing (CCDP) SEI Message Syntax (A Revision of JCT-S0031)
Presenter : Jar-Ferr Yang
Center for Tomorrow Ubiquitous Cloud and Hypermedia Services
Institute of Computer and Communication Engineering
Department of Electrical Engineering
National Cheng Kung University

## Slide 2: Outlooks of CCDPs (color 3/4, 7/8, 15/16)
1H
3/4H
1/8H
1/8H
1H
Color-3/4 CCDP
1H
15/16H
1/32H
1/32H
Color-15/16 CCDP
1H
7/8H
1/16H
1/16H
Color-7/8 CCDP
Original Color
Original Depth

## Slide 3: CCDP SEI Syntax
centralized_color_depth_packing( payloadSize ) { | Descriptor
centralized_color_depth_packing_id | ue(v)
centralized_color_depth_packing_cancel_flag | u(1)
if( ! centralized_color_depth_packing_flag ) { | 
centralized_color_depth_packing_type | u(7)
content_interpretation_type | u(6)
depth_spatial_flipping_flag | u(1)
depth_subpixel_arrangement_type | u(4)
color_samping_type | u(8)
depth_samping_type | u(8)
centralized_color_depth_packing_reserved_byte | u(8)
centralized_color_depth_packing_persistence_flag | u(1)
} | 
} | 

## Slide 4: centralized_color_depth_packing_type
Value | Interpretation
4 | View and depth plane of the decoded frames contains a color-3/4 CCDP arrangement of corresponding planes of 2D and depth frames as illustrated in Figure x1.
6 | View and depth plane of the decoded frames contains a color-5/6 CCDP arrangement of corresponding planes of 2D and depth frames as illustrated in Figure x2.
8 | View and depth plane of the decoded frames contains a color-7/8 CCDP arrangement of corresponding planes of 2D and depth frames as illustrated in Figure x3.
12 | View and depth plane of the decoded frames contains a color-11/12 CCDP arrangement of corresponding planes of 2D and depth frames as illustrated in Figure x4.
16 | View and depth plane of the decoded frames contains a color-15/16 CCDP arrangement of corresponding planes of 2D and depth frames as illustrated in Figure x5.

## Slide 5: content_interpretation_type
Value | Interpretation
0 | Unspecified relationship between the frame packed constituent frames
1 | Indicates that the packed frame is arrange by depth1, view, depth 2 order form top to bottom
2 | Indicates that the packed frame is arrange by depth1, view, depth 2 order form left to right
NOTE X: When value is 1 or 2 in content_interpretation_type, and
centralized_color_depth_packing_type should be equal to 4, 6, 8, 12, or 16
1H
1W
content_interpretation_type =1
content_interpretation_type =2

## Slide 6: spatial_flipping_flag
spatial_flipping_flag equal to 1, when frame_packing_arrangement_type is equal to 4, 6, 8, 12 or 16 and content_interpretation_type equal 1 or 2, indicates that depth frame is spatially flipped relative to its intended orientation for display or other such purposes.
When frame_packing_arrangement_type is equal to 4, 6, 8, 12, or 16, content_interpretation_type equal 1 or 2, and spatial_flipping_flag is equal to 1, the type of spatial flipping that is indicated is as follows:
  If content_interpretation_type is equal to 1, the indicated spatial flipping is vertical flipping.
  If content_interpretation_type is equal to 2, the indicated spatial flipping is horizontal flipping.
  Otherwise (spatial_flipping_flag is equal to 0), the indicated spatial flipping is not necessary.
1H
1H
spatial_flipping_flag=1
spatial_flipping_flag=0

## Slide 7: depth_subpixel_rotation_flag
depth_subpixel_rotation_flag equal to 1 indicates that embedding the 3 depth values into R, G and B channels to the colored-depth frame is used the rotation method. depth_subpixel_arrangement_flag equal to 0 indicates that embedding the 3 depth values into R, G, and B channels in the colored-depth frame is used the sequence order.
(Y11, Y21, Y31) (Y22, Y32, Y12) (Y33, Y13, Y23), …
….
depth_subpixel_rotation_flag=1
(Y11, Y21, Y31) (Y12, Y22, Y32) (Y13, Y23, Y33), …
….
depth_subpixel_rotation_flag=0
Y11 Y12 Y13…
Y21 Y22 Y23…
Y31 Y32 Y33…
…
Colored depth in subpixels (R, G, B)
Depth map
Colored depth in subpixels (R, G, B)

## Slide 8: view_samping_type
view_samping_type indicates that the method of the view sampling is used by an encoder to indicate to a decoder as specified in Table D‑13.
Value | Interpretation
0 | Encoder using bilinear method to downscale the vertical resolution of color frame
Values of view_samping_type that do not appear in Table D.13 are reserved for future specification by ITU-T |ISO/IEC and shall not be present in bitstreams conforming to this version of this Specification. Decoders shall ignoreframe packing arrangement SEI messages that contain reserved values of content_interpretation_type.

## Slide 9: depth_samping_type
depth_samping_type indicates that the method of the depth sampling is used by an encoder to indicate to a decoder as specified in Table D‑14.
Value | Interpretation
0 | Encoder using bilinear method to downscale the vertical or horizontal resolution of depth frame
Values of depth_samping_type that do not appear in Table D.14 are reserved for future specification by ITU-T |ISO/IEC and shall not be present in bitstreams conforming to this version of this Specification. Decoders shall ignoreframe packing arrangement SEI messages that contain reserved values of content_interpretation_type.
NOTE 7–When content_interpretation_type equal to 63, the value 0 for depth_samping_type, the depth frame is down scale the vertical resolution by using bilinear method. When content_interpretation_type equal to 64, the value 0 for depth_samping_type, the depth frame is down scale the horizontal resolution by using bilinear method.

## Slide 10: Conclusions
In this contribution, the objective measurements of the proposed color-3/4, color-7/8 and color-15/16 CCDP methods are comparing to that of the frame compatible color-and-depth (SbS) packing format.
To include the color-3/4, color-5/6, color-7/8, color-11/12, and color-15/16 CCDP formats and their settings in the AVC and HEVC standards, we propose a new CCDP SEI message syntax.
The proposed CCDP format attains better image quality in the receiving side compared to the frame compatible color-and-depth (SbS) packing format for both 2D-TV and 3D-TV displays.

## Slide 11
Thanks for your kind attention
Q&A