## Slide 1: CE3:Switching Interpolation Filter (SIF) scheme
T. Yoshino, S. Naito (KDDI)

## Slide 2: Summary
Overview
  Switching Interpolation Filter (SIF) (JCTVC-D285)
  Report the result under CE3 coding conditions
Result
  -0.06% and -0.09% BD-rate improvement for LD/LC and LD/HE
  0.04% and 0.15% BD-rate degradation for RA/LC and RA/HE
Cross-check
  NTT (E205)

## Slide 3: Switching Interpolation Filter(SIF)
Feature
  8-tap separable interpolation filter
  Pre-define 8 sets of interpolation filter coefficient
  Low-complexity filter decision algorithm (encoder)
Change(s) from D285
  Pre-defined filter coefficient
    [-2, 5, -11, 40, 40, -11, 5, -2]/64
    [-1, 3, -10, 40, 40, -10, 3, -1]/64
    [0, 2, -9, 39, 39, -9, 2, 0]/64
    [2, -2, -5, 37, 37, -5, -2, 2]/64
    [1, -2, -3, 36, 36, -3, -2, 1]/64
    [1, -5, 3, 33, 33, 3, -5, 1]/64
    [-1, -4, 5, 32, 32, 5, -4, -1]/64
    [-1, -4, 7, 30, 30, 7, -4, -1]/64

## Slide 4: Experimental results (LD-LC)
 | Y BD-rate[%] | BD-PSNR[dB]
Class B | -0.14 | 0.00
Class C | -0.06 | 0.00
Class D | 0.15 | -0.01
Class E | -0.23 | 0.01
All | -0.06 | 0.00
Enc Time [%] | 103 | 
Dec Time [%] |  | 
BD-rate[%] and BD-PSNR[dB] vs HM2.0

## Slide 5: Experimental results (LD-HE)
 | Y BD-rate[%] | BD-PSNR[dB]
Class B | -0.24 | 0.00
Class C | -0.08 | 0.00
Class D | 0.08 | 0.00
Class E | -0.08 | 0.00
All | -0.09 | 0.00
Enc Time [%] | 102 | 
Dec Time [%] |  | 
BD-rate[%] and BD-PSNR[dB] vs HM2.0

## Slide 6: Experimental results (RA-LC)
 | Y BD-rate[%] | BD-PSNR[dB]
Class A | 0.09 | 0.00
Class B | -0.02 | 0.00
Class C | 0.01 | 0.00
Class D | 0.10 | 0.00
All | 0.04 | 0.00
Enc Time [%] | 101 | 
Dec Time [%] |  | 
BD-rate[%] and BD-PSNR[dB] vs HM2.0

## Slide 7: Experimental results (RA-HE)
 | Y BD-rate[%] | BD-PSNR[dB]
Class A | 0.06 | 0.00
Class B | 0.04 | 0.00
Class C | 0.10 | 0.00
Class D | 0.44 | -0.02
All | 0.15 | -0.01
Enc Time [%] | 99 | 
Dec Time [%] |  | 
BD-rate[%] and BD-PSNR[dB] vs HM2.0

## Slide 8: Conclusion
Summary
  Report coding performance of SIF (JCTVC-D285)
  -0.06% and -0.09% BD-rate improvement for LD/LC and LD/HE
  0.04% and 0.15% BD-rate degradation for RA/LC and RA/HE
  Degrade the SIF coding performance due to 6-bit filter coefficient
    JCTVC-D285 reported -0.4% BD-rate improvement for LD/LC
Conclusion
  Have potential of providing additional performance for other coding tools while maintaining encoding time
  Further discussed in interpolation filter CE