## Slide 1: JCTVC-H0398 CE10 Subtest 4: Transform dependent Deblocking Filter Parameter Adjustment
Geert Van der Auwera, Rajan Joshi, Xianglin Wang, Marta Karczewicz
Qualcomm Inc.

## Slide 2: Summary
Signaling of deblocking filter adjustment parameters in APS and/or slice header to adjust tC depending on:
  Transform size to control deblocking strength, because of significantly different psycho-visual importance of blocking artifact sizes (4x4 up to 32x32)
    Allows subjective tuning depending on content, frame resolution, screen size, viewing distance, etc.
  Intra or inter mode of block
deblocking_filter_control_present_flag in SPS:
  Control presence of deblocking adjustment parameters (disable/enable)
    Avoids signaling overhead in case no parameters need signaling
BD-rates and execution times similar to anchor:
  AI-HE: -0.1%, AI-LC: -0.1%, RA-HE: 0.0%, RA-LC: 0.0%, LB-HE: 0.0%, LB-LC: 0.0%, LP-HE: 0.1%, LP-LC: 0.0%

## Slide 3: Adjusting tC
HM5.1:
  Signaling of tc_offset_div2
  TcOffset = IF “Bs = 2” THEN “2 + 2×tc_offset_div2” ELSE “2×tc_offset_div2”
  Q = Clip3(0, MAX_QP+2, QP + TcOffset )
  tC[Q]
Proposed adjustment parameters:
  Intra/inter dependent (+3 parameters):
    tc_offset_intra_div2 (replaces tc_offset_div2; value used for 4×4 block)
    tc_offset_intra_delta (used to compute offset for other block sizes)
    tc_offset_inter_div2
    tc_offset_inter_delta
  Simplified: intra/inter independent (one additional parameter)
    tc_offset_div2 (already in HM5.1; value used for 4×4 block)
    tc_offset_delta

## Slide 4: Adjusting tC
Proposed computation of TcOffset:
  transform_type = NxN (= 4x4 or 8x8 or 16x16 or 32x32)
    INTRA_TC_OFFSET = (2×tc_offset_intra_div2) + tc_offset_NxN_intra_delta
    INTER_TC_OFFSET = (2×tc_offset_inter_div2) + tc_offset_NxN_inter_delta
  Tc_offset_NxN_intra_delta = tc_offset_intra_delta × factor_NxN
  Tc_offset_NxN_inter_delta = tc_offset_inter_delta × factor_NxN
  Constant values used in the computation (not signaled):
    Factor_4x4 = 0
    Factor_8x8 = 1
    Factor_16x16 = 2
    Factor_32x32 = 3
  IF “Intra Mode” THEN “TcOffset = 2 + INTRA_TC_OFFSET”; ELSE “TcOffset = INTER_TC_OFFSET”
  Q = Clip3(0, MAX_QP + 2, QP + TcOffset )
  tC[Q]
Remark: simplification when intra/inter mode independent

## Slide 5: Proposed Syntax
SPS: deblocking_filter_control_present_flag
seq_parameter_set_rbsp( ) { | Descriptor
profile_idc | u(8)
..... | 
chroma_pred_from_luma_enabled_flag | u(1)
deblocking_filter_control_present_flag | u(1)
if (deblocking_filter_control_present_flag) { | 
deblocking_filter_in_aps_enabled_flag | u(1)
Note that if deblocking_filter_control_present_flag=0, then deblocking_filter_in_aps_enabled_flag=0 and aps_deblocking_filter_flag=0 and disable_deblocking_filter_flag=0 and beta_offset_div2=0 and tc_offset_div2=0 are inferred. | 
} | 
loop_filter_across_slice_flag | u(1)
sample_adaptive_offset_enabled_flag | u(1)
adaptive_loop_filter_enabled_flag | u(1)
pcm_loop_filter_disable_flag | u(1)
..... | 
} | 

## Slide 6: Proposed Syntax
APS:
aps_rbsp( ) { | Descriptor
aps_id | ue(v)
aps_sample_adaptive_offset_flag | u(1)
aps_adaptive_loop_filter_flag | u(1)
aps_deblocking_filter_flag | u(1)
if( aps_sample_adapt ive_offset_flag ¦¦ aps_adaptive_loop_filter_flag ) { | 
aps_cabac_use_flag | u(1)
if( aps_cabac_use_flag ) { | 
aps_cabac_init_idc | ue(v)
aps_cabac_init_qp_minus26 | se(v)
} | 
} | 
if( aps_sample_adaptive_offset_flag ) { | 
..... | 
} | 
if( aps_adaptive_loop_filter_flag ) { | 
..... | 
} | 
if (aps_deblocking_filter_flag){ | 
disable_deblocking_filter_flag | u(1)
if (!disable_deblocking_filter_flag) { | 
beta_ offset_div2 | se(v)
tc_offset_div2 | se(v)
tc_offset_intra_div2 | se(v)
tc_offset_intra_delta | se(v)
tc_offset_inter_div2 | se(v)
tc_offset_inter_delta | se(v)
} | 
} | 
.... | 

## Slide 7: Proposed Syntax
Slice header:
slice_header( ) { | Descriptor
entropy_slice_flag | u(1)
if( !entropy_slice_flag ) { | 
slice_type | ue(v)
pic_parameter_set_id | ue(v)
if( sample_adaptive_offset_enabled_flag ¦¦ adaptive_loop_filter_enabled_flag ) | 
aps_id | ue(v)
if( IdrPicFlag ) { | 
idr_pic_id | ue(v)
.... | u(v)
if( !entropy_slice_flag ) { | 
slice_qp_delta | se(v)
if (deblocking_filter_control_present_flag) { | 
inherit_dbl_params_from_APS_flag | u(1)
if (!inherit_dbl_params_from_APS_flag){ | 
disable_deblocking_filter_flag | u(1)
if (!disable_deblocking_filter_flag) { | 
beta_offset_div2 | se(v)
tc_offset_div2 | se(v)
tc_offset_intra_div2 | se(v)
tc_offset_intra_delta | se(v)
if ( slice_type != I) { | 
tc_offset_inter_div2 | se(v)
tc_offset_inter_delta | se(v)
} | 
} | 
} | 
} | 
..... | 

## Slide 8: Objective Results
Compared with CE10.4 anchor (QP=22, 27, 32, 37)
 | All Intra HE |  |  | All Intra LC |  |  | All Intra HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% |  |  | 
Class B | 0.0% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1% |  |  | 
Class C | -0.1% | -0.3% | -0.3% | -0.1% | -0.2% | -0.1% |  |  | 
Class D | -0.1% | -0.3% | -0.3% | 0.0% | -0.1% | 0.0% |  |  | 
Class E | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.2% |  |  | 
Overall | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | 0.0% |  |  | 
 | -0.1% | -0.2% | -0.2% | -0.1% | -0.1% | 0.0% |  |  | 
Class F | -0.1% | -0.4% | -0.4% | 0.0% | -0.3% | -0.4% |  |  | 
Enc Time[%] | 104% |  |  | 102% |  |  |  |  | 
Dec Time[%] | 100% |  |  | 99% |  |  |  |  | 
 | Random Access HE |  |  | Random Access LC |  |  | Random Access HE-10 |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A (8bit) | 0.0% | -0.1% | -0.2% | 0.0% | -0.1% | -0.2% | 0.1% | 0.1% | 0.1%
Class B | 0.0% | -0.2% | -0.2% | -0.1% | -0.2% | -0.2% | 0.0% | -0.2% | -0.1%
Class C | 0.0% | -0.3% | -0.2% | 0.0% | -0.4% | -0.3% |  |  | 
Class D | 0.1% | -0.1% | -0.3% | 0.1% | -0.2% | -0.3% |  |  | 
Class E |  |  |  |  |  |  |  |  | 
Overall | 0.0% | -0.2% | -0.2% | 0.0% | -0.2% | -0.3% | 0.1% | 0.0% | 0.0%
 | 0.0% | -0.2% | -0.2% | 0.0% | -0.3% | -0.3% | 0.1% | 0.0% | 0.0%
Class F | -0.1% | -0.5% | -0.4% | 0.0% | -0.5% | -0.5% |  |  | 
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 99% |  |  | 99% |  |  | 100% |  | 
 | Low delay B HE |  |  | Low delay B LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.1% | 0.2% | 0.0% | -0.3% | 0.0%
Class C | 0.1% | -0.3% | 0.0% | 0.1% | 0.0% | 0.1%
Class D | 0.1% | 0.1% | 0.3% | 0.1% | 0.6% | -0.1%
Class E | 0.2% | 0.6% | 0.0% | 0.3% | -0.2% | 0.1%
Overall | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0%
 | 0.1% | 0.1% | 0.2% | 0.1% | 0.0% | 0.0%
Class F | 0.0% | -0.2% | -0.5% | 0.0% | -1.4% | -0.6%
Enc Time[%] | 103% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 101% |  | 
 | Low delay P HE |  |  | Low delay P LC |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | 0.0% | 0.0% | 0.0% | -0.1% | 0.2% | -0.4%
Class C | 0.1% | 0.0% | -0.2% | 0.0% | 0.0% | 0.0%
Class D | 0.1% | 0.4% | -0.4% | 0.1% | 0.1% | 0.6%
Class E | 0.2% | 0.2% | 0.2% | 0.1% | -0.2% | -0.4%
Overall | 0.1% | 0.1% | -0.1% | 0.0% | 0.0% | -0.1%
Class F | 0.1% | 0.0% | -0.1% | 0.1% | -0.9% | -0.3%
Enc Time[%] | 100% |  |  | 102% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 

## Slide 9: Subjective Results
Class B “Kimono” sequence (Low delay P LC, QP=37)
HM5.0
Proposal
Frame 240

## Slide 10: Subjective Results
Class C “BQMall” sequence (Low delay P LC, QP=37)
HM5.0
Proposal
Frame 600

## Slide 11: Subjective Results
Class E “Vidyo3” sequence (Low delay P LC, QP=37)
HM5.0
Proposal
Frame 600

## Slide 12: Subjective Adjustment Example
“CrowdRun” coded using “All Intra LC” and QP = 37
  Delta frame demonstrates that block sizes can be targeted differently
    Deblocking of smooth areas with large transforms is nearly unaltered, while the deblocking strength for the smaller transform sizes can be controlled to improve subjective quality
HM5.0
Delta frame for tC offsets 4x4 = -12, 8x8 = -8, 16x16 = -4, 32x32 = 0

## Slide 13: Conclusion
Adjust tC deblocking parameter depending on:
  Transform size (+1 parameter):
    Signaling of tc_offset_delta (tc_offset_div2 already in HM5.1)
  Intra or inter mode (+3 parameters):
    Separate tc_offset_div2 and tc_offset_delta for intra and inter
Add deblocking_filter_control_present_flag in SPS
Purpose is to tune subjective quality of wide range of blocking artifact sizes (4x4 to 32x32)
BD-rates close to HM5.0 anchor
Proposed to adopt in HM6
Thanks to Toshiba for cross checking!