## Slide 1: On stereo 3D coding using frame packing arrangement SEI
JCTVC-I0058
O. Nakagami and T. Suzuki
Sony Corporation
Joint Collaborative Team on Video Coding (JCT-VC) of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11
9th Meeting: Geneva, CH, 27 April – 7 May 2012

## Slide 2: Summary
Background
  It is suggested that 2D compatibility is desirable for frame compatible coding.
  For side-by-side (top-bottom) case, cropping realizes the compatibility (m21278).
  The only issue is conformance for 3D playback because the remaining part after the cropping is necessary.
Proposal
  Modify or create new frame packing arrangement SEI (FPA_SEI) for HEVC

## Slide 3: Method2-1 Cropping & Side-by-side (Top-bottom)
Cropping is used for 2D compatibility (No modify)
  pic_cropping_flag
  pic_crop_(l/r/t/b)_offset
→ Usual decoders output only the base-view.
Modify the definition and decoding process for FPA_SEI
  Add a 1-bit flag in VUI to indicate the existence of Frame packing arrangement SEI
  When the added flag in VUI is true and the FPA_SEI is pursed, the decoders should infer pic_cropping_flag is equal to be 0. and ignore picture cropping information.
→ Decoders, which support FPA_SEI, can decode with keeping regulations.
SPS
FPA_
SEI
VUI
change pic_cropping_flag info.
frame_packing_arrangement_indication_presence_flag
vui_parameters_present_flag
Left
Right
side-by-side
cropping

## Slide 5
related to frame sequential topic

## Slide 6
The followings are initial version.

## Slide 7: Introduction
Stereo 3D using Frame packing arrangement SEI (FPA_SEI)
Left
Right
Right
Left
side-by-side
frame sequential
Left
Right
top-bottom
when decoders do not support
the FPA_SEI
when decoders support
the FPA_SEI
Works fine.
Always output the packed stereo.
+
Other packing type
To support SEI is not mandatory.
In this contribution, methods to output only the base-view are proposed. Thus, 2D/3D compatibility for some packing types are achieved.
Notes: Frame compatible stereo 3D is beneficial because all ver. 1 decoders can decode the stereo 3D bitstream.
However, one issue is compatibility among decoders.
As shown in the figure, decoders, which support FPA_SEI, output correctly for both 2D and 3D display.
But, decoders, which do not decode FPA_SEI, output the decoded pictures directly as the packed frame
Because decoding SEI message is not mandatory process.
When the output display is a 2D display, such result is not desirable.
Thus, the focus of the proposal is on decoders which do not support FPA_SEI.
It’s conceivable that the most part of decoders belong to this category because the most output devices still support 2D only.
In order to resolve these situations, this contribution proposes three alternative methods to realize the 2D compatibility among decoders for frame packing stereo 3D.

## Slide 8: 3 method to realize 2D/3D compatibility
 |  | 2D/3D compatibility |  |  | Burden for decoders which are not interested in FPA_SEI
 |  | Frame sequential | side-by-side, top-bottom | Other packing method | 
HM6.0/CD |  | No | No | No | -
1 | Change decoder process to support FPA_SEI | Yes | Yes | Yes | Yes
2 | Modify decoding process for FPA_SEI | Yes by using max_temporal_id_minus1 | Yes by using cropping or syntax | No | No
3 | Assign a new nal_unit_type for Frame packing Stereo 3D | Yes | No | No | No
Notes: Here is a quick summary of the current status and the three proposed methods.
Currently, compatibility mentioned in the previous slide is not realized. In proposal, compatibility for some type of frame compatible type is realized.
For example, method2 realizes compatibility for frame sequential, side-by-side and top-bottom.
The figure also mention about burden for decoders which are not interested in FPA_SEI .The burden means modification of decoding process from the current draft. As shown, only Method1 effect the decoding process for usual decoders.
Method1 is to expect all decoder to parse the FPA_SEI. Although this method is burden for decoders which are not interested frame compatible coding, it is mentioned for a comparison.
The 2nd one is combination with encoder-side trick. For frame sequential and side-by-side coding, the definition of FPA_SEI is proposed to change.
The 3rd method propose to define new nal_unit_type for stereo 3D.
I’ll present the detail in the following slides.

## Slide 9: Method1: Change decoder process to support FPA_SEI
Add a 1-bit flag in VUI to indicate the existence of Frame packing arrangement SEI in the AU.
And give a strict definition for the flag.
frame_packing_arrangement_indication_presence_flag equal to 1 specifies that a Frame packing arrangement SEI message shall be present in the bitstream (or in the same AU). When the flag equal to 1, decoders should support the SEI message.
SPS
FPA_
SEI
VUI
frame_packing_arrangement_indication_presence_flag
vui_parameters_present_flag
Notes: Method1 is a proposal to expect all decoders to support FPA_SEI
A 1-bit flag, named as frame_packing_arrangement_indication_presence_flag, is added in VUI.
The flag represents that FPA_SEI message exists in the bistream.
The flag enables decoders to parse the SEI easier.
Then, when the flag is true, method1 requires all decoders to decode FPA_SEI as a mandatory process.
Although it is a burden for decoders which are not interested in frame packing 3D, method1 enables all decoders to know the view information

## Slide 10: Method2-1 Cropping & Side-by-side (Top-bottom)
Add a 1-bit flag in VUI to indicate the existence of Frame packing arrangement SEI in the AU.(Same as method1)
Set pic_cropping_flag equal to 1 and the offset to crop the base-view area in SPS
  → Decoders, which don’t support FPA_SEI, output only base-view.
When frame_packing_arrangement_indication_presence_flag is true and the FPA_SEI is pursed, the decoders shall infer pic_cropping_flag is equal to be 0 and ignore picture cropping information.
  → Decoders, which support FPA_SEI, can decode with keeping regulations.
SPS
FPA_
SEI
VUI
change pic_cropping_flag info.
frame_packing_arrangement_indication_presence_flag
vui_parameters_present_flag
Left
Right
side-by-side
cropping
Notes: Method2 uses SPS/NAL syntax for the 2D compatibility
Method2_1 is applied to side-by-side or top-bottom case.
Side-by-side and top-bottom are relatively simple spatial packing type. So, for the 2D compatibility, cropping syntax is used.
According to the cropping syntax, decoders, which do not support FPA_SEI, outputs only the base-view
The issue in AVC is decoders which support FPA_SEI. Because the cropping is mandatory process, to output the right view is non-conforming process.
So, I’d like to propose to change the definition of FPA_SEI in HEVC.
Firstly, 1-bit flag, named as frame_packing_arrangement_indication_presence_flag, is added in VUI.
When frame_packing_arrangement_indication_presence_flag is true and packing type is side-by-side or top-bottom,
the decoders ignore the cropping information.
So, decoders, which support FPA_SEI, can decode both views with conforming process.

## Slide 11: Method2-2 temporal_id & Frame sequential
Add a 1-bit flag in VUI to indicate the existence of Frame packing arrangement SEI in the AU.(Same as method1)
Set max_temporal_id_minus1 equal to the maximum temporal_id minus 1 of Left view in SPS
  → Decoders, which don’t support FPA_SEI, decode only base-view.
When frame_packing_arrangement_indication_presence_flag is true and the FPA_SEI is read, max_temporal_id_minus1 in SPS is overwritten by a value in SEI as the maximum temporal_id minus 1 of Right view.
SPS
FPA_
SEI
VUI
overwrite max_temporal_id_minus1
frame_packing_arrangement_indication_presence_flag
vui_parameters_present_flag
L
R
L
R
temporal_id
POC
Max_t_L
L
Max_t_R
drop
Notes: Method2-2 is for the compatibility of frame sequential coding.
Temporal scalability (temporal_id) is used to realize the compatibility.
As shown in this figure, lower temporal_id is assigned to the base view(left) picture, and higher temporal_id is assigned to the additional view picture.
Then, set max_temporal_id_minus1 in SPS equal to the maximum temporal_id minus 1 of the left view
Decoders, which do not support FPA_SEI, decode only left view due to the max_temporal_id_minux1 syntax.
To overcome the conformance issue, the following definition is proposed.
When a flag in VUI is true and frame sequential coding is used,
max_temporal_id_minus1 in SPS is updated by a value in the SEI as the maximum temporal_id minus 1 of the additional view.
So, Decoders, which support FPA_SEI, decode both views with keeping regulations.

## Slide 12: Method3 Assign new nal_unit_type for Frame packing Stereo 3D
Assign nal_unit_type=X for the base-view, where X belongs to any nal_unit_type defined in the current draft.
Assign nal_unit_type=Y for the additional-view, where Y is a new nal_unit_type for 3D.
→ Decoders, which don’t support nal_unit_type=Y, drop Right-view.
→ Decoders, which support nal_unit_type=Y, can decode both view.
In Method3, Frame sequential is only supported.
Right
nal_unit_type=Y
Left
nal_unit_type=X
Right
nal_unit_type=Y
Left
nal_unit_type=X
POC
Decoders, which don’t support nal_unit_type=Y, drop Right-view.
Notes: Method3 is to define a new nal_unit_type for 3D.
Assign nal_unit_type=X for the base view picture, where X is any nal_unit_type for coded slice defined in the current draft.
Assign nal_unit_type=Y for the additional view picture, where Y is a new nal_unit_type for 3D.
→ Decoders, which do not support nal_unit_type=Y, decode only base view by dropping additional view.
→ Decoders, which support nal_unit_type=Y, decode both views.
It is noted that frame sequential is only supported in method3.
For spatial packing 3D (side-by-side and top-bottom), decoders, which do not support the proposed nal_unit_type, do not decode at all.
Thus, the 2D compatibility is not realized for spatial packing 3D.

## Slide 13: 3 method to realize 2D/3D compatibility
 |  | 2D/3D compatibility |  |  | Burden for decoders which are not interested in FPA_SEI
 |  | Frame sequential | side-by-side, top-bottom | Other packing method | 
HM6.0/CD |  | No | No | No | -
1 | Change decoder process to support FPA_SEI | Yes | Yes | Yes | Yes
2 | Modify decoding process for FPA_SEI | Yes by using max_temporal_id_minus1 | Yes by using cropping or syntax | No | No
3 | Assign a new nal_unit_type for Frame packing Stereo 3D | Yes | No | No | No
Notes: Here is a comparison again.
As mentioned, Method2 requires encoder trick to generate bitstream.
And decoders, which support FPA_SEI, need to modify decode process.
However, the most decoders, which do not support FPA_SAI, can output 2D view without any changing decoding process.
Also, by the proposed definition of frame_packing_arrangement_indication_presence_flag, the decoder conformance is satisfied.
Furthermore, method2 supports both spatial and temporal packing.

## Slide 14: Conclusion
Method2 realizes 2D/3D compatibility with the minimum change of decode procedure of the three.
Proposed modification for method2
  Add a 1-bit flag in VUI which represents the existence of the Frame packing arrangement SEI in the same AU.
  To realize compatibility,
    For side-by-side (top-bottom)coding, cropping info. in SPS are discarded by the SEI.
    For frame sequential coding, max_temporal_id in SPS are overwritten by a parameter in the SEI.