## Slide 1: JCTVC-J0268 AHG6: on SAO signalling
Jun Xu, Ali Tabatabai
SONY

## Slide 2: Introduction
SAO in HM7.0
  If no merges, SAO offset information is signaled.
  SAO offsets
    SAO type(i.e. on/off, BO, EO classes)
    BO bandposition
    BO/EO offsets
Problems
  Unbalanced structure
  Interleaving of context coded bins and by-pass bins
SAO type
BO band positions
Offset absolute values
Offset absolute values
Offset signs
BO
EO

## Slide 3: Proposal
Proposal on SAO signaling
  New SAO type (sao_type_idx, Truncated unary with 2 contexts: one for each bin)
    On/Off flag
    BO
    EO
  Subtype (FLC with by-pass)
    BO: band position
    EO: classes (sao_eo_class)
  Reordering of syntax
    Resolve interleaving of context coded bins and by-pass coded bins
  Reduced context coded bins
    SAO type
      HM7.0 : 6 bins in context
      Proposal: 2 bins in cotnext
  Increased throughput
    More bins are encoded in by-pass

## Slide 4: Interleaving
Resolving interleaving of context coded bins and by-pass bins by re-ordering
Same re-ordering can apply to HM7.0 only
  JCTVC-J0046 and JCTVC-J0054 proposed the same idea.
 | Index | HM7.0 |  | Proposal |  | 
On/Off | 0 | 0 | - | 0 | - | -
EO1 | 1 | 10 | EO offsets | 11 | EO offsets | 00
EO2 | 2 | 110 |  | 11 |  | 01
EO3 | 3 | 1110 |  | 11 |  | 10
EO4 | 4 | 111110 |  | 11 |  | 11
BO | 5 | 1111110XXXXX | BO offsets + BO sign | 10 | 4 BO offsets | BO sign +xxxxx
Blue: SAO on/off flag w/ context
Purple: EO/BO flag w/ context
Red: by-pass

## Slide 5: Diagram
SAO type
EO class
BO band position
Offset absolute values
Offset absolute values
Offset signs
Context coded
By-pass coded
BO
EO

## Slide 6: Results
Thanks to Samsung for cross-checking
 | All Intra Main |  |  | All Intra HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.2% | -0.3% | 0.0% | -0.1% | -0.2%
Class B | 0.0% | -0.3% | -0.4% | 0.0% | -0.1% | -0.2%
Class C | 0.0% | -0.2% | -0.3% | 0.0% | -0.2% | -0.2%
Class D | 0.0% | -0.2% | -0.2% | 0.0% | 0.0% | -0.1%
Class E | 0.0% | -0.4% | -0.5% | 0.0% | -0.1% | -0.2%
Overall | 0.0% | -0.3% | -0.3% | 0.0% | -0.1% | -0.2%
 | 0.0% | -0.2% | -0.3% | 0.0% | -0.1% | -0.2%
Class F | 0.0% | -0.2% | -0.2% | 0.0% | -0.3% | -0.3%
 | Random Access Main |  |  | Random Access HE10 |  | 
 | Y | U | V | Y | U | V
Class A | 0.0% | -0.5% | -0.5% | 0.0% | -0.3% | -0.3%
Class B | 0.0% | -0.3% | -0.4% | 0.0% | -0.3% | -0.3%
Class C | 0.0% | -0.3% | -0.3% | 0.0% | -0.2% | -0.2%
Class D | 0.0% | -0.2% | -0.3% | 0.0% | 0.1% | -0.2%
Class E |  |  |  |  |  | 
Overall | 0.0% | -0.3% | -0.4% | 0.0% | -0.2% | -0.3%
 | 0.0% | -0.3% | -0.4% | 0.0% | -0.2% | -0.3%
Class F | 0.0% | -0.1% | -0.2% | -0.1% | -0.3% | -0.3%
 | Low delay B Main |  |  | Low delay B HE10 |  | 
 | Y | U | V | Y | U | V
Class A |  |  |  |  |  | 
Class B | -0.1% | -0.4% | -0.6% | 0.0% | 0.0% | -0.1%
Class C | -0.1% | -0.3% | -0.5% | 0.0% | -0.3% | -0.2%
Class D | 0.0% | 0.0% | 0.4% | -0.1% | -0.2% | -0.2%
Class E | -0.1% | -0.2% | -0.6% | 0.0% | -0.4% | 0.3%
Overall | -0.1% | -0.2% | -0.3% | 0.0% | -0.2% | -0.1%
 | 0.0% | -0.3% | -0.3% | 0.0% | -0.2% | -0.1%
Class F | -0.2% | -0.5% | -0.1% | 0.1% | -0.4% | -0.1%

## Slide 7: AHG5 results
AHG5 decoder bin count patch
  Count number of context coded bins and by-pass coded bins
 | SAO |  |  |  | 
 | Bins relative to total bins |  |  |  | Delta rates %
 | Reference |  | Tested |  | 
 | ctx | bp | ctx | bp | 
AI Main | 1.06% | 0.14% | 1.03% | 0.33% | 6.28%
RA Main | 3.57% | 0.18% | 3.64% | 0.51% | 4.71%
LB Main | 3.76% | 0.36% | 3.74% | 0.85% | 4.91%
LP Main | 4.10% | 0.23% | 4.04% | 0.87% | 2.54%
Average | 3.12% | 0.23% | 3.11% | 0.64% | 4.61%
 | SAO |  |  |  | 
 | Bins relative to total bins |  |  |  | Delta rates %
 | Reference |  | Tested |  | 
 | ctx | bp | ctx | bp | 
AI HE10 | 0.80% | 0.05% | 0.79% | 0.11% | 6.06%
RA HE10 | 2.50% | 0.06% | 2.50% | 0.16% | 3.53%
LB HE10 | 2.96% | 0.08% | 2.97% | 0.22% | 3.52%
LP HE10 | 3.03% | 0.06% | 3.04% | 0.24% | 3.14%
Average | 2.32% | 0.06% | 2.32% | 0.18% | 4.06%

## Slide 8: Conclusion
Proposed changes to SAO signalling
  Balanced structure
  Grouped by-pass bins for high throughput
  No loss or minor BD gains
Recommend for adopation.