## Slide 1
Presenter : Jar-Ferr Yang
JCTVC-AE0022: Centralized Texture-Depth Packing SEI Message for HEVC and AVC
(Revisions of JCTVC-AD0022)
Institute of Computer and Communication Engineering,
Department of Electrical Engineering,
National Cheng Kung University, Tainan, Taiwan

## Slide 2: Contents
SEI Message Syntax in JCTVC-AE0022
(color_packing_space changed to chroma_usage)
CTDP Formats: Interpretation of ctdp_packing_type
Colored Depth Depacking: Interpretation of chroma_usage
Depth Parameters Related Syntax
Experimental Results
Conclusions
Adoption Status in Taiwan

## Slide 3: Centralized Texture-Depth Packing SEI Message Syntax

## Slide 4: CTDP SEI Syntax in JCTVC-AD0022 (Old)
centralized_texture_depth_packing( payloadSize ) { | Descriptor
centralized_texture_depth_packing_cancel_flag | u(1)
if( ! centralized_texture_depth_packing_cancel_flag ) { | 
ctdp_packing_type | u(3)
color_packing_space | u(1)
baseline_dist_flag | u(1)
focal_length_flag | u(1)
z_near_flag | u(1)
z_far_flag | u(1)
d_min_flag | u(1)
d_max_flag | u(1)
depth_representation_type | ue(v)
if( baseline_dist_flag ) | 
view_syn_rep_info_element( BdistanceSign, BdistanceExp, BdistanceMantissa, BdistanceManLen ) | 
if( focal_length_flag ) | 
view_syn_rep_info_element( FlengthSign, FlengthExp, FlengthMantissa, FlengthManLen ) | 
if( z_near_flag ) | 
view_syn_rep_info_element( ZNearSign, ZNearExp, ZNearMantissa, ZNearManLen ) | 
if( z_far_flag ) | 
view_syn_rep_info_element ( ZFarSign, ZFarExp, ZFarMantissa, ZFarManLen ) | 
if( d_min_flag ) | 
view_syn_rep_info_element ( DMinSign, DMinExp, DMinMantissa, DMinManLen ) | 
if( d_max_flag ) | 
view_syn_rep_info_element ( DMaxSign, DMaxExp, DMaxMantissa, DMaxManLen ) | 
if( depth_representation_type = = 3 ) { | 
depth_nonlinear_representation_num_minus1 | ue(v)
for( i = 1; i <= depth_nonlinear_representation_num_minus1 + 1; i++ ) | 
depth_nonlinear_representation_model[ i ] | 
centralized_texture_depth_packing_persistence_flag | u(1)
} | 
} | 
} | 

## Slide 5: CTDP SEI Syntax in JCTVC-AE0022 (New)
centralized_texture_depth_packing( payloadSize ) { | Descriptor
centralized_texture_depth_packing_cancel_flag | u(1)
if( ! centralized_texture_depth_packing_cancel_flag ) { | 
ctdp_packing_type | u(3)
chroma_subsampling_type | u(1)
chroma_usage | u(2)
baseline_dist_flag | u(1)
focal_length_flag | u(1)
z_near_flag | u(1)
z_far_flag | u(1)
d_min_flag | u(1)
d_max_flag | u(1)
depth_representation_type | ue(v)
if( baseline_dist_flag ) | 
view_syn_rep_info_element( BdistanceSign, BdistanceExp, BdistanceMantissa, BdistanceManLen ) | 
if( focal_length_flag ) | 
view_syn_rep_info_element( FlengthSign, FlengthExp, FlengthMantissa, FlengthManLen ) | 
if( z_near_flag ) | 
view_syn_rep_info_element( ZNearSign, ZNearExp, ZNearMantissa, ZNearManLen ) | 
if( z_far_flag ) | 
view_syn_rep_info_element ( ZFarSign, ZFarExp, ZFarMantissa, ZFarManLen ) | 
if( d_min_flag ) | 
view_syn_rep_info_element ( DMinSign, DMinExp, DMinMantissa, DMinManLen ) | 
if( d_max_flag ) | 
view_syn_rep_info_element ( DMaxSign, DMaxExp, DMaxMantissa, DMaxManLen ) | 
if( depth_representation_type = = 3 ) { | 
depth_nonlinear_representation_num_minus1 | ue(v)
for( i = 1; i <= depth_nonlinear_representation_num_minus1 + 1; i++ ) | 
depth_nonlinear_representation_model[ i ] | 
centralized_texture_depth_packing_persistence_flag | u(1)
} | 
} | 
} | 

## Slide 6: Centralized Texture-Depth Packing (CTDP) Formats : ctdp_packing_type

## Slide 7: ctdp_packing_type
CTDP-TB
CTDP-LR
Value | Interpretation
0 | Indicates the frame of the CTDP-TB type with an arrangement of top color depth (CDT), texture (TS), and bottom color depth (CDB) regions from top to bottom, as illustrated in Figure D‑X1.
1 | Indicates the frame of the CTDP-LR type with an arrangement of left color depth (CDL), texture (TS), and right color depth (CDR) regions from left to right, as illustrated in Figure D‑X2.
(Depth:1/9, Texure:8/9)
(Depth:1/12, Texture:11/12)

## Slide 8: CTDP-TB Packing Procedure (Modified)
Color Depth Packing: Assigned RGB Subpixels
Spatial Subsample in
Vertical Direction
Vertical Subsample or
Original Texture Frame
Vertical
Combination
H
H
Vertical Splitting
& Flipping
HT
HT
HHD
HHD
6HHD
w
w
w
HHD
HHD
w
w
w
w
3HHD
3HHD
w
w

## Slide 9: CTDP-TB Format for HD Video (1920x1080)
CTDP-TB Format :
60
960
1920
60
1080

## Slide 10
CTDP Depacking for ctdp_packing_type =0
Arrangement of the CTDP-TB frame and its depacking steps (ctdp_packing type = 0):

## Slide 11: CTDP-LR Packing Procedure (Modified)
Color Depth Packing: Assigned RGB Subpixels
Spatial Subsample in
Horizontal Direction
Horizontal Subsample or
Original Texture Frame
Combination
W
W
Horizontal Splitting
& Flipping
WHD
WT
WHD
WT
H
H
6WHD
H
WHD
WHD
H
H
H
H
3WHD
3WHD
H
H

## Slide 12: CTDP-LR Format for HD Video (1920x1080)
CTDP-LR Format :
1760
80
80
1080
1920

## Slide 13
CTDP Depacking for ctdp_packing_type =1
Arrangement of the CTDP-LR frame and its depacking steps (ctdp_packing type = 1):

## Slide 14: Colored Depth Pixels Packing and Depacking by Assigned RGB Subpixels: chroma_usage

## Slide 15: Colored Depth Pixels versus Depth Pixels
Basic Concept:
1 color depth pixel in RGB subpixels can carry at most 3 depth pixels
CTDP-TB type RGB subpixels arranged in 3 consecutive vertical depth pixels
CTDP-TB type RGB subpixels arranged in 3 consecutive horizontal depth pixels
Based on Coding System:
4 color depth pixels in RGB subpixels can carry at most 12 depth pixels

## Slide 16
chroma_subsampling_type
Value | Interpretation
0 | Indicates the video coder using direct subsampling to achieve 4 and 2 chroma components downsizing for YCbCr 4:2:0 and YCbCr 4:2:2 chroma formats, respectively.
1 | Indicates the video coder using average subsampling to achieve 4 and 2 chroma components downsizing for YCbCr 4:2:0 and YCbCr 4:2:2 chroma formats, respectively.

## Slide 17
chroma_usage
Value | Interpretation
0 | Indicates the 4 colored depth pixels using 4 luminance components only to carry 4 depth pixels, which could be adopted by the video coders with YCbCr 4:2:0 and YCbCr 4:2:2 chroma formats
1 | Indicates the 4 colored depth pixels using 4 luminance components and 2 chroma components to carry 6 depth pixels, which could be adopted by the video coders with YCbCr 4:2:0 chroma format.
2 | Indicates the 4 colored depth pixels using 4 luminance components and 4 chroma components to carry 8 depth pixels, which could be adopted by the video coders with YCbCr 4:2:2 chroma format.
3 | Indicates 4 colored depth pixels using 4 luminance components and 8 chroma components to carry 12 depth pixels, which could be adopted by the video coders with YCbCr 4:4:4 chroma format.

## Slide 18
For each 4 color pixels, in chroma_usage = 0, only 4 luminance components values {Yi,j, Yi,j+1, Yi+1,j, Yi+1,j+1} are used to carry 4 depth pixels {D3i,j, D3i+1,j+1, D3i+4, j, D3i+5, j+1} for ctdp_packing type =0 or {Di,3j, Di+1,3j+1, Di,3j+4, Di+1, 3j+5} for ctdp_packing type =1.
chroma_usage = 0
Ci,j+1
Ci+1,j+1
Ci,j
Ci+1,j
4 colored
depth pixels
D3i,j
D3i+1,j
D3i+2,j
D3i+3,j
D3i+4,j
D3i+5,j
D3i,j+1
D3i+1,j+1
D3i+2,j+1
D3i+3,j+1
D3i+4,j+1
D3i+5,j+1
ctdp_packing_type = 0
ctdp_packing_type = 1
i = 0, 2, 4…, (HHD-2) and j = 0, 2, 4…, (W-2)
Ri,j+1
Gi,j+1
Gi,j
Bi.j
Bi.j+1
Ri+1,j+1
Ri+1,j
Gi+1,j
Gi+1,j+1
Bi+1,j+1
Bi+1,j
Ri,j
Di,3j
Di,3j+2
Di,3j+4
Di,3j+1
Di.3j+3
Ri,j
Gi,j
Bi.j
Ri,j+1
Gi,j+1
Bi.j+1
Ri+1,j
Gi+1,j
Bi+1,j
Ri+1,j+1
Gi+1,j+1
Bi+1,j+1
Di.3j+5
Di+1,3j
Di+1,3j+2
Di+1,3j+4
Di+1,3j+1
Di+1,3j+3
Di+1,3j+5
i = 0, 2, 4…, (H-2) and j = 0, 2, 4…, (WHD-2)

## Slide 19
chroma_usage = 0
(ctdp_packing_type = 0)
D3i,j
D3i+1,j
D3i+2,j
D3i+3,j
D3i+4,j
D3i+5,j
D3i,j+1
D3i+1,j+1
D3i+2,j+1
D3i+3,j+1
D3i+4,j+1
D3i+5,j+1
i = 0, 2, 4…, (HHD-2) and j = 0, 2, 4…, (W-2)
Ri,j+1
Gi,j+1
Gi,j
Bi.j
Bi.j+1
Ri+1,j+1
Ri+1,j
Gi+1,j
Gi+1,j+1
Bi+1,j+1
Bi+1,j
Ri,j
Depacking Process:
D3i,j = Ri,j, (D-X5)
D3i+4,j = Gi+1,j, (D-X6)
D3i+1,j+1 = Gi,j+1, (D-X7)
D3i+5,j+1 = Bi+1,j+1. (D-X8)
Packing Process (assign RGB Subpixels):
Ri,j = Gi,j = Bi,j = D3i,j, (D-X9)
Ri+1,j= Gi+1,j = Bi+1,j = D3i+4,j, (D-X10)
Ri.j+1 = Gi,j+1 = Bi,j+1 = D3i+1,j+1, (D-X11)
Ri+1,j+1= Gi+1,j+1= Bi+1,j+1=D3i+5,j+1. (D-X12)

## Slide 20
chroma_usage = 0
(ctdp_packing_type = 1)
Depacking Process:
Di,3j = Ri,j, (D-X13)
Di,3j+4 = Gi,j+1, (D-X14)
Di+1,3j+1 = Gi+1,j, (D-X15)
Di+1,3j+5 = Bi+1,j+1. (D-X16)
Packing Process (assign RGB Subpixels):
Ri,j = Gi,j = Bi,j = Di,3j, (D-X17)
Ri.j+1 = Gi,j+1 = Bi,j+1 = Di,3j+4, (D-X18)
Ri+1,j = Gi+1,j = Bi+1,j = Di+1,3j+1, (D-X19)
Ri+1,j+1= Gi+1,j+1 = Bi+1,j+1 = Di+1,3j+5. (D-X20)
Di,3j
Di,3j+2
Di,3j+4
Di,3j+1
Di.3j+3
Ri,j
Gi,j
Bi.j
Ri,j+1
Gi,j+1
Bi.j+1
Ri+1,j
Gi+1,j
Bi+1,j
Ri+1,j+1
Gi+1,j+1
Bi+1,j+1
Di.3j+5
Di+1,3j
Di+1,3j+2
Di+1,3j+4
Di+1,3j+1
Di+1,3j+3
Di+1,3j+5
i = 0, 2, 4…, (H-2) and j = 0, 2, 4…, (WHD-2)

## Slide 21
For each 4 color pixels, in chroma_usage = 0, 4 luminance and 2 chroma components {Yi,j, Yi,j+1, Yi+1,j, Yi+1,j+1, Cbi,j, Ci,j} are used to carry 6 depth pixels {D3i,j, D3i+1,j+1, D3i+4, j, D3i+5, j+1, D3i+2, j, D3i+3, j+1} for ctdp_packing type =0 or {Di,3j, Di+1,3j+1, Di,3 j+4, Di+1, 3j+5, Di,3 j+2, Di+1, 3j+3} for ctdp_packing type =1.
chroma_usage = 1
Ci,j+1
Ci+1,j+1
Ci,j
Ci+1,j
4 color
pixels
ctdp_packing_type = 0
ctdp_packing_type = 1
D3i,j
D3i+1,j
D3i+2,j
D3i+3,j
D3i+4,j
D3i+5,j
D3i,j+1
D3i+1,j+1
D3i+2,j+1
D3i+3,j+1
D3i+4,j+1
D3i+5,j+1
i = 0, 2, 4…, (HHD-2) and j = 0, 2, 4…, (W-2)
Ri,j+1
Gi,j+1
Gi,j
Bi.j
Bi.j+1
Ri+1,j+1
Ri+1,j
Gi+1,j
Gi+1,j+1
Bi+1,j+1
Bi+1,j
Ri,j
Di,3j
Di,3j+2
Di,3j+4
Di,3j+1
Di.3j+3
Ri,j
Gi,j
Bi.j
Ri,j+1
Gi,j+1
Bi.j+1
Ri+1,j
Gi+1,j
Bi+1,j
Ri+1,j+1
Gi+1,j+1
Bi+1,j+1
Di.3j+5
Di+1,3j
Di+1,3j+2
Di+1,3j+4
Di+1,3j+1
Di+1,3j+3
Di+1,3j+5
i = 0, 2, 4…, (H-2) and j = 0, 2, 4…, (WHD-2)

## Slide 22
chroma_usage = 1
(ctdp_packing_type = 0)
D3i,j
D3i+1,j
D3i+2,j
D3i+3,j
D3i+4,j
D3i+5,j
D3i,j+1
D3i+1,j+1
D3i+2,j+1
D3i+3,j+1
D3i+4,j+1
D3i+5,j+1
i = 0, 2, 4…, (HHD-2) and j = 0, 2, 4…, (W-2)
Ri,j+1
Gi,j+1
Gi,j
Bi.j
Bi.j+1
Ri+1,j+1
Ri+1,j
Gi+1,j
Gi+1,j+1
Bi+1,j+1
Bi+1,j
Ri,j
Depacking Process:
D3i,j = Ri,j, (D-X24)
D3i+2,j = Bi,j, (D-X25)
D3i+4,j = Gi+1,j, (D-X26)
D3i+1,j+1 = Gi,j+1, (D-X27)
D3i+3,j+1 = Gi,j, (D-X28)
D3i+5,j+1 = Bi+1,j+1. (D-X29)
Packing Process (assign RGB Subpixels):
Ri,j = D3i,j, (D-X21)
Gi,j = D3i+3,j+1, (D-X22)
Bi,j = D3i+2,j, (D-X23)
Ri+1,j= Gi+1,j = Bi+1,j = D3i+4,j, (D-X10)
Ri.j+1 = Gi,j+1 = Bi,j+1 = D3i+1,j+1, (D-X11)
Ri+1,j+1= Gi+1,j+1= Bi+1,j+1=D3i+5,j+1. (D-X12)

## Slide 23
chroma_usage = 1
(ctdp_packing_type = 1)
Depacking Process:
Di,3j = Ri,j, (D-X33)
Di,3j+2 = Bi,j, (D-X34)
Di,3j+4 = Gi,j+1, (D-X35)
Di+1,3j+1 = Gi+1,j, (D-X36)
Di+1,3j+3 = Gi,j. (D-X37)
Di+1,3j+5 = Bi+1,j+1. (D-X38)
Packing Process (assign RGB Subpixels):
Ri,j = Di,3j, (D-X30)
Gi,j = Di+1,3j+3, (D-X31)
Bi,j = Di,3j+2, (D-X32)
Ri,j = Gi,j = Bi,j = Di,3j, (D-X17)
Ri.j+1 = Gi,j+1 = Bi,j+1 = Di,3j+4, (D-X18)
Ri+1,j = Gi+1,j = Bi+1,j = Di+1,3j+1, (D-X19)
Ri+1,j+1= Gi+1,j+1 = Bi+1,j+1 = Di+1,3j+5. (D-X20)
Di,3j
Di,3j+2
Di,3j+4
Di,3j+1
Di.3j+3
Ri,j
Gi,j
Bi.j
Ri,j+1
Gi,j+1
Bi.j+1
Ri+1,j
Gi+1,j
Bi+1,j
Ri+1,j+1
Gi+1,j+1
Bi+1,j+1
Di.3j+5
Di+1,3j
Di+1,3j+2
Di+1,3j+4
Di+1,3j+1
Di+1,3j+3
Di+1,3j+5
i = 0, 2, 4…, (H-2) and j = 0, 2, 4…, (WHD-2)

## Slide 24
chroma_usage = 1 (Coding in YCbCr 4:2:0)
For each 4 color pixels, the video coding system is operated with chroma YCbCr 4:2:0 format, the chroma components Cb and Cr will perform subsampling in the encoder and upsampling in decoder. By using chroma_subsampling_type, we can directly adjusted chroma components back to the original ones if the depacking can be performed in YCbCr color space.
Color
Space
Transform
Ri,j
Gi,j
Bi,j
Video
Coding
System
Yi,j
Cbi,j
Cri,j
Adjustment
Chroma
Component
{Yi,j, Cbi,j, Cri,j}
{Yi,j+1,128,128}
{Yi+1,j,128,128}
{Yi+1,j+1,128,128}
{Yi,j, Cbi,j, Cri,j}
{Yi,j+1,128,128}
{Yi+1,j,128,128}
{Yi+1,j+1,128,128}
{Yi,j, Cb’i,j, Cr’i,j}
{Yi,j+1, Cb’i,j, Cr’i,j
{Yi+1,j, Cb’i,j, Cr’i,j}
{Yi+1,j+1, Cb’i,j, Cr’i,j}
Yi,j
Cbi,j
Cri,j
Yi,j
Cb’i,j
Cr’i,j
For direct subsampling:
Cbi,j = Cb’i,j,
Cri,j = Cr’i,j
For average subsampling：
Cbi,j = 4Cb’i,j- 384,
Cri,j = 4Cr’i,j - 384
Direct subsampling:
Cb’i,j = Cbi,j,
Cr’i,j = Cri,j
Average subsampling：
Cb’i,j = Cbi,j/4 - 96
Cr’i,j = Cri,j/4 - 96
Inverse
Color
Space
Transform
Ri,j
Gi,j
Bi,j
Color Depth Depacker

## Slide 25
{Yi,j, Cbi,j, Cri,j}
{Yi,j+1, 128, 128}
{Yi+1,j, 128, 128}
{Yi+1,j+1, 128, 128}
{Yi,j, Cbi,j, Cri,j}
{Yi,j+1, 128, 128}
{Yi+1,j, 128, 128}
{Yi+1,j+1, 128, 128}
{Yi,j, Cb’i,j, Cr’i,j}
{Yi,j+1, Cb’i,j, Cr’i,j
{Yi+1,j, Cb’i,j, Cr’i,j}
{Yi+1,j+1, Cb’i,j, Cr’i,j}
For direct subsampling:
Cbi,j = Cb’i,j,
Cri,j = Cr’i,j
For average subsampling：
Cbi,j = 4Cb’i,j- 384,
Cri,j = 4Cr’i,j - 384
Direct subsampling:
Cb’i,j = Cbi,j,
Cr’i,j = Cri,j
Average subsampling：
Cb’i,j = Cb’i,j/4 - 96
Cr’i,j = Cr’i,j/4 - 96
Video
Coding
System
Adjustment
Chroma
Component
Color
Space
Transform
Ri,j
Gi,j
Bi,j
Inverse
Color
Space
Transform
R’i,j
G’i,j
B’i,j
Video Encoder and Decoder
Color
Space
Transform
{Yi,j, Cb’i,j, Cr’i,j}
{Yi,j+1, Cb’i,j, Cr’i,j
{Yi+1,j, Cb’i,j, Cr’i,j}
{Yi+1,j+1, Cb’i,j, Cr’i,j}
Inverse
Color
Space
Transform
Ri,j
Gi,j
Bi,j
Color Depth Depacker
chroma_usage = 1 (Coding in YCbCr 4:2:0)
For each 4 color pixels, the video coding system operated with chroma YCbCr 4:2:0 format, the chroma components Cb and Cr will perform subsampling in the encoder and upsampling in the decoder. By using chroma_subsampling_type, we can directly adjusted chroma components back to the original ones if the depacking can be only performed in RGB color space.

## Slide 26
For each 4 color pixels, in chroma_usage = 0, 4 luminance and 4 chroma components {Yi,j, Yi,j+1, Yi+1,j, Yi+1,j+1, Cbi,j, Ci,j, Cbi+1,j, Ci+1,j} are used to carry 8 depth pixels as {D3i,j, D3i+1,j+1, D3i+4, j, D3i+5, j+1, D3i+2, j, D3i+3, j+1, D3i, j+1, D3i+3, j} for ctdp_packing type =0 or {Di,3j, Di+1,3j+1, Di,3 j+4, Di+1, 3j+5, Di,3 j+2, Di+1, 3j+3} for ctdp_packing type =1.
chroma_usage = 2

## Slide 27
chroma_usage = 2
(ctdp_packing_type = 0)
D3i,j
D3i+1,j
D3i+2,j
D3i+3,j
D3i+4,j
D3i+5,j
D3i,j+1
D3i+1,j+1
D3i+2,j+1
D3i+3,j+1
D3i+4,j+1
D3i+5,j+1
Ri,j+1
Gi,j+1
Gi,j
Bi.j
Bi.j+1
Ri+1,j+1
Ri+1,j
Gi+1,j
Gi+1,j+1
Bi+1,j+1
Bi+1,j
Ri,j
Depacking Process:
Ri,j = D3i,j, (D-X39)
Gi,j = D3i+1,j+1, (D-X40)
Bi,j = D3i+2,j, (D-X41)
Ri+1,j = D3i+3,j+1, (D-X42)
Gi+1,j = D3i+4,j, (D-X43)
Bi+1,j = D3i+5,j, (D-X44)
Ri.j+1 = Gi,j+1 = Bi,j+1 = D3i,j+1, (D-X45)
Ri+1,j+1=Gi+1,j+1=Bi+1,j+1=D3i+5, j+1. (D-X46)
Packing Process (assign RGB Subpixels):
D3i,j = Ri,j, (D-X47)
D3i+2,j = Bi,j, (D-X48)
D3i+4,j = Gi+1,j, (D-X49)
D3i+5,j = Bi+1,j. (D-X50)
D3i,j+1 = Ri,j+1, (D-X51)
D3i+1,j+1 = Gi,j, (D-X52)
D3i+3,j+1 = Ri+1,j, (D-X53)
D3i+5,j+1 = Bi+1,j+1. (D-X54)

## Slide 28
chroma_usage = 2
(ctdp_packing_type = 1)
Di,3j
Di,3j+2
Di,3j+4
Di,3j+1
Di.3j+3
Ri,j
Gi,j
Bi.j
Ri,j+1
Gi,j+1
Bi.j+1
Ri+1,j
Gi+1,j
Bi+1,j
Ri+1,j+1
Gi+1,j+1
Bi+1,j+1
Di.3j+5
Di+1,3j
Di+1,3j+2
Di+1,3j+4
Di+1,3j+1
Di+1,3j+3
Di+1,3j+5
Depacking Process:
Ri,j = Di,3j, (D-X55)
Gi,j = Di,3j+1, (D-X56)
Bi,j = Di,3j+3, (D-X57)
Ri+1,j = Di+1,3j, (D-X58)
Gi+1,j = Di+1,3j+1, (D-X59)
Bi+1,j = Di+1,3j+3, (D-X60)
Ri.j+1 = Gi,j+1 = Bi,j+1 = Di,3j+5, (D-X61)
Ri+1,j+1 Gi+1,j+1=Bi+1,j+1=Di+1,3j+5. (D-X62)
Packing Process (assign RGB Subpixels):
Di,3j = Ri,j, (D-X63)
Di,3j+1 = Gi,j, (D-X64)
Di,3j+3 = Bi,j, (D-X65)
Di,3j+5 = Bi,j+1. (D-X66)
Di+1,3j = Ri+1,j, (D-X67)
Di+1,3j+1 =Gi+1,j, (D-X68)
Di+1,3j+3 = Bi+1,j, (D-X69)
Di+1,3j+5 = Bi+1,j+1. (D-X70)

## Slide 29
chroma_usage = 2 (Coding in YCbCr 4:2:2)
For each 4 color pixels, the video coding system operated with chroma YCbCr 4:2:2 format, the chroma components Cb and Cr will perform subsampling in the encoder and upsampling in decoder, we can directly adjusted chroma component back to the original ones if the depacking can be performed in YCbCr color space.
Color
Space
Transform
Ri,j
Gi,j
Bi,j
Video
Coding
System
Yi,j
Cbi,j
Cri,j
Adjustment
Chroma
Component
Yi,j
Cbi,j
Cri,j
Yi,j
Cb’i,j
Cr’i,j
For direct subsampling:
Cbi,j = Cb’i,j, Cb’i+1,j = Cbi+1,j,
Cri,j = Cr’i,j, Cr’i+1,j = Cri+1,j
For average subsampling：
Cbi,j = 2Cb’i,j-128,
Cbi+1,j = 2Cb’i+1,j-128,
Cri,j = 2Cr’i,j -128,
Cri+1,j = 2Cr’i+1,j-128
Inverse
Color
Space
Transform
Ri,j
Gi,j
Bi,j
Colored
Depth
Depacker
{Yi,j, Cbi,j, Cri,j}
{Yi,j+1, 128, 128}
{Yi+1,j, Cbi+1,j, Cri+1,j}
{Yi+1,j+1, 128, 128}
{Yi,j, Cb’i,j, Cr’i,j}
{Yi,j+1, Cb’i,j, Cr’i,j
{Yi+1,j, Cb’i+1,j, Cr’i+1,j}
{Yi+1,j+1, Cb’i+1,j, Cr’i+1,j}
Direct subsampling :
Cb’i,j = Cbi,j, Cb’i+1,j = Cbi+1,j,
Cr’i,j = Cri,j, Cr’i+1,j = Cri+1,j
Average subsampling：
Cb’i,j = Cb’i,j/2-64,
Cb’i+1,j = Cb’i+1,j/2-64
Cr’i,j = Cr’i,j/2-64,
Cr’i+1,j = Cr’i+1,j/2-64
{Yi,j, Cbi,j, Cri,j}
{Yi,j+1, 128, 128}
{Yi+1,j, Cbi+1,j, Cri+1,j}
{Yi+1,j+1, 128, 128}

## Slide 30
{Yi,j, Cbi,j, Cri,j}
{Yi,j+1, 128, 128}
{Yi+1,j, Cbi+1,j, Cri+1,j}
{Yi+1,j+1, 128, 128}
{Yi,j, Cb’i,j, Cr’i,j}
{Yi,j+1, Cb’i,j, Cr’i,j
{Yi+1,j, Cb’i+1,j, Cr’i+1,j}
{Yi+1,j+1, Cb’i+1,j, Cr’i+1,j}
Direct subsampling:
Cb’i,j = Cbi,j, Cb’i+1,j = Cbi+1,j,
Cr’i,j = Cri,j, Cr’i+1,j = Cri+1,j
Average subsampling：
Cb’i,j = Cb’i,j/2-64,
Cb’i+1,j = Cb’i+1,j/2-64
Cr’i,j = Cr’i,j/2-64,
Cr’i+1,j = Cr’i+1,j/2-64
Video
Coding
System
Adjustment
Chroma
Component
Color
Space
Transform
Ri,j
Gi,j
Bi,j
Inverse
Color
Space
Transform
R’i,j
G’i,j
B’i,j
Video Encoder and Decoder
Color
Space
Transform
Inverse
Color
Space
Transform
Ri,j
Gi,j
Bi,j
Color Depth Depacker
chroma_usage = 2 (Coding in YCbCr 4:2:2)
For each 4 color pixels, the video coding system operated with chroma YCbCr 4:2:0 format, the chroma components Cb and Cr will perform subsampling in the encoder and upsampling in the decoder, we can directly adjusted chroma component back to the original ones if the depacking can be only performed in RGB color space.
{Yi,j, Cbi,j, Cri,j}
{Yi,j+1, 128, 128}
{Yi+1,j, Cbi+1,j, Cri+1,j}
{Yi+1,j+1, 128, 128}
{Yi,j, Cb’i,j, Cr’i,j}
{Yi,j+1, Cb’i,j, Cr’i,j
{Yi+1,j, Cb’i+1,j, Cr’i+1,j}
{Yi+1,j+1, Cb’i+1,j, Cr’i+1,j}
For direct subsampling:
Cbi,j = Cb’i,j, Cb’i+1,j = Cbi+1,j,
Cri,j = Cr’i,j, Cr’i+1,j = Cri+1,j
For average subsampling：
Cbi,j = 2Cb’i,j-128,
Cbi+1,j = 2Cb’i+1,j-128,
Cri,j = 2Cr’i,j -128,
Cri+1,j = 2Cr’i+1,j-128

## Slide 31: Relationship of Depacked Depth and Texture
ctdp_packing_type=0 and H is divisible to 36

## Slide 32: Relationship of Depacked Depth and Texture
ctdp_packing_type=1 and W is divisible to 48

## Slide 33: Depth Parameters Related Syntax (Transferred from 3D-HEVC)

## Slide 34: Depth Parameter Related Flags
baseline_dist_flag equal to 0 specifies that the syntax elements specifying the baseline distance are not present in the syntax structure. baseline_dist_flag equal to 1 specifies that the syntax elements specifying the baseline distance value are present in the syntax structure.
focal_length_flag equal to 0 specifies that the syntax elements specifying the focal length are not present in the syntax structure. focal_length_pixel_flag equal to 1 specifies that the syntax elements specifying the focal length value are present in the syntax structure.
z_near_flag equal to 0 specifies that the syntax elements specifying the nearest depth value are not present in the syntax structure. z_near_flag equal to 1 specifies that the syntax elements specifying the nearest depth value are present in the syntax structure.
z_far_flag equal to 0 specifies that the syntax elements specifying the farthest depth value are not present in the syntax structure. z_far_flag equal to 1 specifies that the syntax elements specifying the farthest depth value are present in the syntax structure.
d_min_flag equal to 0 specifies that the syntax elements specifying the minimum disparity value are not present in the syntax structure. d_min_flag equal to 1 specifies that the syntax elements specifying the minimum disparity value are present in the syntax structure.
d_max_flag equal to 0 specifies that the syntax elements specifying the maximum disparity value are not present in the syntax structure. d_max_flag equal to 1 specifies that the syntax elements specifying the maximum disparity value are present in the syntax structure.

## Slide 35: depth_representation_type
Value | Interpretation
0 | Each recovered depth value represents an inverse of Z value that is uniformly quantized into the range of 0 to maxVal, inclusive. When z_far_flag is equal to 1, the recovered depth value equal to 0 represents the inverse of ZFar (specified below). When z_near_flag is equal to 1, the recovered depth value equal to maxVal represents the inverse of ZNear (specified below).
1 | Each recovered depth value represents disparity that is uniformly quantized into the range of 0 to maxVal, inclusive. When d_min_flag is equal to 1, the recovered depth value equal to 0 represents DMin (specified below). When d_max_flag is equal to 1, the recovered depth value equal to maxVal represents DMax (specified below).
2 | Each recovered depth value represents a Z value uniformly quantized into the range of 0 to maxVal, inclusive. When z_far_flag is equal to 1, the recovered depth value equal to 0 corresponds to ZFar (specified below). When z_near_flag is equal to 1, the recovered depth value equal to maxVal represents ZNear (specified below).
3 | Each recovered depth value represents a nonlinearly mapped disparity, normalized in range from 0 to maxVal, as specified by depth_nonlinear_representation_num_minus1 and depth_nonlinear_representation_model[i]. When d_min_flag is equal to 1, the recovered depth value equal to 0 represents DMin (specified below). When d_max_flag is equal to 1, the recovered depth value equal to maxVal represents DMax (specified below).
Other values | Reserved for future use
The variable maxVal is set equal to ( 1 << ( 8 + bit_depth_luma_minus8 ) ) − 1, where bit_depth_luma_minus8 is the value included in or inferred for the active SPS of the layer with nuh_layer_id equal to targetLayerId.
depth_representation_type specifies the representation definition of the recovered depth values as specified in Table D-X3. In Table D-X3, disparity specifies the horizontal displacement between two texture views and Z value specifies the distance from a camera.

## Slide 36: depth_representation_type versus disparity
depth_representation_type = 1:
di,j = ( / maxVal) * DMax – DMin) + DMin. (D-X71)
depth_representation_type = 0:
Zi,j = 1 / {( / maxVal) * (1/ZNear – 1/ZFar) – 1/ZFar}. (D-X72)
depth_representation_type = 2:
Zi,j = ( / maxVal) * (ZFar – ZNear)– ZNear. (D-X73)
depth_representation_type = 0 or 2:
di,j = Bdistance * Flength ÷ Zi,j (D-X74)

## Slide 37: Representation information element syntax
The syntax structure specifies the value of an element in the view synthesis representation information SEI message.
The syntax structure sets the values of the OutSign, OutExp, OutMantissa and OutManLen variables that represent a floating-point value. When the syntax structure is included in another syntax structure, the variable names OutSign, OutExp, OutMantissa and OutManLen are to be interpreted as being replaced by the variable names used when the syntax structure is included.
da_sign_flag equal to 0 indicates that the sign of the floating-point value is positive. da_sign_flag equal to 1 indicates that the sign is negative. The variable OutSign is set equal to da_sign_flag.
da_exponent specifies the exponent of the floating-point value. The value of da_exponent shall be in the range of 0 to 27 − 2, inclusive. The value 27 − 1 is reserved for future use by ITU-T | ISO/IEC. Decoders shall treat the value 27 − 1 as indicating an unspecified value. The variable OutExp is set equal to da_exponent.
da_mantissa_len_minus1 plus 1 specifies the number of bits in the da_mantissa syntax element. The value of da_mantissa_len_minus1 shall be in the range of 0 to 31, inclusive. The variable OutManLen is set equal to da_mantissa_len_minus1 + 1.
da_mantissa specifies the mantissa of the floating-point value. The variable OutMantissa is set equal to da_mantissa.
view_syn_rep_info_element( OutSign, OutExp, OutMantissa, OutManLen ) { | Descriptor
da_sign_flag | u(1)
da_exponent | u(7)
da_mantissa_len_minus1 | u(5)
da_mantissa | u(v)
} | 

## Slide 38: Depth parameter variables and syntax elements
x | s | e | n | v
Bdistance | BdistanceSign | BdistanceExp | BdistanceMantissa | BdistanceManLen
Flength | FlengthSign | FlengthExp | FlengthMantissa | FlengthManLen
ZNear | ZNearSign | ZNearExp | ZNearMantissa | ZNearManLen
ZFar | ZFarSign | ZFarExp | ZFarMantissa | ZFarManLen
DMax | DMaxSign | DMaxExp | DMaxMantissa | DMaxManLen
DMin | DMinSign | DMinExp | DMinMantissa | DMinManLen
The variables in the x column of table are derived from the respective variables in the s, e, n and v columns as follows:
– If the value of e is in the range of 0 to 127, exclusive, x is set equal to ( −1 )s* 2e - 31 * ( 1 + n ÷ 2v ).
– Otherwise (e is equal to 0), x is set equal to ( −1 )s * 2−( 30 + v ) * n.
The DMin and DMax values, when present, are specified in units of a luma sample width of the coded picture.
The units for the ZNear and ZFar, when present, are identical but unspecified.
When depth_representation_type is equal to 0 or 2, the disparity D can further be obtained from the value of Z, Bdistance, and Flength, where D = Bdistance × Flength ÷ Z

## Slide 39: Other Syntax Elements
depth_nonlinear_representation_num_minus1 plus 2 specifies the number of piecewise linear segments for mapping of depth values to a scale that is uniformly quantized in terms of disparity.
depth_nonlinear_representation_model[ i ] for i ranging from 0 to depth_nonlinear_representation_num_minus1 + 2, inclusive, specify the piecewise linear segments for mapping of the recovered depth values to a scale that is uniformly quantized in terms of disparity. The values of depth_nonlinear_representation_model[0] and depth_nonlinear_representation_model[ depth_nonlinear_representation_num_minus1 + 2 ] are both inferred to be equal to 0.
centralized_texture_depth_packing_persistence_flag specifies the persistence of the centralized texture-depth packing arrangement SEI message.
centralized_texture-depth_packing_persistence_flag equal to 0 specifies that the centralized texture-depth packing arrangement SEI message applies to the current decoded frame only.
centralized_texture-depth_packing_persistence_flag equal to 1 specifies that the centralized texture-depth packing arrangement SEI message persists in output order until any of the following conditions are true:
– A new CVS begins.
– The bitstream ends.
– A frame in an access unit containing a centralized texture-depth packing SEI message with the same

## Slide 40: Performance Evaluations
1. Uncompressed CTDP Performance (Compare to Ground True Values) 2. HEVC-Coded CTDP Performance (Compare to 3D-HEVC Results)

## Slide 41
Sequences | Clipped Resolution | Frames | 1 View | Synthesized View
Undo Dancer | 1920×1080 | 250 | 3 | 4
Shark | 1920×1080 | 300 | 5 | 7
Computer Generated Test Sequences

## Slide 42: Experimental Settings
Uncoded and Coded HD Computer Generated Videos:
ratios of depth region :
CTDP TB: Depth:1/9, Texture: 8/9
CTDP LR: Depth: 1/12, Texture: 11/12
HEVC-CTDP Coding Parameters:
encoding mode: All Intra, Low delay, Random access
QP: 27,32,37,42
ctdp_packing_type: CTDP-TB and CTDP-LR
image resizing: Lancos 4
depth resizing: bicubic

## Slide 43
CTDP depacked texture, depth, and synthesized view are compared to ground truth ones
Uncoded CTDP Performances
of YCbCr and RGB Color Packing Methods

## Slide 44
Performances of Uncoded CTDP Formats
CTDP-TB: ctdp_packing_type = 0
CTDP-LR: ctdp_packing_type = 1
Performances | Depacked Texture |  |  | Depacked Depth |  |  |  | Synthesized Virtual View Generated by VSRS |  |  | 
 | DPCM-based YUV | Adjust RGB | Assign RGB | DPCM-based YUV | Adjust RGB | Assign RGB (Y) | Assign RGB (Y+C) | DPCM-based YUV | Adjust RGB | Assign RGB (Y) | Assign RGB (Y+C)
PSNR | 46.149 | 47.092 |  | 44.102 | 44.625 | 41.200 | 44.163 | 38.888 | 38.028 | 37.500 | 37.973
SSIM | 0.9938 | 0.9938 |  | 0.9918 | 0.9943 | 0.9880 | 0.9910 | 0.9867 | 0.9754 | 0.9760 | 0.9770
Performances | Depacked Texture |  |  | Depacked Depth |  |  |  | Synthesized Virtual View Generated by VSRS |  |  | 
 | DPCM-based YUV | Adjust RGB | Assign RGB | DPCM-based YUV | Adjust RGB | Assign RGB (Y) | Assign RGB (Y+C) | DPCM-based YUV | Adjust RGB | Assign RGB (Y) | Assign RGB (Y+C)
PSNR | 49.214 | 49.244 |  | 39.888 | 40.432 | 37.102 | 40.039 | 38.288 | 37.493 | 36.200 | 37.419
SSIM | 0.9958 | 0.9955 |  | 0.9873 | 0.9905 | 0.9820 | 0.9860 | 0.9882 | 0.9768 | 0.9750 | 0.9770

## Slide 45
Depacked Depth from Uncoded CTDP-LR Format
Depacked Depth for Direct RGB Color Packing

## Slide 46
Depacked Depth of DPCM-based YUV (4:2:0)
Depacked Depth from Uncoded CTDP-LR Format

## Slide 47
Depacked Depth of Adjusted RGB Color Packing
Depacked Depth from Uncoded CTDP-LR Format

## Slide 48
Depacked Depth of Assigned RGB Color Packing (4:0:0)
Depacked Depth from Uncoded CTDP-LR Format

## Slide 49
Depacked Depth of Assigned RGB Color Packing (4:2:0)
Depacked Depth from Uncoded CTDP-LR Format

## Slide 50
HEVC-coded CTDP Performances
of YCbCr and RGB Color Packing Methods
CTDP-HEVC decoded and depacked texture, depth, and synthesized view are compared to 3D-HEVC decoded ones

## Slide 51
HEVC-coded CTDP-TB Performances
BDBR (%) Performance with respect to 3D-HEVC
BDPSNR (dB) Performance with respect to 3D-HEVC
Coding Modes | Depacked Texture |  |  |  | Depacked Depth |  |  |  | Virtual View by VSRS |  |  | 
 | DPCM YUV | Adjust RGB | Assign RGB(Y) | Assign RGB (Y+C) | DPCM YUV | Adjust RGB | Assign RGB(Y) | Assign RGB (Y+C) | DPCM YUV | Adjust RGB | Assign RGB (Y) | Assign RGB (Y+C)
ra | 13.6254 | 11.8079 | 10.2413 | 11.3696 | -30.6426 | -41.9352 | -37.3007 | -43.3599 | 25.7829 | 28.5642 | 27.3187 | 27.1948
ldp | 8.2266 | 7.0231 | 5.4145 | 6.5359 | -53.8872 | -61.2222 | -59.7979 | -62.1773 | 13.9024 | 16.9534 | 15.2695 | 15.8299
ai | 6.8931 | 5.4887 | 4.0781 | 5.1018 | -19.7578 | -30.0731 | -15.7421 | -31.9427 | 29.2954 | 34.6573 | 35.4913 | 32.4152
ave | 9.5817 | 8.1065 | 6.5779 | 7.6691 | -34.7625 | -44.4102 | -37.6136 | -45.8266 | 22.9936 | 26.7250 | 26.0265 | 25.1466
Coding Modes | Depacked Texture |  |  |  | Depacked Depth |  |  |  | Virtual View by VSRS |  |  | 
 | DPCM YUV | Adjust RGB | Assign RGB(Y) | Assign RGB (Y+C) | DPCM YUV | Adjust RGB | Assign RGB(Y) | Assign RGB (Y+C) | DPCM YUV | Adjust RGB | Assign RGB (Y) | Assign RGB (Y+C)
ra | -0.4247 | -0.3737 | -0.3233 | -0.3598 | 1.3941 | 2.1227 | 1.6104 | 2.2124 | -0.6789 | -0.7511 | -0.7264 | -0.7207
ldp | -0.2707 | -0.2344 | -0.1829 | -0.2190 | 3.6932 | 4.4448 | 4.5038 | 5.2205 | -0.4051 | -0.4940 | -0.4581 | -0.4683
ai | -0.2557 | -0.2088 | -0.1541 | -0.1940 | 0.8799 | 1.5138 | 0.3691 | 1.6067 | -0.8694 | -1.0012 | -1.0307 | -0.9518
ave | -0.3170 | -0.2723 | -0.2201 | -0.2576 | 1.9902 | 2.6937 | 2.1611 | 3.0132 | -0.6511 | -0.7487 | -0.7384 | -0.7136

## Slide 52
HEVC-coded CTDP-LR Performances
BDBR (%) Performance with respect to 3D-HEVC
BDPSNR (dB) Performance with respect to 3D-HEVC
Coding Modes | Depacked Texture |  |  |  | Depacked Depth |  |  |  | Virtual View by VSRS |  |  | 
 | DPCM YUV | Adjust RGB | Assign RGB(Y) | Assign RGB (Y+C) | DPCM YUV | Adjust RGB | Assign RGB(Y) | Assign RGB (Y+C) | DPCM YUV | Adjust RGB | Assign RGB (Y) | Assign RGB (Y+C)
ra | 11.7019 | 10.3264 | 9.8741 | 9.7372 | -1.0712 | 26.5047 | 14.3735 | 5.1253 | 67.8342 | 64.9970 | 73.0169 | 65.3218
ldp | 6.9614 | 5.9485 | 4.9930 | 5.4378 | 1.3046 | -30.2637 | -39.8038 | -41.0947 | 42.2946 | 40.5865 | 46.4557 | 40.1147
ai | 3.7328 | 2.8620 | 2.5671 | 2.3678 | -1.6007 | 27.8123 | 26.9585 | 10.5722 | 69.7477 | 68.4575 | 84.1826 | 68.8946
ave | 7.4653 | 6.3790 | 5.8114 | 5.8476 | -0.4558 | 8.0178 | 0.5094 | -8.4657 | 59.9588 | 58.0137 | 67.8850 | 58.1103
Coding Modes | Depacked Texture |  |  |  | Depacked Depth |  |  |  | Virtual View by VSRS |  |  | 
 | DPCM YUV | Adjust RGB | Assign RGB(Y) | Assign RGB (Y+C) | DPCM YUV | Adjust RGB | Assign RGB(Y) | Assign RGB (Y+C) | DPCM YUV | Adjust RGB | Assign RGB (Y) | Assign RGB (Y+C)
ra | 11.7019 | 10.3264 | 9.8741 | 9.7372 | -1.0712 | 26.5047 | 14.3735 | 5.1253 | 67.8342 | 64.9970 | 73.0169 | 65.3218
ldp | 6.9614 | 5.9485 | 4.9930 | 5.4378 | 1.3046 | -30.2637 | -39.8038 | -41.0947 | 42.2946 | 40.5865 | 46.4557 | 40.1147
ai | 3.7328 | 2.8620 | 2.5671 | 2.3678 | -1.6007 | 27.8123 | 26.9585 | 10.5722 | 69.7477 | 68.4575 | 84.1826 | 68.8946
ave | 7.4653 | 6.3790 | 5.8114 | 5.8476 | -0.4558 | 8.0178 | 0.5094 | -8.4657 | 59.9588 | 58.0137 | 67.8850 | 58.1103

## Slide 53
Depacked Depth of Direct RGB Color Packing
(QP=27)
Depacked Depth of Coded CTDP-LR Format

## Slide 54
Depacked Depth of DPCM-based YUV Color Packing
(QP=27)
Depacked Depth of Coded CTDP-LR Format

## Slide 55
Depacked Depth of Adjusted RGB Color Packing
(QP=27)
Depacked Depth of Coded CTDP-LR Format

## Slide 56
Depacked Depth of Assigned RGB Color Packing (YUV4:0;0)
(QP=27)
Depacked Depth of Coded CTDP-LR Format

## Slide 57
Depacked Depth of Assigned RGB Color Packing (YUV4:2;0)
(QP=27)
Depacked Depth of Coded CTDP-LR Format

## Slide 58: Conclusions

## Slide 59: Conclusions
In this document, the CTDP formats have only two formats (CTDP-TB and CTDP-LR), which will help to simplify the system.
The colored depth packing and depacking is now simplified by direct assignments in uses of 4 chroma_usage modes. The new assigned RGB method avoids all complex computation and independent of color transformations.
In this document, the colored depth packing depacking is performed in assignments of RGB subpixels, which could be depacked either in YCbCr or RGB color space, which allows 4 color pixels can carry 4 or 6 depth values for video coders in YCbCr 4:2:0 chorma format.
In Taiwan, the CTDP formats have been adopted in HYA Company to deliver the 3D video and AR/VR services in CATV systems. The testing channel delivers 4-hour 3D test program per days.

## Slide 60: Adoption Status in Taiwan (3D AR/VR Broadcasting Services)
Hsin Yeong An (HYA) Cable TV Company
Public Television Services

## Slide 61
Depth Texture Packed VR Contents
1 : 3D CTDP; 2 : 3D One view one depth; 3 : 3D Side by side; 4 : 3D Anaglyph; 0 : 2D render

## Slide 62
First 3D and VR Broadcasting System in Taiwan

## Slide 63: CTDP 3D VR Adoption Program
The National Cheng Kung University and the Hsin Yeong An (HYA) Cable TV Company have signed Memorandum of Understanding (MOU) to adopt the CTDP formats to delivering 3D TV programs in HYA Broadcasting Systems. The test and adoption plan is divided into five stages and designed as:
1. Jan. 15, 2017: Complete MOU signing (completed)
2. Mar. 15, 2017: Propose and confirm the test and adoption detailed plans (completed)
3. Dec. 22, 2017: Launched 3D AR/VR Video CTDP broadcasting services (Each day with 4-hour 3D testing program)
4. Aug. 15, 2018: Deliver 3D AR/VR Video CATV services in a remote server and set-top-box with CTDP separate module.
5. Aug.15, 2019: Deliver 3D AR/VR Video CATV services through Set-top-Boxes with Integrated CTDP depacking module (open to all users and charged 3D TV services)
completed

## Slide 64: Test Plan for Headend (New with AR/VR)

## Slide 65
Interactive
Devices
2D
Display
Naked-eyes
3D Display
CTDP
Depacking
VLSI
Digital
Set Top Box
DIBR View Synthesizer
VLSI
Uncompressed
SbS 3D Display
RB-glasses
3D
2D TV Programs
Traditional
SbS 3D
Packing
SbS 3D Display
User 3D Effective Adjustment
Combined
Multiview
Two Views
Mixed RB 2-view
video
CTDP Packing Format
2 Views
Selection
RB 2-view
Mixing
Interactive
Inform
Wireless Unit
Wireless Unit
Reception of AR/VR 3D CTDP Programs

## Slide 66
Thanks for your attentions !