## Slide 1
Simplification of motion compensation filter for affine inter prediction (JVET-C0025)
May 2016
LG Electronics
Hyeongmoon Jang (hyeongmoon.jang@lge.com)

## Slide 2: Summary
  Simplify motion compensation filter for affine inter prediction
Proposed simplification method
  Simplification #1: 1/16 pel motion vector accuracy
  Simplification #2: 6 bit precision filter + 1/16 pel motion vector accuracy
Experimental results
Crosscheck
  JVET-C0093 (by Huawei)
 | RA10 | LDB10 | LBP10
Class A1 | 0.0% |  | 
Class A2 | -0.1% |  | 
Class B | 0.0% | -0.2% | 0.1%
Class C | 0.0% | -0.1% | 0.1%
Class D | 0.0% | 0.2% | 0.1%
Class E |  | 0.1% | 0.1%
Overall | 0.0% | 0.1% | 0.1%
 | RA10 | LDB10 | LBP10
Class A1 | 0.0% |  | 
Class A2 | 0.0% |  | 
Class B | 0.0% | 0.0% | 0.0%
Class C | 0.0% | 0.0% | 0.1%
Class D | 0.0% | 0.1% | 0.1%
Class E |  | 0.0% | 0.2%
Overall | 0.0% | 0.0% | 0.1%
Simplification #1 vs. JEM 2.0
Simplification #2 vs. JEM 2.0

## Slide 3: Proposed method
Simplification #1
  Affine prediction uses 1/64 pel MV accuracy both Luma and Chroma
  Proposed: 1/16 pel & 1/32 pel MV accuracy for each components
    Sub-sampling of 1/64 accuracy filters in JEM2.0 (8-bit precision filters)
    Luma uses 1/16 pel MV accuracy
    Chroma uses 1/32 pel MV accuracy

## Slide 4: Proposed method
Simplification #2
  Proposed: 6-bit filter precision with 1/16-pel filter accuracy
  6-bit filter precision is already used to other MC process
  No need of additional storage for affine inter prediction filters
Position | Filter coefficients
1/16 | { 0, 0, 0, 64, 0, 0, 0, 0 }
2/16 | { 0, 1, -3, 63, 4, -2, 1, 0 }
3/16 | { -1, 2, -5, 62, 8, -3, 1, 0 }
: | :
15/16 | { 0, 1, -2, 4, 63, -3, 1, 0 }
Position | Filter coefficients
1/64 | {-1, 4, -13, 254, 16, -5, 2, -1}
2/64 | {-2, 8, -23, 248, 34, -12, 4, -1}
3/64 | {-2, 10, -31, 239, 52, -17, 5, 0}
: | :
63/64 | {-3, 13, -40, 213, 94, -28, 9, -2}

## Slide 5: Experimental results
 | Random Access Main |  |  | Low-delay B |  |  | Low-delay P |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A1 | 0.0% | 0.0% | 0.1% |  |  |  |  |  | 
Class A2 | -0.1% | -0.1% | -0.1% |  |  |  |  |  | 
Class B | 0.0% | 0.1% | 0.1% | 0.0% | -0.2% | 0.1% | 0.1% | 0.2% | 0.1%
Class C | 0.0% | 0.1% | 0.0% | 0.0% | -0.1% | -0.3% | 0.1% | 0.0% | 0.2%
Class D | 0.0% | -0.1% | -0.2% | 0.2% | 0.2% | 0.3% | 0.1% | 0.7% | -0.1%
Class E |  |  |  | 0.0% | 0.1% | 0.4% | 0.1% | -0.3% | -0.1%
Overall | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.1% | 0.2% | 0.0%
Enc [%] | 100 |  |  | 100 |  |  | 100 |  | 
Dec [%] | 100 |  |  | 100 |  |  | 100 |  | 
 | Random Access Main |  |  | Low-delay B |  |  | Low-delay P |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A1 | 0.0% | 0.0% | -0.1% |  |  |  |  |  | 
Class A2 | 0.0% | -0.1% | -0.1% |  |  |  |  |  | 
Class B | 0.0% | 0.1% | 0.2% | 0.0% | -0.2% | -0.1% | 0.0% | 0.1% | -0.1%
Class C | 0.0% | 0.0% | -0.1% | 0.0% | 0.1% | -0.3% | 0.1% | -0.1% | 0.0%
Class D | 0.0% | -0.2% | -0.1% | 0.1% | 0.0% | -0.3% | 0.1% | 0.6% | -0.3%
Class E |  |  |  | 0.0% | 0.3% | -0.3% | 0.2% | 0.5% | 1.1%
Overall | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | 0.1% | 0.3% | 0.1%
Enc [%] | 101 |  |  | 100 |  |  | 100 |  | 
Dec [%] | 100 |  |  | 100 |  |  | 100 |  | 
Simplification #1 (filter accuracy)
Simplification #2 (filter precision & simplification #1)
Roller Coaster (class A1): -0.7% / -0.3% / -0.2%

## Slide 6: Conclusion
Recommendation
  It is recommended to use the filter set which has 6-bit precision and 1/16-pel filter accuracy for the Affine prediction case also.