## Slide 1: Perceptual Quality Assessment Metric MS-SSIM
Author/ Email:
Hong Zhang, Xiang Ma, Yin Zhao, Haitao Yang
summer.zhanghong@huawei.com
maxiang6@huawei.com

## Slide 2: Motivation
AN OPTIMIZED SYSTEM IS ONLY AS GOOD AS THE OPTIMIZATION CRITERION USED TO DESIGN IT.

## Slide 3: Motivation
Exist metric: MSE or PSNR
  Advantage
    Easy to compute and understand
    Has many desirable mathematical properties
  Disadvantage
    Not so accurate to measure perceived signal quality, sometimes.
      People is more sensitive to structure information
A Perceptual Assessment metric is needed

## Slide 4: SSIM & MS-SSIM
SSIM
MS-SSIM
  Reason for MS
    images contain structures that occur over a range of spatial scales
    HVS decomposes visual data into multiscale spatial channel early in the visual pathway

## Slide 5: Performance comparison of different metrics
Image Database | Measure | PSNR | SSIM | MS-SSIM
LIVE JPEG/JPEG2000 [3] | SCC | 0.901 | 0.936 | 0.966
 | KCC | - | - | -
TID2013[4-6] | SCC | 0.640 | 0.637 | 0.787
 | KCC | 0.470 | 0.464 | 0.608
A57[7] | SCC | 0.825 | 0.903 | -
 | KCC | - | - | -
LIVE2006[8-10] | SCC | 0.876 | - | 0.953
 | KCC | - | - | -
VCL@FER[11] | SCC | - | 0.911 | 0.923
 | KCC | - | 0.733 | 0.750
Video Database | Measure | PSNR | SSIM | MS-SSIM
LIVE [12-13] | SCC | 0.368 | 0.526 | 0.736
 | LCC | 0.404 | 0.544 | 0.744
LIVE Mobile [14-16] | SCC | 0.678 | 0.650 | 0.743
 | LCC | 0.691 | 0.664 | 0.708
MCL-V [17] | SCC | 0.464 | 0.648 | 0.623
 | LCC | 0.472 | 0.650 | 0.621
LCC: (Pearson) Linear Correlation Coefficient
SCC: Spearman Correlation Coefficient
KCC: Kendall Correlation Coefficient

## Slide 6: A: BasketballDrill (original)

## Slide 7: B: BasketballDrill(34.980dB, 0.973363)

## Slide 8: C: BasketballDrill(34.640dB, 0.974801)

## Slide 9: A: BQSquare (original)

## Slide 10: B: BQSquare (32.502dB, 0.982089 )

## Slide 11: C: BQSquare (32.036dB, 0.985329 )

## Slide 12: A: RaceHorses (original)

## Slide 13: B: RaceHorses (27.309dB, 0.931476)

## Slide 14: C: RaceHorses (27.206dB, 0.934179)

## Slide 15: Observations/Suggestions
Observations
  At relatively high bitrates
    Both PSNR and MS-SSIM are consistent with subjective perceptual quality.
  At relatively low bitrates
    PSNR and MS-SSIM may go oppositely, where MS-SSIM is aligned with subjective observation.
Suggestions
  Add MS-SSIM into JEM as an additional quality metric for reference
  Tool evaluation procedure for consideration
    PSNR & MS-SSIM goes to the same direction: rely on PSNR, as always
    PSNR & MS-SSIM goes to opposite direction: pay special attention, may require further analysis