## Slide 1: 360tools usage & results
Samsung

## Slide 2: 360tools SW location
https://github.com/Samsung/360tools

## Slide 3: Projections supported
ERP –
Equi-rectangular projection
ISP –
Icosahedral projection
CMP –
Cube Map projection
OHP –
Octahedron projection
TSP – Truncated square
pyramid projection
SSP - segmented sphere projection

## Slide 4: Conversion to/from ISP
360tools_conv -w WI -h HI -i origERP -o CPP -l WI -m HI -f 0 -n 1 -x 1 -y 2
360tools_conv -w WI -h HI -i CPP -o origISP -l WT -m HT -f 32 -n 1 -x 2 -y 2
360tools_conv -w WT -h HT -i origISP -o origRISP -l WR -m HR -f 11 -n 1 -x 2 -y 2
encoding / decoding
360tools_conv -i origRISP -w WR -h HR -l WT -m HT -o recISP -f 12 -n 1 -x 2 -y 2
360tools_metric -w WI -h HI -l WT -m HT -o CPP -o recISP -f 6 –t 2 -n 1 -x 2 -y 2
-x input bit-depth -w, -h input width, height
-y output bit-depth -l, -m output width, height -q metric indicator
-n number of frames -f conversion format -f , -t projection for metric
ERP
ISP
RISP
-f 1
-f 11
-f 12
-f 2
-f 0
-f 32
Supported, but not used for tests

## Slide 5: Conversion to/from CMP
360tools_conv -w WI -h HI -i origERP -o CPP -l WI -m HI -f 0 -n 1 -x 1 -y 2
360tools_conv -w WI -h HI -i CPP -o origCMP -l WT -m HT -f 33 -n 1 -x 2 -y 2
360tools_conv -w WT -h HT -i origCMP -o origRCMP -l WR -m HR -f 13 -n 1 -x 2 -y 2
encoding / decoding
360tools_conv -i origRCMP -w WR -h HR -l WT -m HT -o recCMP -f 14 -n 1 -x 2 -y 2
360tools_metric -w WI -h HI -l WT -m HT -o CPP -o recCMP -f 6 –t 3 -n 1 -x 2 -y 2
-x input bit-depth -w, -h input width, height
-y output bit-depth -l, -m output width, height -q metric indicator
-n number of frames -f conversion format -f , -t projection for metric
ERP
-f 3
-f 13
-f 14
-f 4
CMP
RCMP
Cube 4x3
Cube 3x2
-f 0
-f 33
Supported, but not used for tests

## Slide 6: Conversion to/from OHP
360tools_conv -w WI -h HI -i origERP -o CPP -l WI -m HI -f 0 -n 1 -x 1 -y 2
360tools_conv -w WI -h HI -i CPP -o origOHP -l WT -m HT -f 34 -n 1 -x 2 -y 2
360tools_conv -w WT -h HT -i origOHP -o origROHP -l WR -m HR -f 15 -n 1 -x 2 -y 2
encoding / decoding
360tools_conv -i origROHP -w WR -h HR -l WT -m HT -o recOHP -f 16 -n 1 -x 2 -y 2
360tools_metric -w WI -h HI -l WT -m HT -o CPP -o recOHP -f 6 –t 4 -n 1 -x 2 -y 2
-x input bit-depth -w, -h input width, height
-y output bit-depth -l, -m output width, height -q metric indicator
-n number of frames -f conversion format -f , -t projection for metric
ERP
-f 5
-f 15
-f 16
-f 6
OHP
ROHP
-f 0
-f 34
Supported, but not used for tests

## Slide 7: Conversion to/from TSP
360tools_conv -w WI -h HI -i origERP -o origTSP -l WT -m HT -f 7 -n 1 -x 1 -y 2
encoding / decoding
360tools_conv -w WT -h HT -l WI -m HI -i recTSP -o recERPfromOHP -f 8 -n 1 -x 2 -y 2
-x input bit-depth -w, -h input width, height
-y output bit-depth -l, -m output width, height
-n number of frames -f conversion format
ERP
-f 7
-f 8
TSP
-f 0
-f 35
Under implementation

## Slide 8: Metrics supported
PSNR (YCbCr)
S-PSNR
  “A frame-work to evaluate omnidirectional video coding schemes, in Mixed and Augmented Reality
WS-PSNR (up-dated by owner)
  m38551(Zhejiang University )
CPP-PSNR
  V. Zakharchenko, K.P. Choi, J.H. Park, Video quality metric for spherical panoramic video, Optics and Photonics, SPIE, 9970, 2016

## Slide 9: ERP specific metrics
S-PSNR
360tools_metric -w WI -h HI -o origERP -r recERPfromISP -l WI -m HI -f 1 –t 1 –q 2 -n 1 -x 1 –y 1 –s sphere_file
360tools_metric -w WI -h HI -o origERP -r recERPfromCMP -l WI -m HI -f 1 –t 1 –q 2 -n 1 -x 1 –y 1 –s sphere_file
WS-PSNR
360tools_metric -w WI -h HI -o origERP -r recERPfromISP -l WI -m HI -f 1 –t 1 –q 3 -n 1 -x 1 –y 1
360tools_metric -w WI -h HI -o origERP -r recERPfromCMP -l WI -m HI -f 1 –t 1 –q 3 -n 1 -x 1 –y 1
-x original/ reconstructed bit-depth -n number of frames
-q metric ID (1 PSNR, 2 S-PSNR, 3 WS-PSNR, 4 –CPP-PSNR)
-f , -t input/output projection indication (1 – ERP, 2 – ISP, 3 –CMP)
sphere_file=../app/360tools_metric/sphere_655362.txt
origERP
WIHI 8b
origISP
WTHT 10b
origCMP
WCHC 10b
recERPfromISP
WIHI 8b
recERPfromCMP
WIHI 8b
2) S-PSNR 3) WS-PSNR,

## Slide 10: Universal metric
CPP-PSNR for 2 ERP inputs:
360tools_metric -w WI -h HI -o origERP -r recERPfromISP -l WI -m HI -f 1 –t 1 –q 4 -n 1 -x 1 –y 1
360tools_metric -w WI -h HI -o origERP -r recERPfromCMP -l WI -m HI -f 1 –t 1 –q 4 -n 1 -x 1 –y 1
CPP-PSNR between ERP and ISP or CMP :
360tools_metric -w WI -h HI -o origERP -r origISP -l WT -m HT -f 1 –t 2 –q 4 -n 1 -x 1 –y 2
360tools_metric -w WI -h HI -o origERP -r origCMP -l WC -m HC -f 1 –t 3 –q 4 -n 1 -x 1 –y 2
-x, y original/ reconstructed bit-depth
-n number of frames
-q metric ID (1 PSNR, 2 S-PSNR, 3 WS-PSNR, 4 –CPP-PSNR)
-f , -t input/output projection indication (1 – ERP, 2 – ISP, 3 –CMP)
origERP
WIHI 8b
origISP
WTHT 10b
origCMP
WCHC 10b
recERPfromISP
WIHI 8b
recERPfromCMP
WIHI 8b
4) CPP-PSNR

## Slide 11: CPP-PSNR explanation
CPP Craster parabolic projection
Each sample has equal area on sphere:
in CCP representation MSE is calculated for only “meaningful” samples (black areas are excluded). MSEPSNR

## Slide 12: Suggested JVET test #1
origERP
origISP
origCube
Enc/Dec:
HM vs JEM
recERP
recISP
recCube
bits
CPP-PSNR
CPP-PSNR
None of the projections has a benefits, all equivalent
Discarded

## Slide 13: Suggested JVET test #2
origERP
origISP
origCube
Enc/Dec:
HM vs JEM
recERP
recISP
recCube
bits
S-PSNR, WS-PSNR
recERPfromISP
recERPfromCMP
In this testing procedure ERP has a benefits (goes through fewer number of conversion steps)
Done, results published, Sept. 8

## Slide 14: Suggested JVET test #3
Test materials come in ERP
ERP
CMP
ISP
TSP
OHP
Enc/Dec
recERP
recCMP
recISP
recTSP
recOHP
CPP-PSNR*
Test materials come in ERP
Enc/Dec
recERP
recCMP
recISP
recTSP
recOHP
Recommended by Huawei:
Informative ** :
ERPrecCMP
ERPrecISP
ERPrecTSP
ERPrecOHP
WS-PSNR
ERP
CMP
ISP
TSP
OHP
*CPP-PSNR means both inputs are converted to CPP and MSE for not-black samples of CPP is calculated
*In this test ERP goes through fewer amount of conversion steps, so has benefits compared to other projections
temporally
temporally

## Slide 15: Test#3 results summary
  BD-rate gain vs ERP as coding projection
Suggested by Huawei
  Each projections goes through the
  same number of conversion steps
Informative
  Gives understanding
  how much benefits ERP has due to
  fewer amount of conversion steps
  (not recommended)
 |  | CPP -PSNR |  | 
 |  | Y | U | U
ISP | 75 | -0.3% | 1.4% | -0.1%
ISP | 100 | -0.7% | 0.1% | -0.6%
CMP | 75 | -0.2% | -0.1% | -0.6%
CMP | 100 | 1.1% | 0.5% | 0.5%
OHP | 75 | 10.3% | 16.3% | 11.8%
OHP | 100 | 10.9% | 16.9% | 12.3%
 |  | WS-PSNR |  | 
 |  | Y | U | U
ISP | 75 | 0.0% | 0.5% | -0.9%
ISP | 100 | 0.5% | -0.8% | -1.4%
CMP | 75 | 3.8% | 0.9% | 0.1%
CMP | 100 | 3.4% | -0.5% | -0.4%
OHP | 75 | 12.0% | 16.4% | 13.0%
OHP | 100 | 12.1% | 15.8% | 12.3%

## Slide 16: Test w/o encoding
 |  | S-PSNR |  |  | WS-PSNR |  |  | CPP-PSNR | 
 | Y | Cb | Cr | Y | Cb | Cr | Y | Cb | Cr
ERP100 | 48.58 | 58.49 | 58.79 | 47.45 | 56.98 | 57.24 | 49.30 | 59.62 | 59.94
ISP75 | 46.70 | 56.23 | 56.39 | 48.03 | 57.91 | 58.12 | 49.05 | 59.34 | 59.48
ISP100 | 47.48 | 57.05 | 57.26 | 48.87 | 58.75 | 59.01 | 51.10 | 61.49 | 61.72
CMP75 | 46.40 | 55.96 | 56.08 | 47.74 | 57.63 | 57.80 | 48.58 | 58.96 | 59.09
CMP100 | 47.16 | 56.63 | 56.82 | 48.47 | 58.28 | 58.51 | 50.41 | 60.59 | 60.86
OHP75 | 46.83 | 56.29 | 56.56 | 48.22 | 58.01 | 58.32 | 49.21 | 59.46 | 59.71
OHP100 | 47.54 | 56.99 | 57.26 | 48.95 | 58.72 | 59.03 | 51.17 | 61.38 | 61.66
TSP25 | 33.60 | 47.23 | 47.13 | 33.82 | 47.73 | 47.62 | 33.68 | 47.67 | 47.59
ERP4K-->CPP4K-->Coding Projection-->ERP4K
CPP4K-->Coding Projection
 | Y | Cb | Cr
BearAttackLeft | 50.74 | 51.57 | 51.66
SheriffLeft | 49.45 | 55.81 | 56.39
LRRHLeft | 37.11 | 47.74 | 49.05
Paramotor | 45.51 | 56.36 | 59.64
Jump | 53.99 | 59.25 | 59.54
Building | 48.50 | 64.78 | 66.27
Boarding | 55.90 | 66.32 | 68.07
Bicyclist | 41.80 | 59.09 | 63.06
Glacier | 48.29 | 63.12 | 63.42
Shark | 43.72 | 57.54 | 49.27
Driving | 55.98 | 61.27 | 60.74
Dancing | 52.04 | 59.05 | 58.41
 | 48.58 | 58.49 | 58.79
Y | Cb | Cr
49.14 | 49.77 | 49.96
47.41 | 53.51 | 54.09
38.52 | 46.50 | 47.80
44.35 | 55.16 | 58.27
52.74 | 57.87 | 57.93
46.70 | 63.22 | 64.89
54.42 | 64.77 | 66.52
40.88 | 58.14 | 61.65
47.76 | 61.90 | 62.19
42.93 | 56.44 | 48.25
53.87 | 59.29 | 58.81
50.64 | 57.16 | 56.55
47.45 | 56.98 | 57.24
Y | Cb | Cr
51.54 | 52.56 | 52.68
50.66 | 58.73 | 59.78
39.45 | 47.76 | 49.07
45.38 | 57.10 | 60.84
54.70 | 60.42 | 60.96
49.02 | 65.35 | 66.57
56.87 | 67.22 | 68.67
41.98 | 59.27 | 63.25
48.42 | 63.93 | 64.28
43.46 | 57.76 | 49.08
57.54 | 63.69 | 63.08
52.54 | 61.70 | 60.97
49.30 | 59.62 | 59.94
ERPCPPERP S-PSNR WS-PSNR CPP-PSNR

## Slide 17: How to generate test materials for Test#3
Size, MD5 check sum

## Slide 18: Recommended sizes for ERP coding
 | WI | HI | WI | HI | WI | HI | %,sizeERP
“ERP100” | 3840 | 1920 | 4448 | 3336 | 3840 | 1920 | 100%
 | 4096 | 2048 | 4736 | 3552 | 4096 | 2048 | 
 | 4320 | 2160 | 4992 | 3744 | 4320 | 2160 | 
 | ERP | CPP | ERPcoding
WIHI
WIHI
Input for Encoder
WIHI
Common projection for quality estimation

## Slide 19: ERPCPPERPfromCPP (for Test#3)
CPP frame size is equal to ERP frame size
Command line
../bin/360tools_conv -i ${ERP} -w ${wi} -h ${hi} -l ${wi} -m ${hi} -o ${CPP} -f 0 -n $2 -x 1 -y 2
../bin/360tools_conv -i ${CPP} -w ${wi} -h ${hi} -l ${wi} -m ${hi} -o ${ERPfromCPP} -f 31 -n $2 -x 2 -y 2
MD5 check sum for {CPP}
  a5f6f4b895af234c0f2a27f6ad9e6131 abyss_great_shark_vr_30p_3840x1920.yuv
  4b3d81b91e87363dac3d48261a4a106a BearAttack-equirect-left-3840x1920.yuv
  d6b22bf490ac6da45e98c3f51d7fe3b3 bicyclist_vr_25p_3840x1920.yuv
  80b5bbeb41876c2d95560a14d30c36e1 glacier_vr_24p_3840x1920.yuv
  608effba2fd645c30d349c5640f16e3c GT_Sheriff-equirect-left-4320x2160.yuv
  086bd2259d8d5c5ae344175656a164c5 LRRH-equirect-left-3840x1920.yuv
  b1ae2c2d8dfa74b03c6bca2455ae3a10 paramotor_training_vr_25p_3840x1920.yuv
  af49a68691d000c91661fbf820093767 skateboarding_vr_60p_4096x2048.yuv
  58451488b18c658d678a04dd4ef47200 Stiched_left_Driving360_30p_4096x2048.yuv
  93c8ad11292d16251d1677cf1a9b7eb1 Stitched_left_Dancing360_30p_4096x2048.yuv
  801874d806d4e82005db73af10ed0bc7 timelapse_basejump_vr_25p_3840x1920.yuv
  09c51bde153137b823d77213bd5e2fd6 timelapse_building_vr_25p_3840x1920.yuv
MD5 check sum for {ERPfromCPP}
  c97a87646f6b452cce588c669018539a abyss_great_shark_vr_30p_3840x1920.yuv
  5262ad8fcfd27ad13298d0bee4a09c5b BearAttack-equirect-left-3840x1920.yuv
  3449cbb9c226776c35dcac1e56444bae bicyclist_vr_25p_3840x1920.yuv
  52f2333d4793f3124a98ad9e9b003372 glacier_vr_24p_3840x1920.yuv
  63248164bdb1851319cdd4116bfa6e53 GT_Sheriff-equirect-left-4320x2160.yuv
  e7843491dc9256c9a75041b62b063fa1 LRRH-equirect-left-3840x1920.yuv
  b8247d866e10aed3e2716df88802c847 paramotor_training_vr_25p_3840x1920.yuv
  27b23d6d0f532808dc3e5edfe3ee8366 skateboarding_vr_60p_4096x2048.yuv
  1a58c19f36e8a4b840c3336eac223f8c Stiched_left_Driving360_30p_4096x2048.yuv
  f62853399f22613ffb79f39deb456a58 Stitched_left_Dancing360_30p_4096x2048.yuv
  e84c465eeeb33e28f0cd1e85be1fcfbb timelapse_basejump_vr_25p_3840x1920.yuv
  c3b979aa878158db3b3f232f07c7a5be timelapse_building_vr_25p_3840x1920.yuv

## Slide 20: Recommended sizes for CMP coding
 | WI | HI |  | WT | HT | WR | HR | %,sizeERP
“CMP75” | 3840 | 1920 | 960 | 3840 | 2880 | 2880 | 1920 | 75%
 | 4096 | 2048 | 1024 | 4096 | 3072 | 3072 | 2048 | 
 | 4320 | 2160 | 1080 | 4320 | 3240 | 3240 | 2160 | 
“CMP100” | 3840 | 1920 | 1112 | 4448 | 3336 | 3336 | 2224 | 100%
 | 4096 | 2048 | 1184 | 4736 | 3552 | 3552 | 2368 | 
 | 4320 | 2160 | 1248 | 4992 | 3744 | 3744 | 2496 | 
 | ERP | CMPRCMP
WIHI
WTHT
WRHR
WIHI
Input for Encoder

## Slide 21: CPPCMP100 (for Test#3)
CPPCMP (Cube 43) RCMP (Cube 23)
../bin/360tools_conv -i ${CPP} -w ${wi} -h ${hi} -l ${wt} -m ${ht} -o ${CMP} -f 33 -n $2 -x 2 -y 2
../bin/360tools_conv -i ${CMP} -w ${wt} -h ${ht} -l ${wr} -m ${hr} -o ${RCMP} -f 13 -n $2 -x 2 -y 2
MD5 check sum for {CMP100}
  f12c79d89882a23b985f5cd2c270455a abyss_great_shark_vr_30p_4448x3336.yuv
  81d3dac94855bb7a5dc1e4f3661edb38 BearAttack-equirect-left-4448x3336.yuv
  8b3389923cb6af09400e912ea548a686 bicyclist_vr_25p_4448x3336.yuv
  fa139e1ec23d71e198bb4cd8ea27c8ce glacier_vr_24p_4448x3336.yuv
  5603c248bf6502a9391e83f8a5dc895b GT_Sheriff-equirect-left-4992x3744.yuv
  752a03dacbed03664528f76f6e36a3e0 LRRH-equirect-left-4448x3336.yuv
  07139f75a0ae8d61b9bfedf1c2e56066 paramotor_training_vr_25p_4448x3336.yuv
  258a81d927840a72bc581a23fa9ea2d8 skateboarding_vr_60p_4736x3552.yuv
  d21881f6807d73cb797c25b15e8cad33 Stiched_left_Driving360_30p_4736x3552.yuv
  e1e853c0b8a901d6f901d6505186cdc2 Stitched_left_Dancing360_30p_4736x3552.yuv
  42dac6d561afa86ceb8a26ba484d227a timelapse_basejump_vr_25p_4448x3336.yuv
  3bfd0dc9bc1b583940efa18a99a53b6b timelapse_building_vr_25p_4448x3336.yuv
MD5 check sum for {RCMP100}
  c38613e32508c8ea46ce055dc68f1bab abyss_great_shark_vr_30p_3336x2224.yuv
  4904a8c6128e5918d991274cff42b07b BearAttack-equirect-left-3336x2224.yuv
  54f276f038e7e39bf55e5e5e8b09b1f3 bicyclist_vr_25p_3336x2224.yuv
  7c5b69f324472a891607d9e7c308c0d1 glacier_vr_24p_3336x2224.yuv
  bd4579ec464be9d99a718b69ae7c9c4a GT_Sheriff-equirect-left-3744x2496.yuv
  bd27c85d82fd025b8184d4697dd4bb97 LRRH-equirect-left-3336x2224.yuv
  39822550cb6ae0c4f2e5580f6901976b paramotor_training_vr_25p_3336x2224.yuv
  0d75ec179336a9ee192da9f2ac3ffa49 skateboarding_vr_60p_3552x2368.yuv
  1d9f0ceda55d5ce8b2f20f622e0cc2b0 Stiched_left_Driving360_30p_3552x2368.yuv
  9257cf6ee481be6594c41836290b5598 Stitched_left_Dancing360_30p_3552x2368.yuv
  be7481e34c4eaedf4ead1c1e5ee39bc8 timelapse_basejump_vr_25p_3336x2224.yuv
  1e6eb4993cc4d006af2153af1c41962b timelapse_building_vr_25p_3336x2224.yuv

## Slide 22: CMP75 (for Test#3)
CPPCMP (Cube 43) RCMP (Cube 23)
../bin/360tools_conv -i ${CPP} -w ${wi} -h ${hi} -l ${wt} -m ${ht} -o ${CMP} -f 33 -n $2 -x 2 -y 2
../bin/360tools_conv -i ${CMP} -w ${wt} -h ${ht} -l ${wr} -m ${hr} -o ${RCMP} -f 13 -n $2 -x 2 -y 2
MD5 check sum for {CMP75}
  b50ebeb3474188295404b87d3a1970e5 abyss_great_shark_vr_30p_3840x2880.yuv
  64930ba5f084c1b0dda2c1fd3bd746c5 BearAttack-equirect-left-3840x2880.yuv
  e2d1ec73966289185eb48f173e55c9c6 bicyclist_vr_25p_3840x2880.yuv
  8ea775c214172982f0fac72f04df6662 glacier_vr_24p_3840x2880.yuv
  9f6d40ffb7da7357ad278179d1e6e2f8 GT_Sheriff-equirect-left-4320x3240.yuv
  e081fc3a05ec818513a166d7e74d6c84 LRRH-equirect-left-3840x2880.yuv
  81c21f4e15021eaa930c268ce2a913bb paramotor_training_vr_25p_3840x2880.yuv
  9ed185d07d5e9a1d96ef2232d7fff44b skateboarding_vr_60p_4096x3072.yuv
  dce88073c0ed2097a4cd56cabce009b0 Stiched_left_Driving360_30p_4096x3072.yuv
  034d13dbc59c9e4c699bbc4c85bfd1dd Stitched_left_Dancing360_30p_4096x3072.yuv
  2d4a0ab39809a21e150b842ae1a87268 timelapse_basejump_vr_25p_3840x2880.yuv
  680bc9532014cfe166de93a50c8c37f9 timelapse_building_vr_25p_3840x2880.yuv
MD5 check sum for {RCMP75}
  14aa130e1d325ee972bcb0cdd96d4a99 abyss_great_shark_vr_30p_2880x1920.yuv
  7e3beebac9da0ce8cd9ed3ca6127b69a BearAttack-equirect-left-2880x1920.yuv
  068482da2e3d2d38e00927b0af15d1fb bicyclist_vr_25p_2880x1920.yuv
  df330d9cd16945fbc3898321ce8ae156 glacier_vr_24p_2880x1920.yuv
  4dab0c7aa25a432ae06e807fcac419f8 GT_Sheriff-equirect-left-3240x2160.yuv
  8bf3fb5f5ffc1236e86ee9f8c0b43f21 LRRH-equirect-left-2880x1920.yuv
  e53b6f0a2c97a83d3d8d10d59aba715b paramotor_training_vr_25p_2880x1920.yuv
  e80cc7fc929c2439c9be1f18466ad95d skateboarding_vr_60p_3072x2048.yuv
  5f193ab42b1d3bebb934f1fe1c82f9ee Stiched_left_Driving360_30p_3072x2048.yuv
  89ae8804628c9636f08e50f607b300b4 Stitched_left_Dancing360_30p_3072x2048.yuv
  d13a97ee04d3daa4783ad76dd5b82029 timelapse_basejump_vr_25p_2880x1920.yuv
  e2b8e6a01ffc95d145b6f439953fff75 timelapse_building_vr_25p_2880x1920.yuv

## Slide 23: Recommended sizes for ISP coding
 | WI | HI |  | WT | HT | WR | HR | %,sizeERP
“ISP75” | 3840 | 1920 | 624 | 3960 | 1872 | 1800 | 2536 | 62%
 | 4096 | 2048 | 776 | 4928 | 2328 | 2240 | 3144 | 84%
 | 4320 | 2160 | 776 | 4928 | 2328 | 2240 | 3144 | 75%
“ISP100” | 3840 | 1920 | 776 | 4928 | 2328 | 2240 | 3144 | 96%
 | 4096 | 2048 | 928 | 5896 | 2784 | 2680 | 3752 | 120%
 | 4320 | 2160 | 928 | 5896 | 2784 | 2680 | 3752 | 108%
 | ERP | ISPRISP
WIHI
WTHT
WRHR
(Sept. 26)
WIHI
WIHI
Input for Encoder

## Slide 24: CPPISP100 (for Test#3)
CPPISP (with black regions) RISP (compact)
../bin/360tools_conv -i ${CPP} -w ${wi} -h ${hi} -l ${wt} -m ${ht} -o ${ISP} -f 32 -n $2 -x 2 -y 2
../bin/360tools_conv -i ${ISP} -w ${wt} -h ${ht} -l ${wr} -m ${hr} -o ${RISP} -f 12 -n $2 -x 2 -y 2
MD5 check sum for {ISP100}
  6c030c2871a603ef4a38069de728f690 abyss_great_shark_vr_30p_4928x2328.yuv
  de93529fda872d5116a7d8e30499c863 BearAttack-equirect-left-4928x2328.yuv
  5fd7002490029ea8eab0e8a83230c2c7 bicyclist_vr_25p_4928x2328.yuv
  464c254a62306ca36826b42b802a9d55 glacier_vr_24p_4928x2328.yuv
  b7e0b981290a094b760edced4a5749c4 GT_Sheriff-equirect-left-5896x2784.yuv
  d04f4e3d2261ca5d092b5460d3e33640 LRRH-equirect-left-4928x2328.yuv
  360f89aa3a19a97f240ed14dae688abd paramotor_training_vr_25p_4928x2328.yuv
  f5f33f94dbf9627327c539a35d170615 skateboarding_vr_60p_5896x2784.yuv
  7d4813c258c6fb6a1a7bb9e6f7936c13 Stiched_left_Driving360_30p_5896x2784.yuv
  5e044a069b1862e54a4afa3aa1fb4b79 Stitched_left_Dancing360_30p_5896x2784.yuv
  f87c66630c3854198505cf863d8fcc32 timelapse_basejump_vr_25p_4928x2328.yuv
  c9e0f82c2b7b25742505aeb1eb261954 timelapse_building_vr_25p_4928x2328.yuv
MD5 check sum for {RISP100}
  eabb16d42d1885d915273dd3a490affc abyss_great_shark_vr_30p_2240x3144.yuv
  6e9c82ab24b877da006f9d490b29d04a BearAttack-equirect-left-2240x3144.yuv
  d15239ed78226d2b8c409ff4212a6200 bicyclist_vr_25p_2240x3144.yuv
  0d7d14837a00e9eea7a34a5f4392147c glacier_vr_24p_2240x3144.yuv
  c5fcccd0b9066b1e93b2d6c32100da4d GT_Sheriff-equirect-left-2680x3752.yuv
  5e576abc1b5abee893e259e7d5b7b885 LRRH-equirect-left-2240x3144.yuv
  611262eee6e7f06e07de473ac1a59230 paramotor_training_vr_25p_2240x3144.yuv
  46d649c68423f4f9ebf82c1babe254f0 skateboarding_vr_60p_2680x3752.yuv
  b82e18c83b454bbc2ee61133b9bbdc0a Stiched_left_Driving360_30p_2680x3752.yuv
  eaf03c33d105e63a8a0a00f1cd91a627 Stitched_left_Dancing360_30p_2680x3752.yuv
  712bb31f2cbbafbeed8dc7761315578b timelapse_basejump_vr_25p_2240x3144.yuv
  a79991236d658590ed124d7d9195fd23 timelapse_building_vr_25p_2240x3144.yuv

## Slide 25: CPPISP75 (for Test#3)
CPPISP (with black regions) RISP (compact)
../bin/360tools_conv -i ${CPP} -w ${wi} -h ${hi} -l ${wt} -m ${ht} -o ${ISP} -f 32 -n $2 -x 2 -y 2
../bin/360tools_conv -i ${ISP} -w ${wt} -h ${ht} -l ${wr} -m ${hr} -o ${RISP} -f 12 -n $2 -x 2 -y 2
MD5 check sum for {ISP75}
  cf5d80b387bdea24082ec4f4ad629363 abyss_great_shark_vr_30p_3960x1872.yuv
  75e5e4651e3c27c8c16ca8d725b915e0 BearAttack-equirect-left-3960x1872.yuv
  bc66311c8de5849d6c7b3c4bf1f5c0bf bicyclist_vr_25p_3960x1872.yuv
  98302df0a32766009c03f4395c3fd685 glacier_vr_24p_3960x1872.yuv
  5d9c3a350af86dcc86fb4b2ebc6b4019 GT_Sheriff-equirect-left-4928x2328.yuv
  ea3c6ee569e462d6eb24f5cac8f6cf05 LRRH-equirect-left-3960x1872.yuv
  40629ce157f6ec4945a4c9ddd9e4e2b3 paramotor_training_vr_25p_3960x1872.yuv
  f6cac53db38ffb09026be49421583f2a skateboarding_vr_60p_4928x2328.yuv
  181229a91289fdfdf1e03aec63fec172 Stiched_left_Driving360_30p_4928x2328.yuv
  b1f0f438fe89e7ff287ab4830085349f Stitched_left_Dancing360_30p_4928x2328.yuv
  e42887b48e5589afd05e58a179eb3648 timelapse_basejump_vr_25p_3960x1872.yuv
  6eb8e9c981103d3bc8c22f98c4be3083 timelapse_building_vr_25p_3960x1872.yuv
MD5 check sum for {RISP75}
  cd44a16233373ac137f36bc9e9670075 abyss_great_shark_vr_30p_1800x2536.yuv
  26c5e97000f27ae2858e639aad742ff0 BearAttack-equirect-left-1800x2536.yuv
  3c1daba6ced9533e12b8dda7cf2790cf bicyclist_vr_25p_1800x2536.yuv
  fb0fa4518dab52694046a7dc1379c4e7 glacier_vr_24p_1800x2536.yuv
  8a9ec54636941f873adc7a8b1e69addc GT_Sheriff-equirect-left-2240x3144.yuv
  70f9e51c78b7b725e11431c8f00a2fbe LRRH-equirect-left-1800x2536.yuv
  dbce7030e9d772ac0e990d685c8db7a7 paramotor_training_vr_25p_1800x2536.yuv
  e88d703ce57134f1fd92060ce4723e86 skateboarding_vr_60p_2240x3144.yuv
  0b7dc6e5eafc0b3d5b948101ea81e970 Stiched_left_Driving360_30p_2240x3144.yuv
  fa4130ace05aac65db07a815efc4c2f5 Stitched_left_Dancing360_30p_2240x3144.yuv
  21fe90efa8520441eaa94ec2228cfbc7 timelapse_basejump_vr_25p_1800x2536.yuv
  5c73ce219c8fd8ee7f06afa186f130a5 timelapse_building_vr_25p_1800x2536.yuv

## Slide 26: Recommended sizes for OHP coding
 | WI | HI |  | WT | HT | WR | HR | %,sizeERP
“OHP75” | 3840 | 1920 | 1088 | 5024 | 2176 | 5024 | 1088 | 74%
 | 4096 | 2048 | 1136 | 5248 | 2272 | 5248 | 1136 | 71%
 | 4320 | 2160 | 1240 | 5728 | 2480 | 5728 | 1240 | 76%
“OHP100” | 3840 | 1920 | 1296 | 5984 | 2592 | 5984 | 1296 | 105%
 | 4096 | 2048 | 1344 | 6208 | 2688 | 6208 | 1344 | 99%
 | 4320 | 2160 | 1448 | 6688 | 2896 | 6688 | 1448 | 104%
 | ERP | OHPROHP
WTHT
WRHR
WIHI
WIHI
Input for Encoder

## Slide 27: CPPOHP100 (for Test#3)
CPPOHP (with black regions) ROHP (compact)
../bin/360tools_conv -i ${CPP} -w ${wi} -h ${hi} -l ${wt} -m ${ht} -o ${ISP} -f 34 -n $2 -x 2 -y 2
../bin/360tools_conv -i ${ISP} -w ${wt} -h ${ht} -l ${wr} -m ${hr} -o ${RISP} -f 15 -n $2 -x 2 -y 2
MD5 check sum for {OHP100}
  982404c919fee7f2949778e89eb5bd36 abyss_great_shark_vr_30p_5984x2592.yuv
  92c07e838170f2f5a79afe7bf10aa3b8 BearAttack-equirect-left-5984x2592.yuv
  8548f0d22bdb078cabe254b49c4a4498 bicyclist_vr_25p_5984x2592.yuv
  5918154cd3efbf12613a39448b72bcd4 glacier_vr_24p_5984x2592.yuv
  27faa7898e8689bea4df9989e01adac4 GT_Sheriff-equirect-left-6688x2896.yuv
  516e7d18e4ee5a89e2fa4c27c61e2c0c LRRH-equirect-left-5984x2592.yuv
  6190ab419894ec91de3ffefcb72a5486 paramotor_training_vr_25p_5984x2592.yuv
  e77f4019f38679fa81d049bed6dcc9a9 skateboarding_vr_60p_6208x2688.yuv
  fb803735c60fe65ed97567553023c115 Stiched_left_Driving360_30p_6208x2688.yuv
  65b3c4d0d3c10bd0b7f31ceda2c922cb Stitched_left_Dancing360_30p_6208x2688.yuv
  defaa91f39b2f404283cfbcb80d991b3 timelapse_basejump_vr_25p_5984x2592.yuv
  c9493e321f8e118210912d2011e20118 timelapse_building_vr_25p_5984x2592.yuv
MD5 check sum for {ROHP100}
  d8c91d1de5b6a94dbc5a914b1eeefd2e abyss_great_shark_vr_30p_5984x1296.yuv
  7e03e8a5fafd2e1589600537ed1edd06 BearAttack-equirect-left-5984x1296.yuv
  4630128ee7eda6b05683155dd501fdf7 bicyclist_vr_25p_5984x1296.yuv
  d32211813594e5ce5af99234cc11e3a5 glacier_vr_24p_5984x1296.yuv
  d9ba9a5cc4cab27d2c6af0250be1038c GT_Sheriff-equirect-left-6688x1448.yuv
  175fcf31b33526de110b46531c9fc1d0 LRRH-equirect-left-5984x1296.yuv
  985c66c1d4d5fd308f26a737d692be60 paramotor_training_vr_25p_5984x1296.yuv
  df8a83d8246ce9d7ce633ccccf98f47a skateboarding_vr_60p_6208x1344.yuv
  9f4069b3f679041013b314883054996f Stiched_left_Driving360_30p_6208x1344.yuv
  77544df7e5c050f06e925fa954ffdf60 Stitched_left_Dancing360_30p_6208x1344.yuv
  4357c89d9ed2c0fbc256afc0d09ece61 timelapse_basejump_vr_25p_5984x1296.yuv
  e18e49df4de82bf77f24e50a3c194864 timelapse_building_vr_25p_5984x1296.yuv

## Slide 28: CPPOHP75 (for Test#3)
CPPOHP (with black regions) ROHP (compact)
../bin/360tools_conv -i ${CPP} -w ${wi} -h ${hi} -l ${wt} -m ${ht} -o ${ISP} -f 34 -n $2 -x 2 -y 2
../bin/360tools_conv -i ${ISP} -w ${wt} -h ${ht} -l ${wr} -m ${hr} -o ${RISP} -f 15 -n $2 -x 2 -y 2
MD5 check sum for {OHP75}
  0460d77be8a0f47cae5bdbc42c27eb7d abyss_great_shark_vr_30p_5024x2176.yuv
  132946b21a5b809b0d534070089276d3 BearAttack-equirect-left-5024x2176.yuv
  c44669bbb9c7acc6a6bd7dc9482fc8bf bicyclist_vr_25p_5024x2176.yuv
  db721d00cfa1fe667baaf4d64cce4f11 glacier_vr_24p_5024x2176.yuv
  ce2fef3ddd747a6d3ff1cab6f62f50cb GT_Sheriff-equirect-left-5728x2480.yuv
  d825bed3d4006da82122678aa6bfca0b LRRH-equirect-left-5024x2176.yuv
  b68c0b90eff9984cde177b5656e3f236 paramotor_training_vr_25p_5024x2176.yuv
  085f1bb602321ca4e513d7649f46a5d0 skateboarding_vr_60p_5248x2272.yuv
  3813847f0d994ac676f45f1f3cc3882e Stiched_left_Driving360_30p_5248x2272.yuv
  5ed915cb83541b4b9cf5ee9b405388ab Stitched_left_Dancing360_30p_5248x2272.yuv
  47d3390d57d2be48b51a2297c83e4f83 timelapse_basejump_vr_25p_5024x2176.yuv
  80ef683f0da1291cff6c0735a9e7bf60 timelapse_building_vr_25p_5024x2176.yuv
MD5 check sum for {ROHP75}
  e4c12edeea0e3b55455d4dcc89a2391e abyss_great_shark_vr_30p_5024x1088.yuv
  b8f08303a43a244d39ee1b3b0d7139cd BearAttack-equirect-left-5024x1088.yuv
  dfe55c412b76bba0d2ad6dac427366b4 bicyclist_vr_25p_5024x1088.yuv
  85cd0a7cd9572c7cc927208bbafceae7 glacier_vr_24p_5024x1088.yuv
  70071456a75b4c6a5c48c344eb32ea76 GT_Sheriff-equirect-left-5728x1240.yuv
  c979166dad4d01d785ea579c608adf99 LRRH-equirect-left-5024x1088.yuv
  2203da489df57478a61c9984709e741c paramotor_training_vr_25p_5024x1088.yuv
  24f3a57ec194a136d2f70185662e3aec skateboarding_vr_60p_5248x1136.yuv
  4e7bb232366a834162721c9485f43b9f Stiched_left_Driving360_30p_5248x1136.yuv
  f5de95eaf5b906d5bc478b0054255a89 Stitched_left_Dancing360_30p_5248x1136.yuv
  be546c6c82a23bc9746a04138c5c04af timelapse_basejump_vr_25p_5024x1088.yuv
  963f73284192abe7562dd51ac19453ad timelapse_building_vr_25p_5024x1088.yuv

## Slide 29: Recommended sizes for TSP coding
 | WI | HI | WT | HT | %,sizeERP
“TSP25” | 3840 | 1920 | 1920 | 960 | 25%
 | 4096 | 2048 | 2048 | 1024 | 25%
 | 4320 | 2160 | 2160 | 1080 | 25%
 | ERP | TSP
WIHI
WIHI
CPPTSP is under implementation
WTHT

## Slide 30: ERPTSP25 (for Test#3)
ERPTSP
../bin/360tools_conv -i ${ERP} -w ${wi} -h ${hi} -l ${wt} -m ${ht} -o ${TSP} -f 7 -n $2 -x 1 -y 2
MD5 check sum for {TSP25}
  14c5aafaef40fd82ec2bbd380ee4e056 abyss_great_shark_vr_30p_1920x960.yuv
  3bb29a5a4ce0f8bdaa22a0ff25b57352 BearAttack-equirect-left-1920x960.yuv
  4c214e50229b532f40ec9b418b27b6e9 bicyclist_vr_25p_1920x960.yuv
  b13c78883721f0013b17787a3ecd20b5 glacier_vr_24p_1920x960.yuv
  2072eac382c73b9f40f087c8ce59c892 GT_Sheriff-equirect-left-2160x1080.yuv
  9f7df5a5ed03cb5b854ce2bbbee6f2f3 LRRH-equirect-left-1920x960.yuv
  175e3d00a27c283d34fb008db8eb59c6 paramotor_training_vr_25p_1920x960.yuv
  0cb70da8df7a0cefb58b87395d1d2fae skateboarding_vr_60p_2048x1024.yuv
  0703a10a07d896ebfc45f391bd4e1514 Stiched_left_Driving360_30p_2048x1024.yuv
  6d48b849d28311023bc39194901fdc74 Stitched_left_Dancing360_30p_2048x1024.yuv
  d15adef5d7866fe06f0a40ddb2a481f7 timelapse_basejump_vr_25p_1920x960.yuv
  85a010169e240a87768d63efdad3ce74 timelapse_building_vr_25p_1920x960.yuv