## Slide 1: D0069: Bilateral filter after inverse transform
Jacob Ström, Per Wennersten, Ying Wang, Kenneth Andersson, Jonatan Samuelsson
Ericsson Research

## Slide 2: Outline
What is a bilateral filter
Where in the decoder to place it
The particular bilateral filter tested
Results

## Slide 3: Regular fir filter
A regular FIR filter has weights that depend on the distance to the pixel in screen space.
1
1
6
1
1
6
6
6
36
64
1

## Slide 4: Regular fir filter

## Slide 5: Bilateral filter

## Slide 6: Bilateral filter
That value up there is surely a long way off...

## Slide 7: Bilateral filter
In a bilateral filter the weights depend both on the spatial distance and the distance in intensity.
0
1
6
1
1
6
6
6
36
63
1
That value up there is surely a long way off...

## Slide 8: example
Before filtering
FIR filtering
Bilateral filtering

## Slide 9: where in the decoder
transform coefficients
decoded residual
prediction
clip to [0, 1023]
recon- struction
bilateral filter
new recon- struction

## Slide 10: ReGULAR FIR filter
spatial distance
weight
pixel to filter is (i,j)
weight to calculate is (k,l)

## Slide 11: General bilateral filter
spatial distance
intensity distance
weight

## Slide 12: Proposed bilateral filter
spatial distance
intensity distance
weight
determined by TU size
determined by QP

## Slide 13: Proposed bilateral filter
Plus-shaped filter
  Only two distances simplifies spatial part of filter
Weights pre-calculated using look-up table (LUT)
four
TU
sizes
1023 possible values of
(4 kilobytes)

## Slide 14: Results
Overall BD-rate improvement: 0.5% (All Intra) and 0.5% (Random Access, 3 sequences not yet ready.)
No change for low delay P (0.0%) and small loss for low delay B (-0.1%)
Complexity increase AI: 9% (encoder) and 7% (decoder).
Complexity increase RA: (estimate): 4% (encoder) and 3% (decoder).
Thanks to Qualcomm for crosscheck.

## Slide 15: proposal
Start an exploration experiment to study bilateral filtering in more detail until next JVET meeting.

## Slide 17: Details of sigmas

## Slide 18
 | Over HM-16.6-JEM-3 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,34% | 0,49% | 0,42% | 108% | 106%
Class A2 | -0,49% | 0,17% | 0,24% | 101% | 103%
Class B | -0,28% | 0,49% | 0,33% | 100% | 103%
Class C | -0,86% | 0,12% | 0,15% | 101% | 101%
Class D | -0,60% | 0,28% | 0,28% | 100% | 101%
Class E | -0,60% | 0,11% | 0,05% | 98% | 101%
Overall | -0,51% | 0,29% | 0,26% | 101% | 103%
Class F (optional) | -1,91% | -0,11% | 0,02% | 99% | 101%
 | Over HM-16.6-JEM-3 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,64% | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | -0,52% | 0,04% | -0,22% | 89% | 87%
Class C | -0,43% | -0,26% | -0,18% | 89% | 85%
Class D | -0,45% | 0,17% | 0,54% | 88% | 89%
Class E |  |  |  |  | 
Overall (Ref) | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class F (optional) | -1,32% | -0,19% | -0,06% | 86% | 84%
Our computer cluster was overloaded and these timing measurements are unreliable. The timings reported on slide 14 are for part of one sequence running Basketballdrive (QP 32) on a single computer.
Class A2 is not yet ready. Averaging over all other classes brings the gain for RA to 0.5%.
All Intra
Random Access

## Slide 19: Low delay
 | Over HM-16.6-JEM-3 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0,01% | 0,81% | 0,84% | 103% | 102%
Class C | -0,23% | 0,45% | 0,32% | 97% | 97%
Class D | -0,74% | 0,45% | 0,83% | 94% | 95%
Class E | 1,37% | 1,05% | 1,85% | 89% | 92%
Overall (Ref) | 0,01% | 0,67% | 0,90% | 96% | 97%
Class F (optional) | -1,94% | -0,07% | -0,52% | 101% | 100%
 | Over HM-16.6-JEM-3 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,18% | 0,91% | 0,80% | 100% | 100%
Class C | -0,06% | 0,81% | 0,46% | 96% | 95%
Class D | -0,78% | 0,65% | 0,26% | 125% | 120%
Class E | 1,58% | 1,19% | 1,51% | 97% | 99%
Overall (Ref) | 0,14% | 0,87% | 0,71% | 104% | 103%
Class F (optional) | -1,56% | 0,05% | 0,03% | 95% | 97%
Small loss for Low Delay B -0.1%
Low Delay B
Low Delay P
No change for Low Delay P 0.0%