## Slide 1: JVET-E0035: Enhanced Template Matching in FRUC Mode
Yongbing Lin, Xu Chen, Jicheng An, Jianhua Zheng

## Slide 2: Outlines
Issues in existing template matching FRUC mode in JEM-4.0
  mismatch issue: uni-directional template matching vs. bi-directional MCP
Proposed enhancements
  bi-directional template matching
  selection between uni-directional MCP and bi-directional MCP
Experimental results
  coding gain: 0.38%(RA), 0.12%(LDB), with no enc/dec time increase

## Slide 3: Template matching(TM) based prediction in JEM-4.0
Mismatch issue
  The existing TM is a kind of uni-directional search
  The motion derived by uni-directional TM is not optimal for bi-directional MCP
Proposed enhancements
  bi-directional TM is introduced, and following rules are enabled
    Uni-directional MCP uses the motion derived by uni-directional TM
    Bi-directional MCP uses the motion derived by bi-directional TM
  Adaptive selection between uni-directional MCP and bi-directional MCP
    In terms of distortion costs of 1st and 2nd template matchings
1st template matching in list0 ref Pictures
2nd template matching in list1 ref Pictures
Bi-directional MCP
template
CurrPU
CurrPic (B frame)
Ref1
Ref0
template

## Slide 4: Proposed enhancements(red color)
The proposed bi-directional TM consists of
  Updating of current template: T’C = 2*TC – T0
  The 2nd TM uses the updated template
The proposed selection between uni-directional MCP and bi-directional MCP
  cost0: distortion of uni-directional TM, i.e. 1st TM
  costBi: distortion of bi-directional TM, i.e. 2nd TM
  If cost0 is less than 0.5*cost1, then perform uni-directional MCP, otherwise perform bi-directional MCP
get template T0 matched to current template Tc from list0 reference pictures ( motion info MV0, cost0 )
get template T1 matched to updated template T’C from list1 reference pictures ( motion info MV1, cost1 )
Bi-prediction based on MV0 and MV1
Update current template:
T’C = 2*TC – T0
cost0 < 0.5*cost1
Uni-prediction based on MV0
get template T0 matched to current template Tc from list0 reference pictures ( motion info MV0 )
get template T1 matched to current template Tc from list1 reference pictures ( motion info MV1 )
Bi-prediction based on MV0 and MV1
Proposed template matching FRUC mode
Existing template matching FRUC mode
Y
N
1st TM
2nd TM
MCP

## Slide 5: Comparison between cost0 and 0.5*cost1
cost0 in the 1st template matching is just prediction error of current template from uni-prediction point of view.
cost1 in the 2nd template matching is 2 times of prediction error of current template from bi-prediction point of view.
1st template matching, ( cost0 )
2nd template matching, ( cost1 )
Uni-/Bi-directional MCP
Update template: T’C = 2*TC – T0
template
CurrPU
CurrPic (B frame)
Ref1
Ref0
template

## Slide 6: Experimental results
 | Over HM-16.6-JEM-4 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.08% | -0.08% | -0.20% | 99% | 103%
Class C | -0.15% | -0.37% | -0.59% | 99% | 96%
Class D | -0.11% | -0.19% | -0.21% | 98% | 102%
Class E | -0.14% | -0.41% | -0.01% | 100% | 99%
Overall (Ref) | -0.12% | -0.24% | -0.27% | 99% | 100%
Class F (optional) | -0.17% | -0.48% | -0.44% | 100% | 100%
Recommendation
  Due to the coding gain and no enc/dec time increase, it is recommended to inclusion of the proposed methods into next JEM version.
 | Over HM-16.6-JEM-4 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.53% | -0.14% | -0.57% | 99% | 100%
Class A2 | -0.57% | -0.60% | -0.69% | 98% | 98%
Class B | -0.25% | -0.29% | -0.21% | 99% | 102%
Class C | -0.40% | -0.65% | -0.54% | 98% | 103%
Class D | -0.16% | -0.36% | -0.02% | 99% | 99%
Class E |  |  |  |  | 
Overall (Ref) | -0.38% | -0.40% | -0.40% | 99% | 100%
Class F (optional) | -0.33% | -0.38% | -0.31% | 98% | 102%
Table 1. BD rate saving for the proposed methods under RA configuration
Table 2. BD rate saving for the proposed methods under LDB configuration
Anchor: JEM-4.0, CTC
Test: the proposed methods
0.38% BD rate saving for RA
0.12% BD rate saving for LDB
no encoding/decoding time increase
Thanks Qualcomm for crosschecking!

## Slide 7
Thank You
www.hisilicon.com

## Slide 8: Combination of proposal and JVET-E0052
Performance test
  Anchor: JEM-4.0 CTC, RA configuration
 | BD rate Y | U | V | EncTime | DecTime
Proposal | -0.38% | -0.40% | -0.40% | 99% | 100%
JVET-E0052 (EE5.2) | -0.42% | -0.45% | -0.47% | 102% | 102%
Proposal + E0052 | -0.76% | -0.79% | -0.84% | 103% | 100%
Test results show that performance of proposal and JVET-E0052 can be additive