## Slide 1: JVET-E0051 EE1: Residual Coefficient Sign Prediction
Gordon Clare, Félix Henry – Orange Labs, bcom

## Slide 2: Residual Coefficient Sign Prediction
Presented in JVET-D0031 (Chengdu)
Principle
  Predict N luma signs per TU and replace them with CABAC-coded sign residues
  The top/left border pixels of the current block are reconstructed under all 2N sign assumptions
    A trick is used to reduce the number of inverse transforms
  Signs are predicted by minimizing top/left border distortion of the current block against past pixels
  Two CABAC contexts used for the signs (low/high probability)
p0,0
p1,0
p2,0
p3,0
p0,1
p0,2
-5
-1
p0,3
p0,0
p1,0
p2,0
p3,0
p0,1
p0,2
-5
-1
p0,3
p0,0
p1,0
p2,0
p3,0
p0,1
p0,2
-5
-1
p0,3
2N hypothesis reconstructions
p-1,0
p-1,1
p-1,2
p-1,3
p-2,0
p-2,1
p-2,2
p-2,3
p0,-1
p1,-1
p2,-1
p3,-1
p0,-2
p1,-2
p2,-2
p3,-2
previously reconstructed neighbor pixels

## Slide 3: Exploration Experiment 1
Questions raised
  Test 1 to 5: Gain and complexity increase with number of predicted signs?
    What was tested: Implementation of sign prediction in JEM4 with N=1,2,3,4,5
  Test 6: What is the complexity and gain impact if residue sign prediction processing is moved from it's current position in RDO to final encode?
    What was tested: Non-normative change of the encoder, blocks with one size strictly larger than 16 do not use sign prediction during RDO

## Slide 4: All Results
TEST1
n=1
TEST6
n=4, out of RDO
TEST2
n=2
TEST3
n=3
TEST4
n=4
TEST5
n=5
 | Main 10 over HM-16.6-JEM-4 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
AI | -0,4% | -0,4% | -0,4% | 141% | 127%
RA | -0,5% | -0,3% | -0,4% | 117% | 103%
LD | -0,5% | -0,1% | -0,2% | 112% | 104%
LP | -0,5% | -0,2% | -0,2% | 119% | 105%
AVERAGE | -0,5% | -0,3% | -0,3% | 122% | 110%
 | Main 10 over HM-16.6-JEM-4 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
AI | -0,4% | -0,3% | -0,3% | 133% | 122%
RA | -0,4% | -0,2% | -0,4% | 114% | 103%
LD | -0,4% | 0,0% | -0,2% | 110% | 103%
LP | -0,4% | -0,3% | -0,2% | 115% | 105%
AVERAGE | -0,4% | -0,2% | -0,3% | 118% | 108%
 | Main 10 over HM-16.6-JEM-4 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
AI | -0,5% | -0,5% | -0,5% | 158% | 141%
RA | -0,6% | -0,4% | -0,5% | 123% | 105%
LD | -0,6% | 0,0% | -0,3% | 116% | 105%
LP | -0,6% | -0,3% | -0,4% | 124% | 107%
AVERAGE | -0,6% | -0,3% | -0,4% | 130% | 114%
 | Main 10 over HM-16.6-JEM-4 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
AI | -0,5% | -0,4% | -0,4% | 141% | 138%
RA | -0,5% | -0,3% | -0,4% | 111% | 103%
LD | -0,4% | -0,1% | -0,1% | 104% | 107%
LP | -0,5% | -0,3% | -0,3% | 107% | 105%
AVERAGE | -0,5% | -0,3% | -0,3% | 116% | 113%
 | Main 10 over HM-16.6-JEM-4 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
AI | -0,5% | -0,4% | -0,4% | 149,4% | 132,7%
RA | -0,6% | -0,5% | -0,6% | 120,0% | 104,4%
LD | -0,5% | -0,2% | -0,3% | 114,1% | 104,5%
LP | -0,5% | -0,4% | -0,4% | 121,4% | 105,5%
AVERAGE | -0,5% | -0,4% | -0,4% | 126,2% | 111,8%
 | Main 10 over HM-16.6-JEM-4 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
AI | -0,2% | -0,2% | -0,2% | 125% | 116%
RA | -0,3% | -0,2% | -0,3% | 110% | 102%
LD | -0,2% | 0,0% | -0,3% | 108% | 103%
LP | -0,3% | -0,1% | -0,2% | 112% | 104%
AVERAGE | -0,2% | -0,1% | -0,3% | 114% | 106%

## Slide 5: Synthetic View - Random Access
EncT
Y BDR - RA
Test1
Test2
Test3
Test4
Test5
Test6
 | Y | U | V | EncT | DecT
Test1 (N=1) | -0,3% | -0,2% | -0,3% | 110% | 102%
Test1 (N=2) | -0,4% | -0,2% | -0,4% | 114% | 103%
Test1 (N=3) | -0,5% | -0,3% | -0,4% | 117% | 103%
Test1 (N=4) | -0,6% | -0,5% | -0,6% | 120% | 104%
Test1 (N=5) | -0,6% | -0,4% | -0,5% | 123% | 105%
Test1 (N=4, NoRDO16) | -0,5% | -0,3% | -0,4% | 111% | 103%
Chart: 
| 1.1044039959456269 | 1.1376788330880725 | 1.1688588784260767 | 1.2002850416953814 | 1.2312811804795709 | 1.1079725173745443
 | -0.0026709 | -0.0042122 | -0.0052075 | -0.0056434 | -0.0061255 | -0.0048781

## Slide 6: Proposal
Adopt Test 6 variant in next JEM version
Crosschecks
  Tests 1,2 and 3 by Samsung in JVET-E0038
  Test 4 by Sharp in JVET-0102
  Tests 5 and 6 by Fujitsu in JVET-E0072
 | Main 10 over HM-16.6-JEM-4 (parallel) |  |  |  | 
 | Y | U | V | EncT | DecT
AI | -0,5% | -0,4% | -0,4% | 141% | 138%
RA | -0,5% | -0,3% | -0,4% | 111% | 104%
LD | -0,4% | -0,1% | -0,1% | 104% | 107%
LP | -0,5% | -0,3% | -0,3% | 107% | 105%
AVERAGE | -0,5% | -0,3% | -0,3% | 116% | 113%
Average for Inter modes | -0.5% | -0.3% | -0.3% | 107% | 105%