## Slide 1: Floating point QP support for parallel encoding in RA configuration (JVET-E0059)
Xiang Ma, Huanbang Chen, Haitao Yang, Sychev Maxim (Huawei)

## Slide 2: Contents
Background
  Parallel encoding method
  Floating point QP
  Existing frame level QP setting
Parallel encoding problem and solution
Frame level QP setting problem and solution
Conclusion/Suggestion

## Slide 3: Background
  Parallel encoding method
  full-length sequence encoding is split to a set of independent RAS encoding
  RAS: Random Access Segment, about 1s length video segment in current encoder configuration
  Floating point QP
  change the base QP once
  base QP of the pictures starting from switching POC picture (or QP change point) is QP+1
  the switching POC is calculated by encode frame number and the decimal part of the floating point QP, then rounded to the nearest GOP start picture.

## Slide 4: Background
Existing frame level QP setting:
  QP = QPb+QPOffset1+QPOffset2+ QPOffset3 (1)
The QP setting process for a non-I slice can be described as:
  Step1: Get QPb
  Step2: Get QP1= QPb+ QPOffset1, here QPOffset1 is related to picture position in current GOP in hierarchical structure
  Step3: Get QP2= QP1+ QPOffset2, here QPOffset2 = a*QP1+b
  Step4: Get QP3= QP2+ QPOffset3, here QPOffset3 is a two-value (0 or 1) variable , QP3 is the QP of current slice.
QP = QPb+QPOffset1+( a*( QPb+QPOffset1)+b)+ QPOffset3 (2)

## Slide 5: Parallel encoding problem and solution
Problem:
  The existing parallel encoding script cannot be used directly, when floating point QP is used.
Solution/Modification:
  Use RAS level floating point QP instead of current sequence level floating point QP
    the RASs before switching POC picture will be fed QP. (integer QP)
    the RAS containing switching POC picture will be fed a new floating point QP .(floating point QP)
    the RASs after switching POC picture will be fed QP+1. (integer QP)
New floating point QP:
Integer part: QP
Decimal part: (NRAS1-POC’S)/NRAS1
NRAS1 : The frame number of RAS containing switching POC picture
POC’S : The POC of the switching POC picture in RAS containing switching POC picture

## Slide 6: Frame level QP setting problem and solution
Problem
  Occur to QP of picture in the RAS after switching POC picture
    Sequential encoding:
  QP = QPb+QPOffset1+( a*( QPb+QPOffset1)+b)+ QPOffset3
  = QPb+QPOffset1+( a*( QPb+QPOffset1)+b) + 1 (3)
    Parallel encoding:
  QP = QPb+ QPOffset3+QPOffset1+( a*( QPb+ QPOffset3+QPOffset1)+b)
  = QPb+1+QPOffset1+( a*( QPb+1+QPOffset1)+b) (4)
Solution/Modification:
  Step1: Get QPb
  Step2: Get QP’1 = QPb + QPOffset3
  Step3: Get QP’ 2 = QP’1 + QPOffset1
  Step4: Get QP’3 = QP’ 2 + QPOffset2, here QPOffset2 = a* QP’ 2+b;
  Original:
  Step1: Get QPb
  Step2: Get QP1= QPb+ QPOffset1
  Step3: Get QP2= QP1+ QPOffset2
  Step4: Get QP3= QP2+ QPOffset3.

## Slide 7: Conclusion/Suggestion
Two modifications are proposed to existing parallel encoding method and JEM/HM code respectively, to support floating point QP in parallel encoding.
It is suggested to accept these two modifications.