## Slide 1: JVET-F0021 AHG8: Subjective testing of 360º video projection/packing formats
Jill Boyce, Zhipin Deng

## Slide 2: Background
AHG 8 has the mandate: Define subjective testing methodology, in coordination with the MPEG OMAF AhG
Many projection/packing formats have been proposed for mapping omnidirectional spherical video into a rectangular format for encoding and decoding by a video codec
Projection/packing formats introduce edges and discontinuities, where physically neighboring areas in spherical representation are not neighboring in the coded projection/packing format
  Discontinuous edges at picture boundaries
  Discontinuous edges within picture
  Continuous edges of polygonal faces

## Slide 3: CMP layout for compact cube map
Compact layout packing format minimizes discontinuous edges, rotates faces

## Slide 4: Problem with static viewports
Only a small region from the 360x180 degree region is viewed
Two static viewports defined in JVET-D1030 (sequences updated in JVET-E1030) for each sequence, with size and position
Discontinuous and continuous edges occur at different locations for the different projection/packing formats
  Hard to make apples-to-apples comparisons of impact
BD-Rate values for the two static viewports vary dramatically, based on if edges occur within the viewport for particular projection/packing format

## Slide 5: PSNR variation with viewport and projection/ packing format ERP better than CMP, OHP2 for Viewport 0 of Harbor ERP worse than CMP, OHP2 for Viewport 1 of Harbor
CMP vs. ERP | PSNR_Viewport0 |  |  | PSNR_Viewport1 |  | 
 | Y | U | V | Y | U | V
Train | 12.2% | 9.2% | 7.5% | 9.2% | 12.8% | 7.5%
Skateboarding_trick | 8.9% | 4.2% | 4.1% | 26.7% | 15.4% | 15.3%
Skateboarding_in_lot | -6.8% | -8.2% | -6.4% | -14.3% | -11.6% | -2.8%
Chairlift | -20.1% | -18.9% | -18.3% | -13.0% | 3.9% | 6.3%
KiteFlite | -8.7% | -3.1% | -4.6% | -9.2% | -9.3% | -11.1%
Harbor | 7.4% | 0.2% | 4.6% | -10.1% | -5.9% | -6.5%
PoleVault | -3.5% | -9.1% | -7.0% | -1.9% | -2.4% | -4.3%
AerialCity | 2.7% | 0.4% | -0.2% | 5.4% | 4.8% | 2.4%
DrivingInCity | 6.2% | 5.5% | 7.2% | 6.2% | 5.5% | 7.6%
DrivingInCountry | -9.1% | -13.9% | -10.9% | -16.3% | -15.7% | -18.2%
Overall | -1.1% | -3.4% | -2.4% | -1.7% | -0.3% | -0.4%
OHP2 vs. ERP | PSNR_Viewport0 |  |  | PSNR_Viewport1 |  | 
 | Y | U | V | Y | U | V
Train | 25.2% | 20.5% | 26.3% | 18.9% | 26.0% | 27.4%
Skateboarding_trick | 8.4% | 2.8% | 10.9% | -0.3% | 9.2% | 8.9%
Skateboarding_in_lot | -5.3% | 1.6% | 5.0% | -6.4% | 1.0% | -0.5%
Chairlift | -7.3% | -7.9% | -1.5% | 14.3% | 30.3% | 30.2%
KiteFlite | -6.8% | 3.0% | 1.9% | -12.8% | -9.0% | -10.7%
Harbor | 13.1% | 23.1% | 24.2% | -7.6% | 14.3% | 14.4%
PoleVault | -9.8% | -8.4% | -10.1% | 4.8% | 7.4% | 7.5%
AerialCity | 10.4% | 8.8% | 8.8% | 22.8% | 20.3% | 17.4%
DrivingInCity | 14.8% | 28.2% | 22.8% | 11.6% | 19.6% | 18.2%
DrivingInCountry | -11.3% | -7.7% | -11.2% | 4.3% | 3.3% | -1.6%
Overall | 3.1% | 6.4% | 7.7% | 5.0% | 12.2% | 11.1%

## Slide 6: Dynamic viewports
JVET-E1030 defines dynamic viewports
  JVET-E0133 includes example videos demonstrating the dynamic viewports
  Previously defined static viewport center positions (two per sequence) used as center of the middle frame of the sequence
  (yaw, pitch) offset range for first & last pictures of the sequence, with linear interpolation of the viewport position for intermediate pictures of sequence
  Objective results reported as part of CTC
Preliminary CfE (in JEVT-E1002) will use dynamic viewports, with tracking paths not published in advance

## Slide 7: Proposal
4 subjective test methods proposed to be used together
Static viewport with forced discontinuous edges at picture boundary
Static viewport with forced edges
Pre-published dynamic viewports
Non pre-published dynamic viewports

## Slide 8: Method 1: Static viewports with forced discontinuous edges at picture boundary
Useful to specifically examine picture areas where discontinuous edges occur
Desirable for discontinuous edges occur at same location within a picture and viewport, rather than at different locations for the projection/packing formats
Propose to pre-rotate each sequence prior to projection/packing format mapping and encoding, so that a maximum number of discontinuous edges (including a picture boundary) for encoding the particular projection/packing format under test will occur at the center of the static viewport

## Slide 9
Harbor sequence
ERP
ERP original
Viewport 0 coded w/ QP 37
Rotated ERP
Viewport 0 coded w/ QP 37 of rotated

## Slide 10
Harbor sequence
CMP
CMP original
Rotated CMP
Viewport 0 coded w/ QP 37 of rotated

## Slide 11: Method #1 viewport comparison
Rotated ERP coded at QP37 Rotated CMP coded at Q37
Frame 19

## Slide 12: Method 2: Static viewports with forced edges
Similar to Method 1, place a vertex in the center of the static viewport
Instead of forcing discontinuous edges at the picture boundary, continuous edges can be favored
Because ERP format has no continuous edges, no pre-rotation is required, and no edges need be present in the static viewport

## Slide 13
Harbor sequence
CMP
CMP original
Method #2
Method #1
Viewport 0 coded w/ QP 37 of rotated w/Method #2

## Slide 14: Method #2 viewport comparison
Method 1 Rotated CMP coded Method 2 Rotated CMP coded
Frame 19

## Slide 15: Method #3: Pre-published dynamic viewports
Uses pre-published dynamic viewports, such as the dynamic viewports described in JVET-E1030
Proponents of a particular projection/packing format could optionally perform rotation prior to projection/packing mapping and encoding, in order to optimize the subjective viewing quality of that dynamic viewport
  JVET-E0075, JVET-E0061, and JVET-E0050 showed that applying spherical rotation prior to encoding could improve coding efficiency for some sequences
Spherical rotation can be optionally used to minimize how frequently discontinuous edges occur in the dynamic viewport, and/or where those discontinue edges occur

## Slide 16: Method #4: Non pre-published dynamic viewports
Use same bitstream generated for method #3 will be used to generate a dynamic viewport that is not known in advance by the proponents
Not possible for proponents to minimize how frequently discontinuous edges occur in the dynamic viewport, and/or where those discontinue edges occur within the viewport
Will still be possible to avoid placing discontinuous edges at locations in the video picture where seams would be particularly noticeable because of the type of content at those locations.

## Slide 17: Dynamic Viewport example from JVET-E0133

## Slide 18: Discussion
Method #1“Static viewports with forced discontinuous edges at picture boundary,” aims at enabling viewing of “worst case” projection/packing format mapping
Method #2 “Static viewports with forced edges” avoids discontinuous edges on the picture boundary.
Method #3 “Pre-published dynamic viewports,” aims at enabling viewing a dynamic viewport of a “best case” projection/packing format mapping for the content and viewing conditions
Method #4 “Non pre-published dynamic viewports” aims at enabling viewing a “typical case” projection/packing format mapping.
For methods #1 and #2, a separate encoding must be performed for each selected static viewport position
For methods #3 and #4 can use a single encoding, e.g. a single bitstream for each QP point tested

## Slide 19: Conclusion
Goal to kickoff discussion of subjective testing methods for 360 video
Propose combination of static viewports with pre-rotation, and dynamic viewports to overcome shortcomings of static viewport testing
Consideration of which vertex and which discontinuous and/or continuous edges to rotated into the viewport may require additional thought
  Are both Methods #1 and #2 necessary? How to properly define to apply to variety of projection/packing formats?