## Slide 1
JVET-F0036
Rotated Sphere Projection (RSP) for 360 Video

## Slide 2
Some Example Projections

## Slide 3
Desirable Qualities in Projections
Low Surface area compared to sphere:
  ISP and SSP get very close to sphere and need 25% fewer pixels than ERP.
  Allows one to pack almost 5K resolution under similar level constraints.
  In contrast, CMP lies farther than sphere, thus needs 22% more pixels than ERP.
Number of faces and face arrangement:
  Projection with fewer faces e.g. SSP get better coding performance.
  Coding tools suffer on projections with more discontinuities e.g. ISP and OHP.
  With more faces, pixels have to be devoted to padding regions, compromising resolution.
Aspect ratio that is closer to 16:9, so that:
  Most already deployed hardware codecs are optimized to handle 3840x2160 resolution.
  For better compatibility with these codecs, desirable to have a projection that has 16:9 aspect ratio.
  Aligns 360 and non-360 development for a future codec.

## Slide 4
Aspect Ratio
For instance, SSP has a wide 6:1 aspect ratio, which has challenges:
  Larger than 4K line buffer requirement.
  One cannot appreciate resolution of content in native projection format.
  Parallel processing tools, e.g. slices get thinner and as a result become inefficient (especially for already deployed codecs)
Suggestion to rotate SSP by 90° and encode the image in 1:6 aspect ratio:
  Even harder to appreciate resolution of content in native projection format
  Most coding tools are being designed for more horizontal than vertical motion.
  Codec pipeline (which was designed for 4K line buffers) may be sub-optimally used as the picture gets taller.

## Slide 5
RSP Explanation
Only 2 faces, arranged in two rows.
The top face is obtained by directly cropping middle 270°x90° from ERP.
For bottom face, rotate ERP such that back side is brought to front and top/bottom are brought to equator.
Top Face
Bottom Face

## Slide 6
RSP Explanation - 2
Stack cropped faces in two rows like CMP
Corners can be greyed out because of overlap
Tennis ball seam line on sphere

## Slide 7
RSP vs CMP
RSP
CMP
Corners can be made inactive to get better coding efficiency and decoder complexity
No continuous edges
Closer to sphere

## Slide 8
Mathematical Formulation
Top face is directly cropped from ERP, so it is mathematically same as ERP
For the bottom face, perform spherical rotation:
  180° rotation along Y-axis (to bring back side to the front)
  90° along X-axis (to bring polar data to equator).
The X’, Y’ and Z’ coordinates on sphere after performing rotation are defined below:
          X’ = –X
          Y’ = –Z
          Z’ = –Y

## Slide 9
RSP Testing Methodology
RSP has been implemented in 360Lib-2.1
Simulations with HM-16.15-360Lib-2.1 using RA configuration
All test conditions same as CTC (JVET-E1030)
RSP face sizes are chosen to have same number of active pixels as ERP:
  1216x1216 for 8K (frame resolution: 3648x2432)
  1008x1008 for 4K (frame resolution: 3024x2016

## Slide 10
Coding Performance Results
Average results for all projections relative to ERP
Average RSP results for all sequences relative to ERP

## Slide 11
Conclusions
RSP:
  Has 3:2 aspect ratio (closer to 16:9 like CMP)
  Gets closer to sphere with 25% fewer pixels needed than ERP
  Two symmetric and continuous faces
  Simple mathematical representation that is based on ERP
Equal area approach on RSP could achieve further coding gains
Thanks to experts from InterDigital to cross-check results in JVET-F0085
Suggestion for inclusion in 360Lib

## Slide 12
Thank You