## Slide 1: JVET-F0083 AHG8: Subjective test pilot study of 360º video projection/packing formats
Zhipin Deng, Lidong Xu, Jill Boyce

## Slide 2: Background
A mini subjective test pilot study of the pre-rotated related methods in F0021
  Method 1: Static viewport with forced discontinuous edges at picture boundary
  Method 2: Static viewport with forced discontinuous edges within the picture
In our subjective test results, seam artifacts were observed in the decoded viewport for both Method 1 and Method 2, and the artifacts were in different extent across different projection formats.

## Slide 3: Testing procedure
Pre-rotate each sequence prior to projection/packing format mapping and encoding, in order to let discontinuous edges in the static viewport.
After lossy encoding, especially with high QP encoding, the compression distortion would make the discontinuous edges visible in the decoded static viewport.

## Slide 4: Testing procedure – how to select the rotation parameters?
Target positions of Method 1 (at the picture boundary) and Method 2 (within the picture)

## Slide 5: Testing procedure

## Slide 6: Subjective quality of the decoded viewport
Test conditions
  4 test sequences in CfE
  2 static viewports in CTC
  5 projection/packing formats including ERP, CMP, ISP, OHP, and SSP
  2 methods of pre-rotation using 360lib software
  encoded at QP37 with HM encoder
80 bitstreams generated
  Visual check of all 80 decoded viewports
2 test sessions
  1 test session for viewport 1 was done
3 viewing subjects hired

## Slide 7: Subjective quality of the decoded viewport
Some example videos

## Slide 8: Subjective quality of the decoded viewport 1

## Slide 9: MOS not well correlated with the PSNR
Chart: Decoded viewport 1 (average all sequences)
| 2.75 | 3.75 | 4.5 | 2.75 | 1.25 | 1.75 | 3.5 | 5 | 1 | 1.25
 | 37.3141 | 35.1706 | 36.2613 | 36.9252 | 37.5024 | 36.0626 | 35.509 | 35.843 | 37.9744 | 37.2645
Chart: Decoded viewport 1 (axis-x MOS, axis-y PSNR)
| 2 | 4 | 4 | 1 | 1 | 3 | 3 | 5 | 1 | 1
ChairLift | 36.26 | 34.99 | 36.1 | 37.96 | 37.75 | 35.82 | 35.15 | 37.76 | 38.06 | 37.6
Harbor | 38.492 | 35.2469 | 38.8236 | 37.3699 | 41.456 | 38.2687 | 38.5448 | 35.5775 | 42.7516 | 38.3869
KiteFlite | 38.6746 | 33.6021 | 35.1122 | 36.0328 | 34.4811 | 34.9514 | 34.8795 | 35.8067 | 34.5905 | 36.9635
SkateboardInLot | 35.8298 | 36.8434 | 35.0095 | 36.3381 | 36.3225 | 35.2103 | 33.4618 | 34.2279 | 36.4957 | 36.1075

## Slide 10: Conclusions
It is worth to include the proposed pre-rotation based methods into the subjective quality evaluation procedure for 360º video coding.
The proposed methods could also be used for the quality assessment of those techniques that would possibly be developed to alleviate or eliminate those seam artifacts.