## Slide 1: Samsung's CfE response (SDR)
E.Alshina, K.Choi

## Slide 2: Motivation
Contribution is not identical to the prepared for CfP
Our goal for CfP:
  Less than 20 tools
  One tools per on functionality
  Clean & HW/SW friendly design
  Outperform JEM
We use CfE response for
  demonstration the goal is achievable
  illustration of design principles we follow preparing CfP response

## Slide 3: Illustration for design principles
Avoid tools with minor gain
  We entirely disabled “Intra boundary filter” and “adaptive clipping”. Nothing against namely those technologies but apparently loses are minimal if we disable them.
Keep in mind realistic use case
  Initialization from previous frame requires overhead per slice. In real life slice size is much smaller than 4K picture. Also storage context state from previous frame requires memory, decision about which context update from previous frame requires additional encoder logic. In order to restore performance drop due to disabling "initialization from previous frame" we modified "multi hypothesis CABAC probability update" to the form we originally proposed it in 2011 (Torino meeting, JCTVC-F254).
Make design HW and SW implementation friendlier
  BIO in EE2 is applied for 4x4 clusters, and so amount of division operations has been reduced by factor 1/16. We support this direction, but did clustering on a different from EE2 way.
Avoid overlapping functionality
  Instead of ARSS, PDPC and 4taps Intra we use one generic design for Intra. AVS2 Intra design (reference sample smoothing is merged with Intra interpolation) is good example. This part is not very mature for now, we still working on tuning and reducing memory usage, but instead of mentioned 3 Intra tools we use one.

## Slide 4: JEM tool on/off tests
Chart: JEM6.0 tools
| QTBT&LB | 4T-INTRA | 67-INTRA | AC | AFFINE | ALF | ATMVP | BIO | BLF | DMVR | EMT | FRUC | IBF | LIC | IMV | INIT_PREV | LM-CHROMA | MCABAC | MV16 | NSST | OBMC | PDPC | ARSS | COEFF-COD
Tool-on | 0.067 | 0.003 | 0.008 | 0.001 | 0.027 | 0.058 | 0.015 | 0.023 | 0.004 | 0.026 | 0.03 | 0.061 | 0.001 | 0.011 | 0.022 | 0.001 | 0.028 | 0.004 | 0.001 | 0.025 | 0.009 | 0.006 | 0.002 | 0.008










Tool -off | 0.078749 | 0.001001 | 0.0070493 | 0.002004 | 0.012146 | 0.05042 | 0.0050251 | 0.011122 | 0.0050251 | 0.003009 | 0.025641 | 0.038422 | 0.001001 | 0.01833 | 0.010101 | 0.0050251 | 0.017294 | 0.0080645 | 0.014199 | 0.017294 | 0.010101 | 0.0050251 | 0.001001 | 0.0050251
SPIE2017, Complexity and performance tradeoff for next generation video coding standard development

## Slide 5: JEM6.0 Performance & run-time
Resolution | Seq. | BD-rate |  | 
 |  | Y | U | V
4K | CrossWalk1 | -37.9% | -43.9% | -47.6%
 | FoodMarket3 | -34.9% | -46.5% | -48.9%
 | Tango1 | -36.4% | -55.0% | -49.5%
 | CatRobot1 | -40.2% | -52.4% | -45.5%
 | DaylightRoad1 | -40.7% | -53.5% | -38.1%
 | BuildingHall1 | -33.3% | -41.4% | -46.5%
 | ParkRunning2 | -31.6% | -26.2% | -29.3%
 | CampfireParty | -37.9% | -35.7% | -56.6%
2K | BQTerrace | -30.4% | -50.5% | -61.2%
 | RitualDance | -27.8% | -37.9% | -41.7%
 | TimeLapse | -26.8% | -61.3% | -67.1%
 | BasketballDrive | -32.1% | -46.9% | -43.3%
 | Cactus | -36.0% | -49.1% | -45.1%
4K All |  | -36.6% | -44.3% | -45.2%
2K All |  | -30.6% | -49.1% | -51.7%
All |  | -34.3% | -46.2% | -47.7%
Decoder  ~  10 compared to HM
Encoder   12 compared to HM

## Slide 6: CfE response performance & run-time
Resolution | Seq. | BD-rate |  | 
 |  | Y | U | V
4K | CrossWalk1 | -38.8% | -34.5% | -38.8%
 | FoodMarket3 | -35.9% | -42.3% | -44.8%
 | Tango1 | -37.6% | -49.4% | -43.9%
 | CatRobot1 | -41.6% | -53.6% | -45.5%
 | DaylightRoad1 | -42.2% | -51.5% | -33.8%
 | BuildingHall1 | -35.1% | -39.4% | -45.5%
 | ParkRunning2 | -35.3% | -20.6% | -24.1%
 | CampfireParty | -43.4% | -33.2% | -58.4%
2K | BQTerrace | -31.9% | -42.5% | -54.3%
 | RitualDance | -28.7% | -34.3% | -37.9%
 | TimeLapse | -29.2% | -61.8% | -65.7%
 | BasketballDrive | -33.7% | -43.6% | -39.1%
 | Cactus | -37.3% | -44.5% | -40.4%
4K All |  | -38.8% | -40.6% | -41.8%
2K All |  | -32.2% | -45.3% | -47.5%
All |  | -36.2% | -42.4% | -44.0%
Decoder  faster than JEM
Encoder  slower than JEM, but acceptable
(bit-rate matching took ~1 week)

## Slide 7: Initialization from previous frame
Storage for ctx
Signaling (per slice)
  Flag  use /not use drop
  Number of ctx initialized from previous frame
  Map form previous / HEVC-like
  JCTVC-F254 Multi-parameter probability up-date for CABAC
  P0 = (Y>>4) + P0 – (P0>>4)
  P1 = (Y>>7) + P1 – (P0>>7)
  counter++;
  P = (counter<Th)?P0:(P0 + P1+1)>>1 gain

## Slide 8: Intra reference filter in JEM6.0
Chart: 
{1,2,1}/4
{1,4,6,4,1}/16
{ 1, 6, 15, 20, 15, 6, 1 }/64,
{ 3, 7, 14, 16, 14, 7, 3 }/64,
{ 4, 9, 12, 14, 12, 9, 4 }/64,
{2,3,6,3,2}/16

## Slide 9: AVS-like Ref smoothing with Intra interpolation
Reference filter {1,2,1}/4 + Bi-linear interpolation {k, 32-k}/32
r0 r1 r2 r3 r4 r5 r6 r7
s0 s1 s2 s3 s4 s5 s6 s7
p=(k*s2+(32-k)*s3+16)>>5
r0 r1 r2 r3 r4 r5 r6 r7
4s0 4s1 4s2 4s3 4s4 4s5 4s6 4s7
p=(k*4s2+(32-k)*4s3+64)>>7
p=(k*(r1+2r2+r3)+(32-k)*(r2+2r3+r4)+64)>>7
{k,2*k+(32-k), k+2*(32-k), (32-k)}/128
{k,32+k, 64-k, 32-k}/128
r1+2r2+r3 r2+2r3+r4

## Slide 10: PCS 2016 BIO
Clustering samples
11
2 divisions per sample
22
divisions per sample
LL
divisions per sample
MV refinement granularity depending on block size
L =Max(Min (W, H)/8,2).
88 , 1632  L = 2; 3232  L = 4; 6464  L = 8; 128128  L = 16
25% 6.3% 1.6% 0.4%