## Slide 1: Additional EE1 Tests (Test 2.1 and Test 10.1) (JVET-G0080) K. Panusopone, S. Hong, Y. Yu, and L. Wang

## Slide 2: PDPC-L Feature
CU size constraint
  PDPC off when CU size is smaller than a threshold
  Threshold set to 64 in EE1 Test3
Number of non-zero coefficient constraint
  PDPC off when number of non-zero coefficient is less than or equal to a threshold
  Threshold set to 1 in EE1 Test3
PDPC flag signaled after coefficient coding
Coding performance improvement reported

## Slide 3: PDPC-L Implementation
JEM-6.0 style mode decision
  2 independent loops; one for PDPC off and another for PDPC on
  Only modify PDPC on loop
  Support ARSS, only with explicit ARSS flag signaling
New macros
  F0054_PDPCL sets to enable PDPC-L option
  MIN_PDPC_COEFF_THRESHOLD sets number of non-zero coefficient threshold (default value is set to 1)
  SECOND_RD_COEFF_CHECK sets to enable second RD mode decision for PDPC off block with number of non-zero coefficient less than a threshold (default value is set to 1)
  MIN_PDPC_BLOCK_THRESHOLD sets block size threshold (default value is set to 32)

## Slide 4: Test 2.1
Based on HM-16.6-JEM-6.0-EE1-Test1-2and10
  Add PDPC-L to Test 2 features
  UWP+UW66, PDPC for other modes, PDPC-L, ARSS off
 | Over JEM 6.0 |  |  |  |  | Over EE1 Test 2 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.04% | -0.04% | -0.08% | 68% | 98% | -0.05% | -0.01% | -0.03% | 101% | 99%
Class A2 | 0.15% | 0.40% | 0.20% | 69% | 98% | -0.07% | 0.03% | -0.07% | 102% | 100%
Class B | 0.16% | 0.23% | 0.23% | 66% | 98% | -0.07% | -0.08% | -0.12% | 101% | 100%
Class C | 0.18% | 0.33% | 0.34% | 64% | 99% | -0.09% | -0.11% | -0.09% | 99% | 99%
Class D | 0.00% | 0.18% | 0.23% | 65% | 99% | -0.10% | -0.01% | 0.03% | 100% | 99%
Class E | 0.08% | 0.32% | 0.28% | 66% | 98% | -0.08% | 0.11% | -0.11% | 101% | 99%
Overall (Ref) | 0.10% | 0.21% | 0.20% | 66% | 98% | -0.08% | -0.02% | -0.06% | 101% | 99%
Class F (optional) | 0.12% | 0.21% | 0.54% | 66% | 100% | -0.01% | -0.04% | 0.12% | 100% | 100%

## Slide 5: Test 10.1
Based on HM-16.6-JEM-6.0-EE1-Test1-2and10
  Add PDPC-L to Test 10 features
  UWP+UW66, PDPC on for other modes, PDPC-L, ARSS constrained as in F0024 but explicit signaling as in F0055
 | Over JEM 6.0 |  |  |  |  | Over EE1 Test 10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT- | DecT
Class A1 | -0.21% | -0.41% | -0.28% | 81% | 100% | -0.04% | -0.03% | -0.05% | 101% | 101%
Class A2 | -0.13% | 0.26% | 0.08% | 82% | 100% | -0.06% | 0.01% | 0.02% | 100% | 100%
Class B | -0.10% | 0.04% | 0.08% | 79% | 100% | -0.06% | -0.03% | -0.07% | 100% | 100%
Class C | -0.12% | 0.11% | 0.09% | 79% | 100% | -0.10% | -0.03% | 0.09% | 100% | 99%
Class D | -0.10% | 0.10% | 0.21% | 78% | 100% | -0.06% | -0.05% | 0.16% | 100% | 100%
Class E | -0.13% | 0.19% | 0.28% | 80% | 100% | -0.06% | -0.07% | 0.04% | 101% | 99%
Overall (Ref) | -0.13% | 0.04% | 0.07% | 80% | 100% | -0.06% | -0.03% | 0.03% | 100% | 100%
Class F (optional) | 0.02% | 0.05% | 0.38% | 79% | 100% | 0.04% | 0.13% | -0.04% | 100% | 99%

## Slide 6: Conclusions
PDPC-L can be implemented without major changes
  No change to NSST, Reference Smoothing
  Maintain 2 loops as in JEM-6.0 mode decision; one for PDPC off and another for PDPC on
  Provide support for ARSS
  Same parsing mechanism
UWP and W66 works well with PDPC-L
  PDPC-L feature provides coding gains with UWP and W66, with little impact on processing time

## Slide 7
Thanks LGE and Sharp (G0091) for cross-checking
Questions?