## Slide 1
JVET-L0121
CE7-related: Support of quantization matrices
T. Toma, K. Abe
Panasonic Corporation

## Slide 2
2
Introduction
Propose to support quantization matrices for VVC
  HEVC based method
  Quantization matrices for a rectangular CU is created from those for a square CU
  Implemented in VTM 2.0.1

## Slide 3
3
Proposed Method
For square CU, HEVC’s quantization matrices implementation that was available in JEM is used and ported to VTM 2.0.1.
  Only modification for square CU is adding matrices for 2x2 chroma and 64x64 luma.
  2x2, 4x4, 8x8 quantization matrices are explicitly signaled. 16x16, 32x32, and 64x64 matrices are created from 8x8 matrices using nearest neighbor.
Quantization matrices for rectangular CU are created from the matrices of square CU.
  Matrices for MxN or NxM (M<N) CU is created by down-sampling from matrices of NxN CU.

## Slide 4
4
Matrices creation of a rectangular CU
INTRA8X8_LUMA =
16, 16, 16, 16, 17, 18, 21, 24,
16, 16, 16, 16, 17, 19, 22, 25,
16, 16, 17, 18, 20, 22, 25, 29,
16, 16, 18, 21, 24, 27, 31, 36,
17, 17, 20, 24, 30, 35, 41, 47,
18, 19, 22, 27, 35, 44, 54, 65,
21, 22, 25, 31, 41, 54, 70, 88,
24, 25, 29, 36, 47, 65, 88,115,
INTRA4X8_LUMA =
16, 16, 17, 21,
16, 16, 17, 22,
16, 17, 20, 25,
16, 18, 24, 31,
17, 20, 30, 41,
18, 22, 35, 54,
21, 25, 41, 70,
24, 29, 47, 88,
If width and height ratio of a CU is M, every M samples from lower frequency is selected.
  For 4x8 CU, every two columns is sampled  ½ down-sampling.

## Slide 5
5
Subjective quality improvement: Quantization matrices ON vs. OFF
Image gets sharper with enhanced low to medium frequency by quantization matrices
Benefit can be seen both for square and rectangular CU
Original
ON
OFF
QP37
QP37
Custom matrices from JCTVC-F362 are used

## Slide 6
6
Simulation results
 | All Intra Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 1.78% | 0.49% | -1.12% | 115% | 99%
Class A2 | 1.99% | -1.37% | -1.68% | 112% | 100%
Class B | 1.34% | -1.49% | -1.83% | 115% | 100%
Class C | 2.18% | -0.35% | -0.25% | 101% | 106%
Class E | 0.42% | -0.87% | -1.05% | 117% | 101%
Overall | 1.55% | -0.78% | -1.21% | 111% | 101%
Class D | 2.24% | -0.05% | -0.46% | 99% | 118%
Class F (optional) | 1.11% | 0.40% | 0.33% | 108% | 104%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.14% | 1.79% | -0.91% | 115% | 101%
Class A2 | -0.70% | -0.74% | -1.15% | 108% | 100%
Class B | 0.34% | -1.42% | -1.93% | 112% | 102%
Class C | 1.75% | -0.37% | -0.70% | 108% | 112%
Class E |  |  |  |  | 
Overall | 0.47% | -0.36% | -1.24% | 111% | 104%
Class D | 1.88% | -0.86% | -0.51% | 105% | 134%
Class F (optional) | 1.14% | 0.75% | 0.47% | 112% | 109%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.53% | -1.57% | -2.40% | 112% | 102%
Class C | 1.85% | -0.57% | -0.83% | 107% | 111%
Class E | 0.59% | -0.32% | -1.01% | 114% | 110%
Overall | 0.99% | -0.92% | -1.53% | 111% | 107%
Class D | 1.94% | -0.47% | -1.05% | 104% | 137%
Class F (optional) | 1.13% | 0.77% | 0.42% | 111% | 111%
 | All Intra Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.68% | -0.98% | -0.55% | 115% | 99%
Class A2 | -0.68% | -1.87% | -1.89% | 112% | 100%
Class B | -0.91% | -1.63% | -1.56% | 115% | 100%
Class C | -0.77% | -1.00% | -0.81% | 101% | 106%
Class E | -0.75% | -1.00% | -1.07% | 117% | 101%
Overall | -0.78% | -1.32% | -1.20% | 111% | 101%
Class D | -0.28% | -0.65% | -1.04% | 99% | 118%
Class F (optional) | -0.21% | -0.35% | -0.15% | 108% | 104%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.94% | -0.54% | -0.98% | 115% | 101%
Class A2 | -1.62% | -1.92% | -1.87% | 108% | 100%
Class B | -1.33% | -1.76% | -1.73% | 112% | 102%
Class C | -0.51% | -0.41% | -0.70% | 108% | 112%
Class E |  |  |  |  | 
Overall | -1.09% | -1.19% | -1.33% | 111% | 104%
Class D | -0.18% | -1.27% | -0.97% | 105% | 134%
Class F (optional) | -0.07% | 0.28% | -0.02% | 112% | 109%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -1.21% | -1.56% | -2.66% | 112% | 102%
Class C | -1.06% | -1.16% | -1.38% | 107% | 111%
Class E | -0.10% | 0.37% | 0.29% | 114% | 110%
Overall | -0.88% | -0.94% | -1.50% | 111% | 107%
Class D | -0.78% | -0.57% | -0.30% | 104% | 137%
Class F (optional) | -0.65% | -0.16% | -0.27% | 111% | 111%
BD-rate loss is 0.47% for RA
Additional results of MS-SSIM shows better gain
PSNR
MS-SSIM
Default matrices that are the same as HEVC for square CU are used

## Slide 7
7
Conclusions
Quantization matrices based on HEVC’s design is proposed with extension to support rectangular CU.
Matrices for rectangular CU is created from those for square CU.
Subjective quality improvement both for square and rectangular block
 Propose to adopt quantization matrices based on this design in VTM

## Slide 8
8
Thank Sony for cross-checking this proposal !