## Slide 1
CE6-related:
Shape adaptive transform selection
JVET-L0134

## Slide 2: Shape adaptive transform selection
Proposal:
  Select horizontal and vertical transforms based on shape of the block
    Use DST-7 for the shorter dimension
    Use DCT-2 for the longer dimension or if block is square
Applied for intra blocks if MTS flag is off (or if MTS is disabled)
  That is, when DCT-2 / DCT-2 is currently used
Using the existing VTM-2 transforms
  Switching to DST-7 if a transform between 4 and 32 points can be used
JVET-L0134

## Slide 3: Shape adaptive transform selection
JVET-L0134
MTS_CU_flag | MTS_Hor_flag | MTS_Ver_flag | Intra |  | Inter | 
 |  |  | Horizontal | Vertical | Horizontal | Vertical
0 |  |  | DST7 if width < height, else DCT2 | DST7 if height < width, else DCT2 | DCT2 | 
1 | 0 | 0 | DST7 | DST7 | DCT8 | DCT8
 | 0 | 1 | DCT8 | DST7 | DST7 | DCT8
 | 1 | 0 | DST7 | DCT8 | DCT8 | DST7
 | 1 | 1 | DCT8 | DCT8 | DST7 | DST7

## Slide 4: Summary of results
JVET-L0134
 | MTS: | Off | Off | On | On
 | Tool in: | All slices | I-slices | All slices | I-slices
 | Y | -1.17 % | -1.17 % | -0.13 % | -0.13 %
 | U | -0.62 % | -0.62 % | 0.72 % | 0.72 %
AI | V | -0.65 % | -0.65 % | 0.75 % | 0.75 %
 | Enc | 106 % | 106 % | 99 % | 99 %
 | Dec | 101 % | 101 % | 99 % | 99 %
 | Y | -0.47 % | -0.26 % | -0.01 % | -0.01 %
 | U | 0.45 % | 0.13 % | 0.77 % | 0.30 %
RA | V | 0.39 % | 0.04 % | 0.83 % | 0.30 %
 | Enc | 102 % | 101 % | 100 % | 100 %
 | Dec | 103 % | 101 % | 98 % | 97 %
 | Y | -0.09 % | -0.01 % | -0.01 % | 0.00 %
 | U | 0.50 % | 0.31 % | 0.57 % | 0.24 %
LB | V | 0.40 % | 0.26 % | 0.63 % | 0.33 %
 | Enc | 100 % | 100 % | 100 % | 99 %
 | Dec | 102 % | 100 % | 97 % | 95 %

## Slide 5: Shape adaptive transform selection
Summary:
  Very simple switching rule between DCT-2 and DST-7
  Nice coding efficiency, especially for practical encoders without the need to check additional transform modes
    -1.17 % AI / -0.47 % RA bitrate impact when MTS is off
JVET-L0134

## Slide 6
Detailed results

## Slide 7: Results (MTS off)
JVET-L0134
 | All Intra Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.43 % | -0.47 % | -0.66 % | 110 % | 104 %
Class A2 | -1.15 % | -0.73 % | -0.91 % | 110 % | 101 %
Class B | -1.16 % | -0.73 % | -0.65 % | 104 % | 100 %
Class C | -0.80 % | -0.39 % | -0.21 % | 104 % | 102 %
Class E | -1.45 % | -0.76 % | -0.93 % | 103 % | 99 %
Overall | -1.17 % | -0.62 % | -0.65 % | 106 % | 101 %
Class D | -0.64 % | -0.19 % | -0.09 % | 103 % | 103 %
Class F | -0.51 % | -0.33 % | -0.47 % | 104 % | 104 %

## Slide 8: Results (MTS off, tool used in all slices)
JVET-L0134
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.50 % | 0.90 % | 0.65 % | 101 % | 101 %
Class A2 | -0.36 % | 0.59 % | 0.13 % | 103 % | 100 %
Class B | -0.54 % | 0.22 % | 0.47 % | 102 % | 101 %
Class C | -0.45 % | 0.29 % | 0.28 % | 101 % | 110 %
Class E |  |  |  |  | 
Overall | -0.47 % | 0.45 % | 0.39 % | 102 % | 103 %
Class D | -0.31 % | 0.28 % | 0.06 % | 101 % | 104 %
Class F (optional) | -0.27 % | 0.07 % | 0.03 % | 100 % | 105 %
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.18 % | 0.20 % | -0.19 % | 101 % | 102 %
Class C | -0.12 % | -0.10 % | -0.09 % | 99 % | 100 %
Class E | 0.09 % | 1.81 % | 2.05 % | 99 % | 104 %
Overall | -0.09 % | 0.50 % | 0.40 % | 100 % | 102 %
Class D | -0.04 % | 0.56 % | 0.99 % | 100 % | 97 %
Class F (optional) | -0.02 % | 0.14 % | 0.46 % | 98 % | 100 %

## Slide 9: Results (MTS off, tool used in I-slices)
JVET-L0134
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.30 % | 0.19 % | 0.02 % | 101 % | 98 %
Class A2 | -0.26 % | 0.29 % | -0.05 % | 101 % | 98 %
Class B | -0.24 % | 0.01 % | 0.13 % | 101 % | 100 %
Class C | -0.24 % | 0.11 % | 0.02 % | 102 % | 108 %
Class E |  |  |  |  | 
Overall | -0.26 % | 0.13 % | 0.04 % | 101 % | 101 %
Class D | -0.18 % | 0.11 % | -0.06 % | 102 % | 101 %
Class F | -0.15 % | -0.08 % | -0.13 % | 102 % | 105 %
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.06 % | 0.03 % | -0.26 % | 101 % | 100 %
Class C | 0.01 % | -0.13 % | -0.17 % | 99 % | 98 %
Class E | 0.04 % | 1.36 % | 1.69 % | 100 % | 103 %
Overall | -0.01 % | 0.31 % | 0.26 % | 100 % | 100 %
Class D | 0.02 % | 0.12 % | 0.04 % | 100 % | 99 %
Class F | -0.13 % | -0.18 % | 0.34 % | 98 % | 100 %

## Slide 10: Results (MTS on)
JVET-L0134
 | All Intra Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.23 % | 1.05 % | 0.80 % | 100 % | 95 %
Class A2 | -0.14 % | 0.58 % | 0.37 % | 101 % | 98 %
Class B | -0.10 % | 0.62 % | 0.82 % | 95 % | 100 %
Class C | -0.06 % | 0.48 % | 0.81 % | 100 % | 99 %
Class E | -0.14 % | 1.00 % | 0.87 % | 99 % | 103 %
Overall | -0.13 % | 0.72 % | 0.75 % | 99 % | 99 %
Class D | -0.07 % | 0.61 % | 0.56 % | 99 % | 104 %
Class F | 0.08 % | 0.29 % | 0.30 % | 100 % | 101 %

## Slide 11: Results (MTS on, tool used in all slices)
JVET-L0134
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.07 % | 1.09 % | 1.07 % | 99 % | 96 %
Class A2 | 0.00 % | 0.90 % | 0.45 % | 99 % | 102 %
Class B | 0.00 % | 0.60 % | 0.99 % | 101 % | 98 %
Class C | 0.01 % | 0.65 % | 0.72 % | 101 % | 96 %
Class E |  |  |  |  | 
Overall | -0.01 % | 0.77 % | 0.83 % | 100 % | 98 %
Class D | 0.02 % | 0.39 % | 0.60 % | 100 % | 97 %
Class F (optional) | 0.07 % | 0.56 % | 0.53 % | 101 % | 95 %
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.05 % | 0.37 % | 0.81 % | 100 % | 93 %
Class C | 0.08 % | 0.20 % | 0.13 % | 100 % | 98 %
Class E | -0.23 % | 1.42 % | 0.99 % | 101 % | 103 %
Overall | -0.01 % | 0.57 % | 0.63 % | 100 % | 97 %
Class D | 0.01 % | 0.90 % | 0.54 % | 100 % | 100 %
Class F (optional) | 0.13 % | 0.82 % | 0.31 % | 99 % | 99 %

## Slide 12: Results (MTS on, tool used in I-slices)
JVET-L0134
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.06 % | 0.37 % | 0.21 % | 99 % | 94 %
Class A2 | -0.02 % | 0.39 % | 0.16 % | 100 % | 99 %
Class B | 0.01 % | 0.23 % | 0.43 % | 101 % | 97 %
Class C | 0.00 % | 0.25 % | 0.33 % | 100 % | 99 %
Class E |  |  |  |  | 
Overall | -0.01 % | 0.30 % | 0.30 % | 100 % | 97 %
Class D | 0.00 % | 0.14 % | 0.30 % | 100 % | 99 %
Class F | 0.04 % | 0.31 % | 0.30 % | 100 % | 99 %
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.03 % | 0.02 % | 0.25 % | 99 % | 89 %
Class C | 0.05 % | 0.03 % | -0.09 % | 100 % | 97 %
Class E | -0.09 % | 0.90 % | 1.01 % | 99 % | 104 %
Overall | 0.00 % | 0.24 % | 0.33 % | 99 % | 95 %
Class D | 0.01 % | 0.40 % | 0.23 % | 100 % | 94 %
Class F | -0.08 % | 0.61 % | 0.11 % | 99 % | 98 %