## Slide 1: JVET-L0158 CE4-related: History-Based Motion Vector Prediction considering parallel processing
N. Park, H. Jang, J. Nam, J. Lee, J. Lim, S. Kim

## Slide 2: Introduction
Problem on current HMVP
  HMVP buffer is initialized based on slice.
  It causes the dependency between CTU rows
 |  |  |  |  |  |  | X |  | 
 |  |  |  |  | X |  |  |  | 
 |  |  | X |  |  |  |  |  | 
 | X |  |  |  |  |  |  |  | 
Thread1
Thread2
Thread3
Thread4
Thread1
Thread2
Data dependency
Blocks being encoded/decoded
X
New data dependency caused by HMVP

## Slide 3: Proposed methods
Two schemes are proposed to resolve the dependency problem caused by HMVP
  Test #1 : Initialize the HMVP buffer on CTU row bases
  Test #2 : Initialize the HMVP buffer on CTU bases
 |  |  |  |  |  |  | X |  | 
 |  |  |  |  | X |  |  |  | 
 |  |  | X |  |  |  |  |  | 
 | X |  |  |  |  |  |  |  | 
Thread1
Thread2
Thread3
Thread4
Thread1
Thread2
Data dependency
Blocks being encoded/decoded
X
HMVP Buffer Initialization Position
…
[Proposed Test #1 scheme]
 |  |  |  |  |  |  | X |  | 
 |  |  |  |  | X |  |  |  | 
 |  |  | X |  |  |  |  |  | 
 | X |  |  |  |  |  |  |  | 
Thread1
Thread2
Thread3
Thread4
Thread1
Thread2
Data dependency
Blocks being encoded/decoded
X
…
[Proposed Test #2 scheme]
…

## Slide 4: Experimental results
Anchor : JVET-L0226 (CE4.4.7a : on MERGE)
  Test #1 : Initialize the HMVP buffer on CTU row bases
  Test #2 : Initialize the HMVP buffer on CTU bases

## Slide 5: Experimental results
Anchor : JVET-L0226 (CE4.4.7c : on MERGE & AMVP)
  Test #1 : Initialize the HMVP buffer on CTU row bases
  Test #2 : Initialize the HMVP buffer on CTU bases

## Slide 6: Conclusion
In this proposal, two solutions are proposed to support compatibility with parallel processing implementation algorithms.
  Test #1 : Initialize the HMVP buffer on CTU Row basis
  Test #2 : Initialize the HMVP buffer on CTU basis
Simulation results show the marginal coding loss on HMVP
Recommended to consider this method for next VTM.
Thanks to Sharp for crosscheck (JVET-K0525)

## Slide 7
Thank you