## Slide 1
More Than Just Cloud
Alibaba Cloud
AHG11 & CE1-related: Luma 2xN and Nx2 Block Partitions Support
Jicheng An, Yu-Chen Sun, Jian Lou

## Slide 2: Luma 2xN and Nx2 CB Support
More Than Just Cloud
Luma 2xN and Nx2 CB are proposed under the current QTBTT block partitioning structure by setting the luma minMtSize down to 2 luma samples for I slice.
Very good results for screen content video !
Thanks Qualcomm for crosscheck!

## Slide 3: Luma 2xN and Nx2 CB Support
More Than Just Cloud
In order to support the 2xN and Nx2 luma CB, some changes are made straightforwardly as follows:
  The mode storage unit is modified to 2x2 sample level instead of 4x4 (software change);
  For the transform of 2xN (and Nx2) luma CB, only DCT2 is used, the DST7, and DCT8 are not supported;
  For the deblocking of luma 2-sample edge, the filtering decision and filtering operations are all changed to 2-line processing instead of 4-line processing.

## Slide 4: For P and B slices
More Than Just Cloud
If the luma CB length is set to 2 samples then the corresponding chroma CB length should be 1 sample for the 4:2:0 sample format.
We have another proposal JVET-L0184 which can separate the luma and chroma partitioning tree in all kinds of slices under arbitrary block size.
Therefore, we may have above two directions for inter slice.

## Slide 5
More Than Just Cloud
A TEAM OF EXPERTS
6000+ Top Technology Experts Based in Hangzhou, Beijing, Silicon Valley and Seattle.
MISSION
为了无法计算的价值
More Than Just Cloud
VISION
成为全球云数据大计算的领导者
Pioneer of Cloud Data and Big Computing
Alibaba Cloud
Thank you for your attention !