## Slide 1: Non-CE4: Parallel Merge for VTM
Semih Esenlik, Han Gao, Biao Wang, Anand Meher Kotra, Jianle Chen

## Slide 2: Parallel Merge in HEVC
Reference: High Efficiency Video Coding (HEVC), Algorithms and Architectures, Vivienne Sze, Madhukar Budagavi, Gary J. Sullivan
B
E
A
C
D
F
G
32
32
Merge Estimation Region with 32x32 size is shown.
Merge estimation for blocks A, B, C and D can be done in parallel.
For Block D  A, B and C are set unavailable for prediction during merge list construction.

## Slide 3: Status of Parallel Merge in VVC
Parallel merge estimation implementation in VTM2.0 is copied from HEVC.
  Implementation in VTM: If top-left coordinates of two PUs are in the same MER, MV prediction is disabled for merge.
Text not present in VVC draft text.
Problems
  Due to coding order parallel processing is not guaranteed.
  ATMVP blocks are not considered as whole CU.

## Slide 4: Problem example 1
B
E
A
Processing order ABCDEF
Problem: Block A should be marked either available or unavailable for both candidate positions of B (left and left bottom)
Question: should it be possible to process A and D in parallel?
F
C
D

## Slide 5: Problem example 2
C
E
A
Processing order ABCDE.
In this example nothing can be processed in parallel.
Although A and C are in the same MER, they cannot be processed in parallel due to coding order, although merge candidate is set unavailable.
Same is true for B and D.
B
D

## Slide 6: Problem example 3
ATVMP CUs are composed of multiple PUs.
B
ATMVP
PU is in considered to be inside the MER, but CU is considered to be outside.

## Slide 7: Proposed Solution
Current block
MER Grid
Mer_width
Mer_heigth
Neighbor block
Proposal:
If bottom-right coordinate of a neighbor block is in Extended MER of current block, prediction between them are disabled for merge.
Extended MER of current block
Algorithm: The neighbor block is marked as unavailable for prediction if any of the conditions are satisfied;
(XNb >> N is equal to XCt >> N) AND (YNb >> N smaller than or equal to YCt >> N)
(YNb >> N is equal to YCt >> N) AND (XNb >> N smaller than or equal to XCt >> N)
(XCt , YCt):top-left coordinate of current block (CB)
(XNb , YNb): bottom-right coordinate of neighbor block (CB)
N defines the MER region

## Slide 8: Proposed Solution
Proposal guarantees that if any part two blocks are in the same MER, they can be processed in parallel.
C
E
A
B
D
B
E
A
F
C
D
A&B, A&D, C&E and D&F can be processed in parallel
A&C and B&D can be processed in parallel

## Slide 9: Proposed solution - details
Application of the proposal to affine merge mode
  The proposal is applied also to affine merge mode, which means that within a MER, coding blocks that are predicted by merge mode or affine merge mode can be estimated in parallel.
Application of the proposal to neighbor blocks with sub-pu based inter prediction
  According to the proposal, if a neighbor block is predicted with affine or ATMVP, the bottom right coordinate of the coding block is used (instead of the sub-PUs that result from further partitioning of the CB) to check neighbor block availability.
Application of the proposal to history based and long distance merge candidates
  The bottom right coordinate of the candidate in question can be used in the proposed algorithm just like spatially adjacent candidates.

## Slide 10: Simulation results
When MER size is 8x8 and 16x16
 | Random Access Main 10 |  |  |  | 
 | Over VTM2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.14% | 0.03% | 101% | 103%
Class A2 | 0.19% | 0.23% | 0.18% | 101% | 102%
Class B | 0.16% | 0.28% | 0.19% | 101% | 104%
Class C | 0.31% | 0.46% | 0.37% | 101% | 105%
Class E |  |  |  |  | 
Overall | 0.18% | 0.29% | 0.21% | 101% | 104%
Class D | 0.34% | 0.42% | 0.37% | 101% | 104%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  | 
 | Over VTM2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.14% | 0.23% | 0.25% | 100% | 105%
Class C | 0.33% | -0.02% | 0.10% | 101% | 104%
Class E | -0.13% | 0.44% | -0.35% | 101% | 109%
Overall | 0.13% | 0.20% | 0.05% | 101% | 106%
Class D | 0.31% | 0.66% | 0.22% | 101% | 106%
Class F (optional) | 0.61% | 0.95% | 0.94% | 101% | 108%
Table 1: Proposal with 8x8 MER
 | Random Access Main 10 |  |  |  | 
 | Over VTM2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.16% | 0.30% | 0.32% | 102% | 102%
Class A2 | 0.55% | 0.88% | 0.93% | 103% | 102%
Class B | 0.56% | 0.63% | 0.55% | 103% | 104%
Class C | 0.91% | 1.06% | 1.08% | 103% | 104%
Class E |  |  |  |  | 
Overall | 0.57% | 0.73% | 0.72% | 103% | 103%
Class D | 0.91% | 1.03% | 0.97% | 103% | 104%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  | 
 | Over VTM2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.47% | 0.46% | 0.18% | 101% | 104%
Class C | 0.81% | 0.63% | 0.78% | 103% | 104%
Class E | -0.10% | 0.49% | 0.15% | 101% | 109%
Overall | 0.44% | 0.52% | 0.37% | 102% | 105%
Class D | 0.88% | 1.37% | 0.82% | 103% | 105%
Class F (optional) | 1.41% | 1.86% | 1.80% | 103% | 109%
Table 2: Proposal with 16x16 MER

## Slide 11: Simulation results
 | Random Access Main 10 |  |  |  | 
 | Over VTM2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.51% | 0.75% | 0.75% | 103% | 102%
Class A2 | 1.23% | 1.84% | 1.92% | 106% | 101%
Class B | 1.28% | 1.35% | 1.35% | 105% | 103%
Class C | 1.80% | 2.16% | 2.22% | 107% | 104%
Class E |  |  |  |  | 
Overall | 1.25% | 1.54% | 1.57% | 105% | 103%
Class D | 1.70% | 1.87% | 2.15% | 107% | 104%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  | 
 | Over VTM2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 1.17% | 0.94% | 0.78% | 104% | 104%
Class C | 1.73% | 1.64% | 1.92% | 105% | 102%
Class E | 0.18% | 0.15% | 0.20% | 101% | 108%
Overall | 1.11% | 0.98% | 1.02% | 103% | 104%
Class D | 1.77% | 1.86% | 1.71% | 106% | 105%
Class F (optional) | 1.90% | 2.33% | 2.25% | 104% | 108%
 | Random Access Main 10 |  |  |  | 
 | Over VTM2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 1.11% | 1.38% | 1.44% | 104% | 102%
Class A2 | 2.11% | 2.96% | 3.18% | 108% | 101%
Class B | 2.31% | 2.35% | 2.33% | 108% | 103%
Class C | 2.78% | 3.27% | 3.48% | 109% | 103%
Class E |  |  |  |  | 
Overall | 2.15% | 2.52% | 2.63% | 108% | 103%
Class D | 2.55% | 2.92% | 3.12% | 109% | 103%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  | 
 | Over VTM2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 2.16% | 1.82% | 1.78% | 106% | 104%
Class C | 2.66% | 2.46% | 2.99% | 107% | 103%
Class E | 0.76% | 0.52% | 0.56% | 103% | 109%
Overall | 1.98% | 1.71% | 1.88% | 106% | 105%
Class D | 2.76% | 3.41% | 2.78% | 108% | 104%
Class F (optional) | 2.63% | 3.32% | 3.38% | 106% | 109%
When MER size is 32x32 and 64x64
Table 3: Proposal with 32x32 MER
Table 4: Proposal with 64x64 MER

## Slide 12
Thank You
www.huawei.com