## Slide 1: CE11-related: Position dependent adaptive Tc clipping range for deblocking filter JVET-L0226
Anand Meher Kotra, Semih Esenlik, Biao Wang, Han Gao, Zhijie Zhao, Jianle Chen

## Slide 2: Prior art
Typical boundary artifact is shown in Fig. 1 below
  Maximum distortion is observed between samples p0 and q0
  Typically samples far away from the boundary tend to have less distortion
Problem
  VTM 2.0.1 strong filter uses a fixed clipping range of [P – 2tc, P + 2tc]
  Fixed clipping range does not take into account the position of the sample from the block boundary
    Therefore “over smoothing” or “blurring” may be observed in few cases
  Problem seems to be amplified for “Longer tap filters”
Figure 1. Typical boundary artifact

## Slide 3: Solution: Position dependent adaptive Tc clipping range
Adaptive Tc clipping range is proposed
  It is a “monotonically decreasing function” where-in the clipping range is defined based on the distance of the sample from the edge
    Closer the sample is to the edge, larger is the clipping range allowed and therefore larger is the deviation allowed after filtering and vice versa
Two monotonic functions are defined
  Function1 : [Pi – (tc + (tc >> i)), Pi + (tc + (tc >> i))]
  Function 2: [Pi – (2tc >> i), Pi + (2tc >> i)]
  Where “i” is the sample distance from the edge

## Slide 4: Objective results for Function 1
On top of VTM 2.0.1
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM-2.0.1 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 98% | 104% | 0.00% | 0.00% | 0.00% | 98% | 103%
Class A2 | 0.00% | 0.00% | 0.00% | 98% | 102% | 0.00% | 0.00% | 0.00% | 98% | 102%
Class B | 0.00% | 0.00% | 0.00% | 98% | 101% | 0.00% | 0.00% | 0.00% | 98% | 101%
Class C | 0.00% | 0.00% | 0.00% | 98% | 99% | 0.00% | 0.00% | 0.00% | 98% | 99%
Class E | 0.00% | 0.00% | 0.00% | 98% | 102% | 0.00% | 0.00% | 0.00% | 98% | 100%
Overall | 0.00% | 0.00% | 0.00% | 98% | 101% | 0.00% | 0.00% | 0.00% | 98% | 101%
Class D | 0.00% | 0.00% | 0.00% | 98% | 98% | 0.00% | 0.00% | 0.00% | 97% | 97%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM-2.0.1 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.03% | 0.02% | 98% | 100% | -0.01% | -0.01% | 0.08% | 98% | 100%
Class A2 | 0.00% | -0.04% | -0.01% | 98% | 99% | 0.04% | -0.03% | -0.08% | 98% | 99%
Class B | -0.01% | -0.02% | -0.01% | 98% | 98% | -0.01% | 0.04% | -0.06% | 98% | 99%
Class C | 0.01% | -0.01% | -0.07% | 98% | 98% | -0.01% | 0.04% | -0.06% | 98% | 97%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.00% | -0.01% | -0.02% | 98% | 99% | 0.00% | 0.02% | -0.04% | 98% | 99%
Class D | -0.01% | 0.03% | 0.02% | 98% | 97% | 0.02% | -0.06% | -0.02% | 98% | 97%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM-2.0.1 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0.01% | 0.08% | -0.18% | 98% | 99% | 0.05% | -0.13% | -0.18% | 98% | 99%
Class C | 0.01% | -0.20% | -0.02% | 98% | 97% | 0.04% | 0.01% | -0.03% | 98% | 97%
Class E | 0.13% | -0.25% | -0.24% | 98% | 97% | -0.12% | 0.27% | -0.02% | 98% | 96%
Overall | 0.03% | -0.10% | -0.14% | 98% | 98% | 0.00% | 0.02% | -0.09% | 98% | 97%
Class D | 0.04% | 0.11% | 0.02% | 98% | 97% | -0.03% | 0.10% | 0.33% | 98% | 97%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay P Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM-2.0.1 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0.01% | -0.16% | 0.16% | 98% | 100% | -0.02% | 0.16% | 0.23% | 98% | 99%
Class C | 0.02% | 0.13% | 0.04% | 98% | 97% | -0.02% | -0.11% | -0.12% | 98% | 97%
Class E | -0.12% | 0.37% | -0.10% | 98% | 98% | -0.10% | 0.03% | 0.28% | 98% | 98%
Overall | -0.03% | 0.07% | 0.06% | 98% | 98% | -0.04% | 0.03% | 0.12% | 98% | 98%
Class D | 0.01% | -0.41% | 0.04% | 98% | 97% | 0.04% | -0.14% | -0.41% | 98% | 97%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!

## Slide 5: Objective results for Function 2
On top of VTM 2.0.1
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM-2.0.1 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 98% | 104% | 0.00% | 0.00% | 0.00% | 98% | 103%
Class A2 | 0.00% | 0.00% | 0.00% | 98% | 102% | 0.00% | 0.00% | 0.00% | 98% | 102%
Class B | 0.00% | 0.00% | 0.00% | 98% | 102% | 0.00% | 0.00% | 0.00% | 98% | 101%
Class C | 0.00% | 0.00% | 0.00% | 98% | 99% | 0.00% | 0.00% | 0.00% | 98% | 100%
Class E | 0.00% | 0.00% | 0.00% | 98% | 102% | 0.00% | 0.00% | 0.00% | 98% | 101%
Overall | 0.00% | 0.00% | 0.00% | 98% | 102% | 0.00% | 0.00% | 0.00% | 98% | 101%
Class D | 0.00% | 0.00% | 0.00% | 98% | 98% | 0.00% | 0.00% | 0.00% | 98% | 99%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM-2.0.1 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | 0.03% | 98% | 100% | -0.01% | 0.09% | -0.01% | 98% | 100%
Class A2 | 0.00% | 0.04% | 0.04% | 98% | 99% | 0.03% | 0.00% | -0.06% | 98% | 99%
Class B | 0.01% | -0.03% | 0.01% | 98% | 98% | -0.01% | -0.04% | -0.02% | 98% | 98%
Class C | -0.01% | -0.03% | -0.03% | 98% | 97% | 0.00% | 0.10% | -0.03% | 97% | 96%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.00% | -0.01% | 0.01% | 98% | 98% | 0.00% | 0.03% | -0.03% | 98% | 98%
Class D | -0.02% | 0.02% | 0.00% | 98% | 97% | 0.03% | -0.09% | -0.07% | 97% | 96%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM-2.0.1 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.00% | 0.05% | -0.14% | 98% | 99% | 0.04% | 0.02% | -0.21% | 98% | 99%
Class C | -0.02% | -0.20% | -0.18% | 98% | 98% | 0.00% | 0.03% | -0.14% | 98% | 97%
Class E | 0.14% | -0.03% | 0.32% | 98% | 99% | -0.14% | -0.33% | 0.04% | 98% | 97%
Overall | 0.03% | -0.05% | -0.04% | 98% | 98% | -0.02% | -0.06% | -0.12% | 98% | 98%
Class D | 0.01% | 0.24% | 0.25% | 98% | 97% | 0.02% | 0.84% | 0.08% | 97% | 95%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay P Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM-2.0.1 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0.02% | -0.07% | 0.06% | 98% | 100% | -0.03% | 0.16% | 0.14% | 98% | 99%
Class C | 0.04% | 0.10% | -0.24% | 98% | 98% | 0.01% | -0.21% | -0.26% | 97% | 98%
Class E | -0.03% | 0.30% | -0.06% | 99% | 99% | 0.00% | 0.05% | 0.80% | 98% | 98%
Overall | -0.01% | 0.08% | -0.07% | 98% | 99% | -0.01% | 0.01% | 0.17% | 98% | 99%
Class D | -0.02% | -0.49% | -0.45% | 98% | 97% | 0.06% | 0.28% | 0.04% | 97% | 93%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!

## Slide 6: Objective results for Function 2 (with longer tap filter – CE 11.1.8 (JVET-L0224)
With ALF ON
Anchor 1: VTM 2.0.1
Anchor 2: VTM 2.0.1 + CE 11.1.8
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF ON) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.06% | 0.00% | 0.00% | 98% | 101% | -0.09% | 0.00% | 0.00% | 98% | 96%
Class A2 | -0.03% | 0.00% | 0.00% | 98% | 101% | -0.02% | 0.00% | 0.00% | 98% | 98%
Class B | -0.02% | -0.01% | 0.00% | 98% | 101% | -0.03% | 0.00% | 0.00% | 98% | 98%
Class C | -0.01% | 0.00% | 0.00% | 97% | 99% | -0.01% | 0.00% | 0.00% | 98% | 99%
Class E | -0.10% | -0.01% | -0.01% | 98% | 100% | -0.02% | 0.00% | 0.00% | 98% | 99%
Overall | -0.04% | 0.00% | 0.00% | 98% | 100% | -0.03% | 0.00% | 0.00% | 98% | 98%
Class D | 0.00% | 0.00% | 0.00% | 97% | 97% | 0.00% | 0.00% | 0.00% | 98% | 98%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF ON) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.19% | 0.16% | 0.04% | 98% | 100% | -0.14% | 0.17% | -0.03% | 99% | 98%
Class A2 | -0.07% | -0.07% | -0.06% | 98% | 100% | -0.03% | 0.03% | 0.02% | 99% | 99%
Class B | 0.00% | -0.02% | -0.01% | 98% | 100% | -0.02% | -0.08% | 0.02% | 99% | 99%
Class C | -0.01% | 0.13% | -0.03% | 98% | 99% | -0.01% | -0.01% | -0.07% | 99% | 99%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.06% | 0.05% | -0.02% | 98% | 100% | -0.05% | 0.01% | -0.01% | 99% | 99%
Class D | 0.00% | -0.14% | -0.04% | 98% | 98% | -0.04% | -0.19% | -0.02% | 98% | 99%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF ON) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.06% | 0.04% | -0.35% | 99% | 100% | -0.09% | -0.04% | -0.11% | 99% | 99%
Class C | 0.01% | -0.16% | -0.14% | 98% | 99% | -0.02% | -0.02% | -0.04% | 99% | 100%
Class E | -0.05% | -0.10% | -0.09% | 98% | 98% | -0.15% | 0.11% | 0.43% | 99% | 100%
Overall | 0.02% | -0.06% | -0.21% | 98% | 99% | -0.08% | 0.01% | 0.05% | 99% | 99%
Class D | 0.02% | 0.72% | -0.44% | 98% | 98% | -0.05% | 0.49% | -0.54% | 98% | 100%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay P Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF ON) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0.06% | 0.22% | 0.23% | 98% | 100% | -0.05% | -0.15% | 0.07% | 98% | 99%
Class C | -0.03% | 0.01% | -0.11% | 98% | 100% | -0.05% | 0.05% | 0.00% | 99% | 99%
Class E | -0.11% | 0.14% | 0.54% | 99% | 100% | -0.21% | 0.12% | 0.38% | 99% | 101%
Overall | -0.06% | 0.13% | 0.20% | 98% | 100% | -0.09% | -0.01% | 0.12% | 99% | 99%
Class D | 0.08% | 0.62% | -0.33% | 98% | 98% | 0.01% | 0.32% | 0.09% | 99% | 99%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!

## Slide 7: Objective results for Function 2 (with longer tap filter – CE 11.1.8 (JVET-L0224)
With ALF OFF
Anchor 1: VTM 2.0.1
Anchor 2: VTM 2.0.1 + CE 11.1.8
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF OFF) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.13% | 0.00% | 0.00% | 98% | 102% | -0.11% | 0.01% | 0.00% | 99% | 96%
Class A2 | -0.03% | 0.00% | 0.00% | 98% | 101% | -0.02% | 0.00% | 0.00% | 99% | 98%
Class B | -0.03% | 0.00% | 0.00% | 98% | 101% | -0.03% | 0.00% | 0.00% | 98% | 98%
Class C | -0.01% | 0.00% | 0.00% | 98% | 100% | -0.01% | 0.00% | 0.00% | 98% | 100%
Class E | -0.10% | -0.01% | 0.00% | 98% | 103% | -0.02% | 0.00% | 0.00% | 98% | 99%
Overall | -0.06% | 0.00% | 0.00% | 98% | 101% | -0.04% | 0.00% | 0.00% | 98% | 98%
Class D | 0.00% | 0.00% | 0.00% | 98% | 99% | -0.01% | 0.00% | 0.00% | 98% | 100%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF OFF) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.31% | -0.03% | 0.07% | 98% | 101% | -0.15% | -0.14% | 0.02% | 99% | 98%
Class A2 | -0.11% | -0.06% | -0.01% | 98% | 99% | -0.01% | -0.09% | -0.06% | 99% | 98%
Class B | -0.04% | 0.03% | 0.00% | 98% | 99% | -0.02% | 0.04% | 0.00% | 99% | 98%
Class C | -0.03% | 0.03% | -0.02% | 98% | 99% | 0.00% | 0.00% | 0.00% | 99% | 99%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.11% | 0.00% | 0.01% | 98% | 99% | -0.04% | -0.03% | -0.01% | 99% | 99%
Class D | -0.02% | 0.07% | 0.05% | 98% | 98% | 0.01% | 0.06% | -0.01% | 99% | 98%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF OFF) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.01% | 0.14% | -0.20% | 99% | 100% | -0.07% | -0.05% | -0.17% | 98% | 98%
Class C | 0.01% | -0.23% | -0.14% | 98% | 98% | -0.01% | -0.01% | -0.05% | 98% | 97%
Class E | 0.02% | -0.12% | 0.08% | 99% | 99% | -0.14% | 0.02% | -0.12% | 99% | 99%
Overall | 0.01% | -0.05% | -0.11% | 98% | 99% | -0.07% | -0.02% | -0.12% | 98% | 98%
Class D | -0.01% | -0.22% | 0.39% | 98% | 97% | -0.04% | -0.38% | 0.34% | 98% | 99%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay P Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF OFF) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0.12% | -0.23% | 0.06% | 98% | 101% | -0.05% | -0.12% | -0.18% | 98% | 98%
Class C | -0.03% | 0.21% | 0.21% | 98% | 98% | -0.05% | 0.13% | 0.20% | 99% | 99%
Class E | -0.27% | 0.22% | -0.15% | 99% | 99% | -0.04% | 0.11% | -0.09% | 99% | 99%
Overall | -0.13% | 0.03% | 0.06% | 98% | 100% | -0.05% | 0.02% | -0.03% | 99% | 98%
Class D | -0.05% | -0.39% | -0.32% | 98% | 98% | -0.01% | -0.13% | 0.08% | 99% | 99%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!

## Slide 8: Objective results for Function 1 (with longer tap filter – CE 11.1.8 (JVET-L0224)
With ALF ON
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF ON) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369(ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.00% | 0.00% | 97% | 100% | 0.00% | 0.00% | 0.00% | 97% | 96%
Class A2 | -0.01% | 0.00% | 0.00% | 97% | 100% | 0.00% | 0.00% | 0.00% | 97% | 97%
Class B | 0.00% | -0.01% | -0.01% | 97% | 99% | 0.00% | 0.00% | 0.00% | 97% | 96%
Class C | 0.00% | 0.00% | 0.00% | 97% | 97% | 0.00% | 0.00% | 0.00% | 98% | 96%
Class E | -0.08% | -0.01% | -0.01% | 97% | 97% | 0.00% | 0.00% | 0.00% | 98% | 96%
Overall | -0.01% | 0.00% | 0.00% | 97% | 99% | 0.00% | 0.00% | 0.00% | 97% | 96%
Class D | 0.00% | 0.00% | 0.00% | 97% | 96% | 0.00% | 0.00% | 0.00% | 98% | 97%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF ON) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369(ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.06% | -0.02% | 0.10% | 98% | 101% | -0.01% | -0.01% | 0.03% | 98% | 98%
Class A2 | -0.05% | -0.06% | -0.14% | 98% | 99% | -0.01% | 0.04% | -0.05% | 98% | 98%
Class B | 0.00% | -0.02% | -0.02% | 97% | 98% | -0.02% | -0.08% | 0.00% | 98% | 98%
Class C | -0.01% | 0.12% | 0.07% | 97% | 97% | -0.01% | -0.03% | 0.03% | 98% | 97%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.02% | 0.01% | 0.00% | 98% | 99% | -0.01% | -0.03% | 0.01% | 98% | 98%
Class D | 0.04% | 0.06% | -0.03% | 98% | 97% | 0.00% | 0.00% | 0.00% | 98% | 97%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF ON) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369(ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.14% | 0.01% | -0.17% | 98% | 100% | -0.01% | -0.07% | 0.06% | 98% | 98%
Class C | 0.05% | 0.14% | -0.10% | 98% | 96% | 0.02% | 0.29% | 0.01% | 98% | 97%
Class E | 0.15% | -0.21% | -0.26% | 98% | 98% | 0.06% | 0.01% | 0.26% | 99% | 100%
Overall | 0.11% | 0.00% | -0.17% | 98% | 98% | 0.02% | 0.07% | 0.09% | 98% | 98%
Class D | 0.05% | 0.43% | -0.68% | 98% | 97% | -0.02% | 0.20% | -0.77% | 98% | 99%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay P Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF ON) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369(ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.01% | 0.12% | 0.19% | 98% | 99% | 0.02% | -0.25% | 0.03% | 98% | 98%
Class C | 0.02% | 0.08% | 0.01% | 97% | 96% | 0.01% | 0.13% | 0.11% | 97% | 96%
Class E | 0.17% | -0.24% | 0.24% | 98% | 97% | 0.06% | -0.27% | 0.07% | 98% | 98%
Overall | 0.05% | 0.01% | 0.14% | 97% | 98% | 0.03% | -0.13% | 0.07% | 98% | 97%
Class D | 0.04% | 0.17% | -0.41% | 97% | 96% | -0.03% | -0.08% | 0.01% | 98% | 97%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
Anchor 1: VTM 2.0.1
Anchor 2: VTM 2.0.1 + CE 11.1.8

## Slide 9: Objective results for Function 1 (with longer tap filter – CE 11.1.8 (JVET-L0224)
With ALF OFF
Anchor 1: VTM 2.0.1
Anchor 2: VTM 2.0.1 + CE 11.1.8
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF OFF) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.01% | 0.00% | 97% | 101% | 0.00% | 0.00% | 0.00% | 98% | 95%
Class A2 | -0.01% | 0.00% | 0.00% | 97% | 100% | 0.00% | 0.00% | 0.00% | 97% | 97%
Class B | 0.00% | 0.00% | -0.01% | 97% | 99% | 0.00% | 0.00% | 0.00% | 97% | 96%
Class C | 0.00% | 0.00% | 0.00% | 97% | 98% | 0.00% | 0.00% | 0.00% | 97% | 98%
Class E | -0.08% | -0.01% | 0.00% | 97% | 100% | 0.00% | 0.00% | 0.00% | 98% | 97%
Overall | -0.02% | 0.00% | 0.00% | 97% | 100% | 0.00% | 0.00% | 0.00% | 97% | 97%
Class D | 0.00% | 0.00% | 0.00% | 97% | 97% | 0.00% | 0.00% | 0.00% | 97% | 97%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF OFF) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.16% | 0.10% | 0.00% | 97% | 100% | 0.00% | -0.02% | -0.05% | 98% | 98%
Class A2 | -0.09% | -0.03% | -0.03% | 97% | 99% | 0.01% | -0.06% | -0.08% | 98% | 98%
Class B | -0.02% | -0.01% | 0.02% | 98% | 99% | 0.00% | 0.00% | 0.02% | 98% | 98%
Class C | -0.02% | 0.01% | -0.05% | 98% | 99% | 0.01% | -0.02% | -0.02% | 99% | 99%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | -0.06% | 0.01% | -0.01% | 98% | 99% | 0.00% | -0.02% | -0.03% | 98% | 98%
Class D | -0.03% | 0.04% | 0.07% | 98% | 98% | -0.01% | 0.03% | 0.02% | 98% | 98%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF OFF) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.09% | 0.28% | -0.16% | 98% | 99% | 0.00% | 0.09% | -0.12% | 98% | 97%
Class C | 0.01% | -0.12% | -0.01% | 97% | 98% | -0.01% | 0.10% | 0.08% | 97% | 97%
Class E | 0.15% | -0.19% | 0.10% | 97% | 97% | -0.01% | -0.04% | -0.10% | 98% | 96%
Overall | 0.08% | 0.03% | -0.05% | 98% | 98% | 0.00% | 0.06% | -0.05% | 98% | 97%
Class D | 0.05% | -0.07% | 0.32% | 97% | 94% | 0.01% | -0.22% | 0.26% | 98% | 95%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!
 | Low delay P Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-2.0.1 (ALF OFF) |  |  |  |  | Over VTM 2.0.1 + JVET-K0369 (ALF OFF) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | -0.07% | 0.12% | -0.08% | 98% | 100% | 0.01% | 0.22% | -0.32% | 98% | 97%
Class C | 0.02% | 0.15% | 0.00% | 97% | 96% | 0.00% | 0.07% | -0.01% | 98% | 97%
Class E | -0.16% | 0.38% | -0.10% | 98% | 96% | 0.07% | 0.27% | -0.04% | 98% | 96%
Overall | -0.06% | 0.19% | -0.06% | 97% | 98% | 0.02% | 0.18% | -0.15% | 98% | 97%
Class D | -0.03% | -0.55% | 0.09% | 97% | 94% | 0.01% | -0.27% | 0.52% | 97% | 95%
Class F (optional) | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #VALUE!

## Slide 10: Subjective results for Function 2
Food Market QP 37, RA, POC 10
Anchor
With longer tap filter and Without “f2”
With longer tap filter and With “f2”

## Slide 11: Conclusion
Adaptive “tc” clipping range proposed to solve the problem of “over smoothing” or “blurring”
  Closer the sample to the boundary, larger is clipping range and vice versa
Two monotonically decreasing functions proposed
  Function1 : [Pi – (tc + (tc >> i)), Pi + (tc + (tc >> i))]
  Function 2: [Pi – (2tc >> i), Pi + (2tc >> i)]
No Objective loss observed
We propose to further study this technique in a core experiment

## Slide 12
Thank You
www.huawei.com

## Slide 13: Subjective results for Function 2
Food Market QP 37, RA, POC 39
Anchor
With longer tap filter and Without “f2”
With longer tap filter and With “f2”