## Slide 1: JVET-L0390 CE4-related: Simplification of Affine merge common codebase
Yao-Jen Chang, Yu-Chiao Yang
Macao, China
Oct. 2018

## Slide 2: Affine merge candidates in CE4.2.1
  CE4.2.1 : Affine merge common base
  Inherited candidates:
    {L, A, AR, LB, AL}
  Constructed candidates:
    6-param Affine model: {CP1, CP2, CP3}、{CP1, CP2, CP4}、{CP1, CP3, CP4}、{CP2, CP3, CP4}
    4-param Affine model: {CP1, CP2}、{CP2, CP3}、{CP1, CP4}、{CP1, CP3}、{CP2, CP4}、{CP3, CP4}
  Candidate comparisons between all candidates
A
AL
L
AR
LB
CP1
CP4
CP3
CP2

## Slide 3: The proposed modifications
  On top of Affine merge common base (CE4.2.1)
  Inherited candidates: Select only 1 candidate from each spatial area (left, above-right, above-left)
    Candidate comparisons to the first two cand. Are applied to the above-left spatial blocks
A
AL0
L
AR
AL1
AL2
LB
  6-param constructed candidates: Select M candidates (M < 4)
    Candidate comparisons to the first 6-param constructed cand.
  4-param constructed candidates: Select N candidates (N < 6)
    Candidate comparisons to the first 4-param constructed cand.

## Slide 4: Comparisons on constructed MV derivations
Get MV information of each CP
Start for each constructed cand.
CPMV derivation
Check availability of each CP
Check refIdx>=0 of each CP
Check picture idx & MVs
Yes
Yes
Yes
No
No
No
For loop (10)
Get MV information of each CP
Start for each constructed cand.
CPMV derivation
Check availability of each CP
Check refIdx>=0 of each CP
Check picture idx & MVs
Yes
Yes
Yes
No
No
No
For loop (1+N)
Affine merge common base
Proposed: constructed MV derivation
Test 2: M = 1, N = 4
Test 3: M = 1, N = 3
10 checks
(1+N)
checks
  6-param constructed candidates: Select 1 candidate
  4-param constructed candidates: Select N candidates (N < 6)

## Slide 5: Summary of experiments
  All implementation on top of Affine merge common base (CE4.2.1)
  Test 1:
    Potential candidates: inherited (3) + 6-param constructed (2) + 4-param constructed (4)
    Other implementation: reduce 72% candidate comparisons
  Test 2:
    Potential candidates: inherited (5, exactly the same as CE4.2.1) + 6-param constructed (1) + 4-param constructed (4)
    Other implementation: remove candidate comparisons and MV scaling
  Test 3:
    Potential candidates: inherited (5, exactly the same as CE4.2.1) + 6-param constructed (1) + 4-param constructed (3)
    Other implementation: remove candidate comparisons and MV scaling

## Slide 6: Simulation results – Test 1

## Slide 7: Simulation results – Test 2

## Slide 8: Simulation results – Test 3

## Slide 9: Summary of RA results
  Test 4.2.1: Affine merge common base
  Test 4.2.2.e: Potential candidates: inherited (2) + constructed (6) + removal of comparisons & scaling
  Test 4.2.5.a: Potential candidates: inherited (5) + constructed (10) + removal of comparisons & scaling
Notes: Short test
4.2.1: -0.59% -0.49% -0.68%
Test 2: -0.59% -0.50% -0.54%

## Slide 10: Summary of LB results
  Test 4.2.1: Affine merge common base
  Test 4.2.2.e: Potential candidates: inherited (2) + constructed (6) + removal of comparisons & scaling
  Test 4.2.5.a: Potential candidates: inherited (5) + constructed (10) + removal of comparisons & scaling

## Slide 11: Conclusion
This contribution proposes several modifications to simplify the Affine merge list construction
Gain is kept the same as Affine common base (CE4.2.1) with much lower complexity
On constructed aspect:
  Compared to CE4.2.2.e, 4.2.6.d
    Similarity: use less candidates than CE4.2.1 does
    Difference: first M available cands selected from 6-param, and first N available cands selected from 4-param
Thank MediaTek for crosschecking!

## Slide 12: Thank you.