## Slide 1: JVET-K0522 – CE4.2.4 simplification Adding constructed temporal affine to affine merge mode
October 2018
F.Galpin - Technicolor

## Slide 2: 4.2.4b: Constructed temporal affine
Add temporal constructed affine candidates
  Full list of candidates for 6 parameters model:
  Add a test to detect spurious affine candidate, similar to pure translational model detection in common base
Final number of candidates | Max Number of inherited candidates | Max Number of constructed candidates (4 prms) | Max Number of constructed candidates (6 prms)
8 | 5 | 12 | 16
Candidate number | Type | Corner number | Corner name
1 | spatial | { 0, 1, 2 } | LT, RT, LB
2 | temporal | { 0, 1, 2 } | LT, RT, LB
3 | spatial | { 0, 1 } | LT, RT
4 | temporal | { 0, 1, 3 } | LT, RT, RB
5 | spatial | { 0, 2 } | LT, LB
6 | temporal | { 0, 2, 3 } | LT, LB, RB
7 | spatial | { 1, 2 } | RT, LB
8 | temporal | { 1, 2, 3 } | RT, LB, RB
9 | spatial | { 0, 1, 3 } | LT, RT, RB
10 | temporal | { 0, 1 } | LT, RT
11 | spatial | { 0, 2, 3 } | LT, LB, RB
12 | temporal | { 0, 2 } | LT, LB
13 | spatial | { 1, 2, 3 } | RT, LB, RB
14 | temporal | { 1, 2 } | RT, LB
15 | spatial | { 0, 3 } | LT, RB
16 | temporal | { 0, 3 } | LT, RB

## Slide 3: Results 4.2.4b
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.02% | -0.68% | -1.01% | 110% | 111%
Class A2 | -1.15% | -1.15% | -1.25% | 112% | 113%
Class B | -0.75% | -0.59% | -0.75% | 111% | 109%
Class C | -0.61% | -0.47% | -0.48% | 110% | 109%
Overall | -0.85% | -0.69% | -0.83% | 111% | 110%
Class D | -0.90% | -0.74% | -0.81% | 111% | 118%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.42% | -0.49% | -0.53% | 117% | 116%
Class C | -0.40% | -0.61% | -0.32% | 110% | 109%
Class E | -0.76% | -0.35% | -0.39% | 111% | 113%
Overall | -0.50% | -0.50% | -0.42% | 113% | 113%
Class D | -0.62% | 0.48% | -0.43% | 109% | 108%
Thanks to Qualcomm for the xcheck (L0580)

## Slide 4: Simplified version
Add temporal constructed affine candidates
  Same as 4.2.4b:
    Same candidates as in 4.2.4b:
      Final list length: M=8
      Potential candidates: P=21
    Add a test to detect spurious affine candidate, similar to pure translational model detection in common base
  Added to 4.2.4b:
    Simplify pruning process: complexity C=3+3*(P-3) instead of C=(M-1)(M-2)/2+(M-1)(P-M+1)
    Replace affine flag contexts (AMVP 3 contexts) by a single context
  Additional test 2: move ATMVP candidate to affine merge list (similar to 4.2.5/4.2.8)

## Slide 5: 4.2.4b simplified - results: test 1
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.97% | -0.78% | -1.05% | 111% | 112%
Class A2 | -1.05% | -0.93% | -1.20% | 113% | 111%
Class B | -0.72% | -0.55% | -0.64% | 111% | 105%
Class C | -0.63% | -0.50% | -0.61% | 110% | 105%
Class E |  |  |  |  | 
Overall | -0.82% | -0.66% | -0.83% | 111% | 107%
Class D | -0.92% | -0.75% | -0.93% | 111% | 111%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.41% | -0.35% | -0.66% | 117% | 114%
Class C | -0.43% | -0.22% | -0.40% | 110% | 110%
Class E | -0.85% | -0.89% | -0.75% | 111% | 113%
Overall | -0.52% | -0.44% | -0.60% | 113% | 113%
Class D | -0.71% | 0.22% | -0.64% | 106% | 104%

## Slide 6: 4.2.4b simplified - results: test 2=test 1+ATMVP in affine merge
 | Random Access Main 10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.02% | -0.65% | -1.05% | 108% | 109%
Class A2 | -1.11% | -1.02% | -1.18% | 111% | 114%
Class B | -0.79% | -0.61% | -0.69% | 109% | 107%
Class C | -0.71% | -0.63% | -0.70% | 109% | 108%
Class E |  |  |  |  | 
Overall | -0.88% | -0.71% | -0.86% | 109% | 109%
Class D | -1.08% | -1.03% | -1.07% | 110% | 112%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-2.0.1 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.42% | -0.34% | -0.35% | 115% | 115%
Class C | -0.45% | -0.48% | -0.46% | 107% | 106%
Class E | -1.26% | -1.15% | -1.34% | 108% | 114%
Overall | -0.64% | -0.59% | -0.63% | 110% | 112%
Class D | -0.60% | -0.09% | -0.79% | 105% | 101%
Thanks to Interdigital for the xcheck (L0642)

## Slide 7: Complexity
  Complexity for candidate comparisons similar to common base (57 instead of 50)
  CPMV comparison has the a complexity of 34 (compared to 14 for the common base), thanks to the reuse of previous comparisons results for temporal candidates (see stroken pairs in the table below)
Complexity analysis of list construction |  |  |  |  |  | 
 | Max number of |  |  |  |  | 
M Merge list size | P Potential candidates | candidate comparison 3+3(P-3) | MV scaling | temporal candidates | Max number of memory access | CPMV comparisons
8 | 21 | 57 | 32 | 8 | 21 | 34
Candidate number | Type | CPMV number | CPMV pair comparison
2 | temporal | { 0, 1, 2 } | (0,1) (0,2)
4 | temporal | { 0, 1, 3 } | (0,1) (0,3)
6 | temporal | { 0, 2, 3 } | (0,3) (0,2)
8 | temporal | { 1, 2, 3 } | (1,2) (1,3)
10 | temporal | { 0, 1 } | (0,1)
12 | temporal | { 0, 2 } | (0,2)
14 | temporal | { 1, 2 } | (1,2)
16 | temporal | { 0, 3 } | (0,3)

## Slide 8: Conclusion
 | Gains |  | Complexity analysis of list construction |  |  |  | 
Tests | RA | LDB | M Merge list size | P Potential candidates | candidate comparison | MV scaling | CPMV comparisons
4.2.1 | -0.75% | -0.44% | 5 | 15 | 50 | 30 | 14
4.2.6d | -0.64% | -0.28% | 5 | 7 | 0 | 2 | 10
4.2.4b | -0.85% | -0.50% | 8 | 21 | 119 | 32 | 34
4.2.4b simplified | -0.82% | -0.52% | 8 | 21 | 57 | 32 | 34
4.2.4b simplied+ATMVP | -0.88% | -0.64% | 8 | 21 | 57 | 32 | 34

## Slide 9: Example of candidate comparisons reduction
Max list size | Type | CPMV number | CPMV comparisons
6 | temporal | { 0, 1, 2 } | {0}: 6, {1}:6, {2}:6
7 | temporal | { 0, 1, 3 } | {0}:1, {1}:1, {2’}:7
7 | temporal | { 0, 2, 3 } | {0’}:7, {1’}:1, {2}:1
7 | temporal | { 1, 2, 3 } | {0’}:7, {1}:1, {2’}:7
7 | temporal | { 0, 1 } | {2’}:7
7 | temporal | { 0, 2 } | {1’}:7
7 | temporal | { 1, 2 } | {0’}:7
7 | temporal | { 0, 3 } | {1’}:7 {2’}:7
Further optimization can also be performed for candidate comparisons. If result of the comparison with each CPMV with the candidates list is kept, it can reduced the number of comparisons to perform. In the table, numbers with an apostrophe refer to CPMV recomputed from other CPMVs. In the last column, we show the number of comparison N to perform for a CPMV C as {C}:N.
The total number of CPMV comparisons is down from 6*3+7*3*7=273 from to 86.