## Slide 1: JVET-M0027
CE7 Summary Report on
Quantization and
Coefficient Coding

## Slide 2: Tools under Test: JVET-L0145
Aspect (1)
VTM-3.0: Up to 32 / 8 regular coded bins per 4x4 / 2x2 subblock (with 4 / 1 abs_gt3 bins)
Proposal: 30 / 16 / 4 regular bins for luma 4x4 / chroma 4x4 / chroma 2x2 subblock (with 4 / 2 / 1 abs_gt3 bins)
Worst case for 4:2:0: Up to 25.33 regular bins per 16 samples (vs 32 in VTM-3)
Aspect (2)
Constraint on number of regular coded bins depends on last scanning position
3 different cases (factor 1, factor 5/4, factor 2)
Aspect (3)
Move abs_gt3_flag into first coding pass over a subblock (3 instead of 4 passes)
Modified context derivation (uses abs_gt3 flag for context modelling in first pass)

## Slide 3: Tests in CE 7
test | tester | document | short description | cross checker
7.1 | Tzu-Der Chuang | JVET-M0173 | Color component dependent constraint on maximum number of regular coded bins (per subblock) | Yu-Chen Sun (Alibaba)
7.2 | Tzu-Der Chuang | JVET-M0173 | Color component dependent constraint on maximum number of regular coded bins (per subblock) + Last significant position dependent constraint on maximum number of regular coded bins (per subblock) | Jung-Ah Choi (LGE) M. Coban (Qualcomm)
7.3 | Tzu-Der Chuang | JVET-M0173 | Color component dependent constraint on maximum number of regular coded bins (per subblock) + Last significant position dependent constraint on maximum number of regular coded bins (per subblock) + Include abs_gt3_flag into first coding pass | H. Schwarz (HHI) M. Coban (Qualcomm)
7.4 | Tzu-Der Chuang | JVET-M0173 | (3) Include abs_gt3_flag into first coding pass | H. Schwarz (HHI)

## Slide 4: CE 7: Average Results