## Slide 1: JVET-M0032
CE12: Summary report on mapping functions

## Slide 2: In-loop mapping design
2 aspects
  In-loop luma reshaping
  Luma-dependent chroma residue scaling
In-loop luma reshaping
  Signaling: parameters of a piece-wise linear (PWL) model for forward mapping (inverse mapping calculated from forward mapping)
  Implementation options:
    look-up tables (forward LUT, inverse LUT), or
    on-the-fly calculation
  Decoder side:
    intra slices: only inverse mapping is applied,
    inter slices: both forward and inverse mapping are applied
Luma-dependent chroma residue scaling
  TU-level fixed-point integer multiplication

## Slide 3: CE12: Tests
CE12-1: In-loop Reshaping for SDR on coding efficiency (JVET-L0246, JVET-L0247)
Test in-loop reshaping for SDR focused on coding efficiency improvement, such as making reshaping function rate adaptive, disable towards higher rates.
CE12-2: In-loop Reshaping for SDR on In-loop Reshaping for SDR on implementation investigation
Test in-loop reshaping for SDR focused on implementation investigation on pipelining of the block-wise prediction loop: such as piece-wise linear interpolation replacing LUT-based mapping, disable intra-block in inter slices.

## Slide 4: CE12-1 tests: SDR coding efficiency
CE12-1: In-loop Reshaping for SDR on coding efficiency
(JVET-L0246, JVET-L0247)
Intra slice reconstruction with in-loop luma reshaper
Inter slice reconstruction with in-loop luma reshaper
32-piece PWL each for luma and chroma residue scaling
Forward mapping inside intra prediction loop in inter slices
Inverse mapping in critical path of prediction loop

## Slide 5: CE12-2 tests: Implementation investigation
CE12-2: In-loop Reshaping for SDR on In-loop Reshaping for SDR on implementation investigation (JVET-L0247)
Intra slice reconstruction with in-loop luma reshaper
Inter slice reconstruction with in-loop luma reshaper
16 32-piece PWL each for luma and chroma residue scaling
Forward mapping not inside intra prediction loop in inter slices
Inverse mapping not in critical path of prediction loop

## Slide 6: Luma-dependent chroma residue scaling
Luma-dependent chroma residue scaling
  Encoder side: cResScale = cRes * cScale = cRes / cScaleInv
  Decoder side: cRes = cResScale / cScale = cResScale * cScaleInv
compensates for luma signal interaction with the chroma signal
one value calculated for each luma PWL range (instead of for each luma code value)
applied at the TU level, indexed by average luma value
simple multiplicative process implemented with fixed-point integer operation.

## Slide 7: Results
All Intra | psnrY | psnrU | psnrV | EncT | DecT
12-1 | -0.89% | 1.52% | 1.15% | 103% | 100%
12-2 | -0.89% | 1.49% | 1.18% | 102% | 101%
Random Access | psnrY | psnrU | psnrV | EncT | DecT
12-1 | -1.28% | 0.53% | 0.52% | 105% | 101%
12-2 | -1.30% | 1.45% | 1.44% | 105% | 104%
Low Delay B | psnrY | psnrU | psnrV | EncT | DecT
12-1 | -0.72% | 0.46% | 0.11% | 100% | 101%
12-2 | -0.76% | 1.78% | 1.42% | 98% | 105%

## Slide 8: CE12-1 / CE12-2 designs comparison
 | CE12-1 | CE12-2
FwdLUT / InvLUT construction | PWL interpolation with 32 pieces | PWL interpolation with 16 pieces
Decoding pipeline implication | need FwdLUT and InvLUT inside intra prediction loop in inter-slice, extra latency | no need for FwdLUT and InvLUT inside intra prediction loop for inter slice, unify intra mode in intra/inter slice, low latency, InvLUT not in critical path of inter prediction
Chroma residue scaling LUT | 32-entry, index by PWL piece idx to which the TU avg. luma belongs | 16-entry, index by PWL piece idx to which the TU avg. luma belongs

## Slide 9: Related CE12 contributions
number | Title | Source
JVET-M0427 | CE12: Mapping functions (test CE12-1 and CE12-2) | T. Lu, F. Pu, P. Yin, W. Husak, S. McCarthy, T. Chen (Dolby)
JVET-M0109 | CE12-related: block-based in-loop reshaping | E. Francois, C. Chevance, F. Hiron (Technicolor)
JVET-M0640 | CE12-related: in-loop reshaping with approximate inverse mapping function | E. Francois (Technicolor)