## Slide 1: JVET-0058 CE8.3.2: BDPCM with H/V predictor and independently decodable areas and modified binarization
M. Abdoli, G. Clare, F. Henry, P. Philippe

## Slide 2: Introduction
During the Macao meeting we proposed a « new » method to encode a block (JVET-L0078)
  BDPCM consists of a straighforward DPCM at CU level
    No intra prediction
    No transform
Fast encoding of Screen Content
  Typical use case: eSport (Live + SCC + High Resolution + High Frame Rate)
Main question at the Macao Meeting: can we increase the throughput of BDPCM?
  Tested modifications:
    Replaced LOCO-I with Horizontal/Vertical predictor (similar to RDPCM)
    Independently decodable areas for small blocks
    Modified binarization

## Slide 3: CE8.3.2 Test on Throughput
Horizontal/Vertical Predictor
  For each BDPCM block a flag is signalled to indicate Horizontal/Vertical predictor (similar to RDPCM)
  Thus pixels in different rows/columns can be processed in parallel
A
X
B
X
Horizontal prediction
Vertical prediction
Processed
in parallel
Processed
in parallel

## Slide 4: CE8.3.2 Test on Throughput
Independently Decodable Areas
  Blocks of size 4xN (resp. Nx4) have two independently decodable areas if the predictor is vertical (resp. horizontal)
  Pixel used for prediction is replaced with reference one when spatial neighbor not available
Area 1
Area 2

## Slide 5: CE8.3.2 Test on Throughput
Independently Decodable Areas
  8 pixels processed in parallel at all times
  Worst case throughput: 8 px/cycle
Throughout
Block size | 4x4 | 4x8, 8x4 | 4x16, 16x4 | 4x32, 32x4
Cycles | 2 | 4 | 8 | 16
Pixels | 16 | 32 | 64 | 128
Throughput (pixels/cycle) | 8 | 8 | 8 | 8

## Slide 6: CE8.3.2b Test on Throughput
Modified binarization of the coefficients
  A CBF flag indicates presence of non-zero coefficients
  The highest value the amplitude can take is 28.
  Truncated unary binarization up to level 12.
    The first bin is context coded with 3 contexts,
    The next coded with one context each (up to 11),
    All remainder coded with equiprobable bits binarized using second order Exp-Golomb codes
CE8-related JVET-M0449 from Tencent
  Proposes to limit the number of context coded bins in a BDPCM block to 2xWxH
  Achieves worst case of 2 context coded bin / coefficient (similar to Transform Coefficients) with negligible impact on compression

## Slide 7: VTM+CPR vs CE8.3.2
 |  | AI Over VTM-3.0 |  |  |  | 
 | Test# | Y | U | V | EncT | DecT
CTC overall | VTM+CPR | -0,27% | -0,40% | -0,33% | 137% | 100%
 | CE8.3.2 | -0,34% | -0,37% | -0,33% | 137% | 106%
Class F | VTM+CPR | -12,09% | -12,04% | -12,10% | 158% | 99%
 | CE8.3.2 | -15,68% | -14,05% | -14,06% | 139% | 106%
SCC 1080p | VTM+CPR | -36,92% | -36,11% | -36,36% | 143% | 90%
 | CE8.3.2 | -41,97% | -39,22% | -39,55% | 107% | 102%

## Slide 8: VTM+CPR+PLT vs CE8.3.2
 |  | AI Over VTM-3.0 |  |  |  | 
 | Test# | Y | U | V | EncT | DecT
CTC overall | VTM+CPR+PLT | -0,19% | -0,26% | -0,26% | 145% | 103%
 | CE8.3.2 | -0,27% | -0,28% | -0,24% | 141% | 109%
Class F | VTM+CPR+PLT | -15,51% | -14,05% | -14,13% | 173% | 97%
 | CE8.3.2 | -16,80% | -15,44% | -15,62% | 143% | 105%
SCC 1080p | VTM+CPR+PLT | -44,77% | -41,06% | -41,27% | 158% | 77%
 | CE8.3.2 | -46,16% | -42,65% | -42,86% | 106% | 90%

## Slide 9: Performance of BDPCM 8.3.2 – All Intra
 |  | AI Over VTM-3.0 |  |  |  | 
 | Test# | Y | U | V | EncT | DecT
CTC overall | CE8.3.2 | -0,08% | 0,00% | 0,04% | 105% | 98%
Class F | CE8.3.2 | -9,00% | -6,50% | -6,48% | 88% | 96%
SCC 1080p | CE8.3.2 | -24,45% | -19,08% | -19,37% | 73% | 99%

## Slide 10: VTM vs CE8.3.2 on Natural Content
 | AI Over VTM-3.0 (Natural Content) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,00% | 0,09% | 0,16% | 106% | 98%
Class A2 | 0,07% | 0,06% | 0,10% | 106% | 101%
Class B | 0,01% | 0,04% | 0,11% | 105% | 98%
Class C | -0,27% | -0,12% | -0,22% | 103% | 96%
Class E | -0,19% | -0,05% | 0,10% | 105% | 97%
Class D | -0,31% | -0,16% | -0,23% | 99% | 98%

## Slide 11: Conclusion
  Combination of well known tools (very similar to RDPCM )
  In all configuration: compression gains AND encoder runtime decrease
  Throughput
    Throughput is higher than most other processes (at least 8 pixels / cycle)
    Bin reduction proposed in JVET-M0449 (Tencent): worst case 2 context coded bin per coeffficient
    We proposed to adopt CE8.3.2 with limitation from JVET-M0449
    Draft text is available in the description
We thank HHI for crosschecking

## Slide 12: Thank you

## Slide 13: CE8.3.2 Test on Throughput
Encoder modification 1
  Suppose that C1, C2 and C3 are the intra modes selected during the rough check
  During the full RD check of intra modes, the following modification applies
    The BDPCM modes and C1 are checked for full RD cost
    If cost(BDPCM)<cost(C1), stop
    Otherwise, proceed with full check of C2 and C3
  This applies to all tests (including natural content)
Encoder modification 2
  A simple form of RDOQ: neighbor levels of quantization are checked for the BDPCM residue

## Slide 14: VTM+CPR+PLT vs VTM+CPR+BDPCM
 |  | AI Over VTM-3.0 |  |  |  | 
 | Test# | Y | U | V | EncT | DecT
CTC overall | VTM+CPR+PLT | -0,19% | -0,26% | -0,26% | 145% | 103%
 | CE8.3.2 | -0,34% | -0,37% | -0,33% | 137% | 106%
Class F | VTM+CPR+PLT | -15,51% | -14,05% | -14,13% | 173% | 97%
 | CE8.3.2 | -15,68% | -14,05% | -14,06% | 139% | 106%
SCC 1080p | VTM+CPR+PLT | -44,77% | -41,06% | -41,27% | 158% | 77%
 | CE8.3.2 | -41,97% | -39,22% | -39,55% | 107% | 102%