## Slide 1: Non-CE3: Intra chroma partitioning and prediction restriction
(JVET-M0065)
Tianyang Zhou
Tomohiro Ikai

## Slide 2: Outline
Proposal
Simulation results
Conclusion

## Slide 3: Proposal
 | Partitioning | Intra prediction
Option1 | Disable 2x2 in dual tree by Disable QT partitioning for 4x4 coding tree Disable BT partitioning when W * H <= 8 Disable TT partitioning when W * H <= 16 | DC for 2x2
Option2 | Disable 2x2/4x2/2x4 in dual tree by Disable QT partitioning for 4x4 coding tree Disable BT partitioning when W * H <= 16 Disable TT partitioning when W * H <= 32 | DC for 2x2, 2x4, 4x2

## Slide 4: Simulation results
 |  | All Intra Main 10 |  |  |  | 
 |  | Over VTM-3.0 |  |  |  | 
 |  | Y | U | V | EncT | DecT
Proposed Option 1 | Class A1 | 0.01% | 0.06% | 0.01% | 100% | 96%
 | Class A2 | 0.00% | 0.05% | 0.03% | 99% | 97%
 | Class B | 0.00% | 0.02% | 0.00% | 100% | 98%
 | Class C | -0.01% | 0.09% | 0.07% | 100% | 99%
 | Class E | -0.01% | -0.01% | 0.05% | 100% | 98%
 | Overall | 0.00% | 0.04% | 0.03% | 100% | 98%
 | Class D | 0.02% | 0.22% | 0.40% | 100% | 99%
Random Access Main 10 |  |  |  | 
OverVTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
0.01% | 0.05% | 0.12% | 100% | 99%
-0.01% | 0.14% | 0.04% | 101% | 100%
0.00% | 0.26% | 0.03% | 100% | 100%
0.04% | 0.19% | 0.47% | 100% | 100%
0.01% | 0.17% | 0.17% | 100% | 100%
0.06% | 0.15% | 0.51% | 100% | 100%
Low delay Main 10 |  |  |  | 
OverVTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
0.03% | -0.11% | -0.01% | 101% | 100%
0.02% | 0.29% | 0.33% | 100% | 100%
0.02% | 0.87% | -0.84% | 100% | 100%
0.03% | 0.27% | -0.11% | 100% | 100%
0.06% | 0.13% | 0.66% | 100% | 100%
Class A1
Class A2
Class B
Class C
Class E
Overall
Class D
Class A1
Class A2
Class B
Class C
Class E
Overall
Class D

## Slide 5: Simulation results 2x2 dual tree restriction only
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.06% | 0.01% | 100% | 83%
Class A2 | 0.00% | 0.05% | 0.03% | 99% | 90%
Class B | 0.00% | 0.02% | 0.00% | 100% | 86%
Class C | -0.01% | 0.09% | 0.07% | 100% | 89%
Class E | -0.01% | -0.01% | 0.05% | 100% | 76%
Overall | 0.00% | 0.04% | 0.03% | 100% | 85%
Class D | 0.02% | 0.22% | 0.40% | 100% | 92%
Class F (optional) | 0.02% | 0.29% | 0.39% | 100% | 82%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.03% | 0.08% | 100% | 88%
Class A2 | -0.02% | 0.13% | 0.05% | 100% | 89%
Class B | -0.02% | 0.13% | 0.03% | 100% | 85%
Class C | 0.02% | 0.13% | 0.24% | 100% | 89%
Class E |  |  |  |  | 
Overall | 0.00% | 0.11% | 0.10% | 100% | 88%
Class D | -0.02% | -0.16% | 0.16% | 100% | 93%
Class F (optional) | -0.01% | 0.31% | 0.25% | 100% | 84%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | -0.28% | -0.25% | 101% | 104%
Class C | 0.00% | 0.27% | 0.20% | 100% | 91%
Class E | 0.04% | 0.71% | -0.80% | 100% | 79%
Overall | 0.01% | 0.15% | -0.24% | 100% | 93%
Class D | 0.04% | -0.49% | 0.41% | 100% | 91%
Class F (optional) | 0.06% | 0.32% | 0.29% | 101% | 84%

## Slide 6: Simulation results
 |  | All Intra Main 10 |  |  |  | 
 |  | Over VTM-3.0 |  |  |  | 
 |  | Y | U | V | EncT | DecT
Proposed Option 2 | Class A1 | 0.03% | 0.17% | 0.04% | 100% | 96%
 | Class A2 | 0.04% | 0.27% | 0.22% | 97% | 97%
 | Class B | 0.00% | 0.09% | 0.24% | 100% | 97%
 | Class C | 0.07% | 0.81% | 1.16% | 99% | 97%
 | Class E | -0.01% | -0.12% | 0.09% | 99% | 98%
 | Overall | 0.03% | 0.26% | 0.38% | 99% | 97%
 | Class D | 0.14% | 1.28% | 2.10% | 99% | 97%
Random Access Main 10 |  |  |  | 
OverVTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
0.07% | 0.06% | 0.23% | 100% | 99%
0.03% | 0.36% | 0.31% | 100% | 100%
0.04% | 0.63% | 0.61% | 100% | 99%
0.19% | 1.24% | 1.98% | 99% | 99%
0.09% | 0.63% | 0.84% | 100% | 99%
0.32% | 1.82% | 2.77% | 99% | 99%
Low delay Main 10 |  |  |  | 
OverVTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
0.02% | -0.06% | 0.12% | 101% | 100%
0.10% | 0.84% | 1.37% | 100% | 100%
-0.16% | -0.08% | -0.33% | 100% | 100%
0.00% | 0.24% | 0.43% | 100% | 100%
0.17% | 0.75% | 1.40% | 100% | 100%
Class A1
Class A2
Class B
Class C
Class E
Overall
Class D
Class A1
Class A2
Class B
Class C
Class E
Overall
Class D

## Slide 7: Conclusion
To restrict intra chroma block partitioning in dual tree
  Option1 (2x2 restriction)
  Option2 (2x2/4x2/2x4 restriction)
To restrict intra chroma prediction modes in small block (DC prediction only)