## Slide 1: JVET-M0096 CE10-related: Inter-intra prediction combination
L. Pham Van, G. Van der Auwera,
A. K. Ramasubramonian, Vadim Seregin, M. Karczewicz
@qualcomm
01/2018
AV

## Slide 2: Proposed improvement of inter-intra prediction
Simplification:
Only Intra planar
No PDPC
Blending scheme:
pred(x, y) = (wT*top << 2 + wL*left << 2 +
(32 − wL − wT)*(wInter*Merge(x, y) + wIntra*PL(x, y)) + 64) >> 7;
wT = 16 >> ((x << 1) >> scl)
wL = 16 >> ((y << 1) >> scl)
scl = (log2(width) + log2(height) − 2) >> 2

## Slide 3: Adaptive weights for inter and planar samples
Weights are determined by number of intra coded neighboring
If top and left are intra-coded:
 (wIntra, wInter) = (3, 1)
If top or left is intra-coded:
 (wIntra, wInter) = (2, 2)
Else:  (wIntra, wInter) = (1, 3)

## Slide 4: Experimental results
Thank Technicolor for cross-checking!
Luma BD-rate gain: 0.10%, 0.15%, and 0.22% for RA, LDB, and LDP, resp.
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.10% | 0.10% | 0.26% | 96% | 102%
Class A2 | -0.12% | 0.04% | 0.14% | 97% | 101%
Class B | -0.13% | 0.11% | 0.02% | 96% | 98%
Class C | -0.03% | 0.14% | 0.17% | 95% | 98%
Class E |  |  |  |  | 
Overall | -0.10% | 0.10% | 0.13% | 96% | 99%
Class D | -0.08% | -0.06% | 0.07% | 96% | 98%
Class F (optional) | -0.04% | 0.04% | 0.06% | 95% | 98%
Low delay B Main10 |  |  |  | 
Over VTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.17% | -0.09% | -0.06% | 97% | 104%
-0.09% | 0.38% | 0.19% | 99% | 99%
-0.21% | -0.02% | -0.32% | 95% | 96%
-0.15% | 0.08% | -0.04% | 97% | 100%
-0.11% | -0.46% | 0.35% | 96% | 100%
-0.06% | -0.02% | 0.43% | 95% | 99%
Low delay P Main10 |  |  |  | 
Over VTM-3.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.26% | 0.33% | -0.08% | 98% | 98%
-0.06% | 0.49% | 0.23% | 99% | 100%
-0.38% | -0.61% | -0.07% | 96% | 97%
-0.22% | 0.15% | 0.02% | 98% | 98%
-0.13% | -0.42% | 0.05% | 97% | 99%
0.01% | 0.07% | -0.26% | 98% | 102%

## Slide 5: Conclusions
Simplification of inter-intra prediction.
Enhanced blending scheme.
Luma BD-rate gain: 0.10%, 0.15%, and 0.22% for RA, LDB, and LDP, resp.
Encoding time is reduced without an increase of decoding time
(EncT, DecT) is: (96%, 99%), (97%, 100%), (98%, 98%) for RA, LDB, and LDP, resp.