## Slide 1: Summary of JVET-M0107 and reliable runtimes
JVET-M0107
Jan. 2019
F. Le Léannec, Y. Chen

## Slide 2: JVET-M0107
  VTM-3.0 for Chroma TU:
    Context ID for gt1, parity, and gt3 flags:
      ctxId = 1 + min( sumAbs1 – numSig, 4 ) + ( diag == 0 ? 5 : 0 )
Current position
Neighboring positions for sumAbsLevel and numSig

## Slide 3: JVET-M0107
  Proposed Method 2 for Chroma TU:
    Context ID for gt1_flag, par_flag, gt3_flag:
      ctxId = 1 + ( diag == 0 ? 1 : 0 )
    Applied only on chroma TU
    Reduced complexity
    Saves 24 contexts
CtxId=2
CtxId=1

## Slide 4: JVET-M0107
  Method 3:
    For DC luma coefficient:
      In VTM-3.0: ctxId = 1 + min( sumAbs1 – numSig, 4 )

## Slide 5: JVET-M0107
  Method 3:
    For DC luma coefficient:
      In VTM-3.0: ctxId = 1 + min( sumAbs1 – numSig, 4 )
      Proposed: ctxId = 1 + min( sumAbs1’ – numSig’, 1 )
    On top of method 2
    Further reduced complexity
    Saves 33 contexts

## Slide 6: JVET-M0107: Method 2 reliable runtimes

## Slide 7: JVET-M0107: Method 3 reliable runtimes

## Slide 8: JVET-M0107: reduced local neighborhood usage for residual coding
  Conclusion
    Reduced complexity for context ID computation for flags gt1, parity and gt3
    Method 2: No more local template in chroma TUs (method2)
    Method 3: Smaller local template for DC luma coefficient
    Cleaned software: reduced runtime compared to VTM-3.0
Proposed method | Nb contexts/VTM-3.0 | RA (Y/Cb/Cr)
1 | -12 | 0.00%/0.19%/0.14%
2 | -24 | -0.01%/0.29%/0.23%
3 | -33 | 0.02% / 0.24% / 0.22%