## Slide 1: CE4: Modification on History-based Motion Vector Prediction
Yu Han, Wei-Jung Chien, Chun-Chi Chen, Han Huang, Chao-Hsiung Hung, Yan Zhang, Marta Karczewicz

## Slide 2: Abstract
This contribution presents modifications on History-based Motion Vector Prediction (HMVP) mode:
    Remove redundancy check from HMVP table update;
    Set the size of HMVP table to 10, and pick one out of every 3 to add in the merge list;
    Partial pruning when adding HMVP in the merge list;
Pairwise candidates generation not using HMVP predictors.
    Remove the dependency between pairwise and HMVP.
Sub tests:
    CE4.1.2.a, first 3 HMVPs pruned by left and above spatial candidates and pairwise not using HMVP predictors, achieved 0.03% loss in RA case;
    CE4.1.2.b, first 2 HMVPs pruned by left and above spatial candidates and pairwise not using HMVP predictors, achieved 0.03% loss in RA case;

## Slide 3: Technical description
Complexity analysis of HMVP mode is shown as below under CTC:
    The runtime saving for HMVP table update and adding HMVP to merge list is as below. In the decoder side, comparing with VTM3.0, sub test CE4.1.2.b achieved 59% time saving in RA case, achieved 62% time saving in LB case;
    Without redundancy check, the HMVP table can be easily implemented in circle buffer which is hardware friendly design
    Number of pruning reduction.
 | stage number | pruning number
VTM3.0 | 1+4=5 | 4+(4+3+2+1)=14
CE4.1.2.a | 3 | 2+2+2=6
CE4.1.2.b | 2 | 2+2=4

## Slide 4: Simulation results
Merge list equal to 6. Thanks MediaTek for crosschecking.
CE4.1.2.a, first 3 HMVPs pruned by left and above spatial candidates and pairwise not using HMVP predictors

## Slide 5: Simulation results
Merge list equal to 6. Thanks MediaTek for crosschecking.
CE4.1.2.b, first 2 HMVPs pruned by left and above spatial candidates and pairwise not using HMVP predictors

## Slide 6: Supplement tests
 |  | merge comparisons per cycle |  |  |  |  |  | RA |  |  | LB |  |  | Peak loss on Class A or B | 
 |  | 1 | 2 | 3 | 4 | 5 | # comp at 2 cycle | Y | U | V | Y | U | V |  | 
 | VTM3.0 | 21 | 11 | 8 | 7 | 6 | 35 |  |  |  |  |  |  |  | 
 | CE4.1.1a | 12 | 7 | 5 | 5 | 4 | 35 | 0.00% | 0.07% | 0.02% | 0.07% | 0.14% | 0.22% | BQTerrace | 0.42%
1 | HMVP table update without pruning and subsampled HMVP | 21 | 11 | 8 | 7 | 6 | 35 | 0.02% | 0.03% | 0.04% | 0.04% | 0.10% | 0.05% | BasketballDrive | 0.11%
2 | No HMVP in pairwise merge candidate | 21 | 11 | 8 | 7 | 6 | 35 | 0.00% | -0.01% | 0.01% | 0.05% | 0.09% | -0.08% | BQTerrace | 0.06%
3 | First 3 HMVPs pruned by left and above spatila candidates | 11 | 6 | 4 | 4 | 3 | 11 | 0.03% | 0.00% | 0.05% | 0.05% | 0.00% | 0.18% | BQTerrace | 0.11%
4 | First 2 HMVPs pruned by left and above spatila candidates | 9 | 5 | 4 | 3 | 2 | 9 | 0.04% | 0.05% | 0.07% | 0.04% | 0.10% | -0.17% | BQTerrace | 0.13%
5 | 1+2 | 21 | 11 | 8 | 7 | 6 | 35 | 0.02% | -0.03% | 0.01% |  |  |  |  | 
6 | 1+3 | 11 | 6 | 5 | 4 | 3 | 11 | 0.03% | -0.03% | 0.03% | 0.09% | 0.07% | 0.17% | BQTerrace | 0.18%
7 | 1+4 | 9 | 5 | 4 | 3 | 2 | 9 | 0.05% | 0.06% | 0.09% | 0.05% | 0.15% | -0.07% | BasketballDrive | 0.13%
8 | 2+3 | 11 | 6 | 4 | 4 | 3 | 11 | 0.02% | 0.09% | 0.00% |  |  |  |  | 
9 | 2+4 | 9 | 5 | 4 | 3 | 2 | 9 | 0.03% | 0.02% | -0.02% |  |  |  |  | 
10 | 1+2+3 (CE4.1.2.a) | 11 | 6 | 5 | 4 | 3 | 11 | 0.03% | 0.06% | 0.03% | 0.08% | 0.07% | 0.13% | BQTerrace | 0.14%
11 | 1+2+4 (CE4.1.2.b) | 9 | 5 | 4 | 3 | 2 | 9 | 0.03% | 0.02% | 0.04% | 0.08% | -0.03% | 0.08% | BQTerrace | 0.14%