## Slide 1: JVET-M0223 Non-CE9: Co-existence analysis for DMVR with BDOF
S. Sethuraman
Ittiam Systems
9 January 2019

## Slide 2: Individual and combined performances in CE
BDOF in VTM3.0 offers -1.17% luma BDRATE gain and ~0.3% chroma BDRATE gain as it is not applied to chroma components
DMVR (CE9.2.2f) offers -1.51% luma BDRATE gain and similar gains in chroma as it is applied to all 3 components
  Even after disabling DMVR for MMVD and SbTMVP blocks which increase EncT and DecT significantly, DMVR offer -1.41% luma BDRATE gain and similar chroma BDRATE gains
DMVR co-existing with BDOF (CE9.2.1g) offers -1.13% luma BDRATE gains and similar chroma BDRATE gains
Hence, BDOF+DMVR offers a total of -2.30% luma BDRATE gains and ~1.8% BDRATE gains for chroma
JVET-M0148 and JVET-M0517 propose certain simplifications to DMVR and BDOF respectively with minimal impact to coding gains
Pipeline dependency and internal memory needs related to different co-existence architectures are studied in this proposal

## Slide 3: CE9.2 – Dependency analysis
The default architecture used in CE (Architecture-1) performs DMVR first, DCTIF-MC follows after knowing refined MVs, and BDOF is performed on DCTIF-MC output samples
Horiz. DCTIF
DMVR Cost Evaluations
Best Integer distance refined MV selection and Error Surface based sub-pel refinement
Vert. DCTIF
Solving for 4x4 Flow vector
Bi-prediction averaging with gradient based correction
Sub-PU level pipeline requires DMVR related computations to be happening on a different sub-PU while MC+BDOF happen on a sub-PU on which DMVR has already happened. Otherwise, both DMVR and MC+BDOF related hardware blocks will have significant idle times.
  This doubles the memory requirement for passing the integer grid samples accessed from pre-fetch cache by DMVR to MC stage.
    2 x 2 x (sPUw + 11)x(sPUh + 5) 10-bit samples will need to be buffered. For 16x16 sub-PU, this will require 2268 10-bit sample memory.
    BiMC interpolated samples require 2 x 5 x (sPUw + 4) x (sPUh + 4) 10-bit samples
    BDOF requires 2 x 8 x 16 14-bit MC sample memory (256 x 14-bit samples)

## Slide 4: Timing Diagram for CE9.2 Architecture
Interpolation for refinement
DMVR Cost Evaluations
Finalize Integer delta MV +
obtain sub-pel deltaMV
Horiz DCTIF
Vert DCTIF
BDOF
Timing if DMVR and MC/BDOF work on the same sub-PU
Timing if DMVR and MC/BDOF work on different sub-PUs
Interpolation for refinement
DMVR Cost Evaluations
Finalize Integer delta MV +
obtain sub-pel deltaMV
Horiz DCTIF
Vert DCTIF
BDOF
Sub-PU N+1
Sub-PU N

## Slide 5: Proposed Architecture-1 – Shared BiMC
BDOF in VTM uses bilinear MC for extended samples and DCTIF-MC for central samples of CU
This architecture aims at sharing the bilinear MC done for DMVR also being used by BDOF for optical flow vector estimation
  BiMC produces (sPUw + 6)x(sPUh + 6) samples
  Flow vector calculation can be done concurrently with DCTIF horizontal interpolation (i.e. ~9 rows in advance than in the CE9.2 architecture)
Final correction is still performed based on DCTIF-MC based samples and gradients coming from both DCTIF-MC and BiMC (where BiMC samples are used only for left/right horizontal boundary gradients and top/bottom boundary gradients)
  Only 3 lines x 2 refs of 14-bit samples need to be buffered (instead of up to 10 lines)
  However, BiMC based gradient storage requires 2xsub-PU-w + 2xsub-PU-h of buffering
Even when DMVR is not applied, BDOF is performed on sub-PUs split as per DMVR logic
  This eliminates the ~25% increase in DCTIF computations (e.g. 18x18 instead of 16x16 DCTIF output) within CUs larger than 16x16 as BDOF assumes DCTIF-MC samples within CU
In an attempt to reduce average decoding time, the error-surface based sub-pixel refinement was disabled so that software can do DCTIF-MC at CU level

## Slide 6: Timing Diagram for Architecture-1
Interpolation for refinement
DMVR Cost Evaluations
Finalize Integer delta MV +
obtain sub-pel deltaMV
Horiz DCTIF
Vert DCTIF
BDOF
Timing if DMVR and MC/BDOF work on the same sub-PU
Timing if DMVR and MC/BDOF work on different sub-PUs
Interpolation for refinement
DMVR Cost Evaluations
Finalize Integer delta MV +
obtain sub-pel deltaMV
Horiz DCTIF
Vert DCTIF
BDOF
Sub-PU N+1
Sub-PU N

## Slide 7: Results for Architecture-1
The BDRATE drop relative to CE 9.2 architecture has come primarily from removing the sub-pixel refinement in DMVR which contributes ~0.13% in the presence of BDOF and higher when BDOF is disabled
However, the normative processing of regular BDOF (in INTER and MMVD Cus) as sub-Pus has caused an increase in encoding and decoding times
Also, the software is not optimized after the changes

## Slide 8: Variant of Architecture-1 (Shared-DCTIF-MC)
In this variant, DCTIF-MC is performed on the integer distance grid to produce the central sub-PU-w x sub-PU-h samples
  The extended samples can be produced using DCTIF itself or bilinear MC
Both DMVR and BDOF use the same set of interpolated samples
This architecture eliminates the need for buffering up the integer grid samples till DCTIF can happen
  However, the interpolated samples at 16-bits per sample need to be maintained 2 x (sub-PU-w + 4) x (sub-PU-h + 4)
Since DCTIF-MC is performed before knowing the delta-MV, sub-pixel refinement through error surface is disabled in this architecture
  However, when BDOF is not possible, gradient based correction at sub-PU level based on estimated sub-pel delta MV as the flow vector is done
DMVR can be pipeline with vertical interpolation of DCTIF-MC in this case
BDOF still needs to wait for DMVR to complete
For the case of MC + DMVR in one pipeline slot and BDOF in another pipeline slot, the memory requirement will be:
  2 x 2 x 20 x 20 = 1600 16-bit samples
  No other line buffers are required
Results not cross-checked, but similar to Arch.-1 but with reduced DecT

## Slide 9: Timing Diagram for variant of Architecture-1
Timing if MC+DMVR-cost evals and DMVR finalization/BDOF work on the same sub-PU
Timing if MC+DMVR-cost evals and DMVR finalization/BDOF work on different sub-PUs
Sub-PU N+1
Sub-PU N
Horiz DCTIF
Vert DCTIF
DMVR Cost Evaluations
Finalize Integer delta MV
BDOF
Horiz DCTIF
Vert DCTIF
DMVR Cost Evaluations
Finalize Integer delta MV
BDOF

## Slide 10: Architecture-2 – Mutual exclusivity between DMVR/BDOF
In the variant of Architecture-1,
  Perform BDOF around zero delta-MV without waiting for delta-MV
  Decide between BDOF and DMVR in a mutually exclusive manner at a PU level as follows:
    If delta-MV from DMVR is zero (or) the delta cost difference between zero-delta-MV cost and final DMVR cost is less than a threshold (e.g. less than 2 per pixel), then select BDOF based correction.
    Else, select DMVR based sub-PU level gradient based correction.
Horiz. DCTIF
DMVR Cost Evaluations
Best Integer distance refined MV selection and Error Surface based sub-pel refinement
Vert. DCTIF
Solve for 4x4 Flow vector at zero delta-MV
Bi-prediction averaging with gradient based correction
Decision between DMVR vs. BDOF

## Slide 11: Timing Diagram for Architecture-2
By performing flow vector computations in parallel with DMVR cost calculations, this offers the best single-PU timing
Memory requirements will be 2 x (sPUw + 4) x (sPUh + 4) 16-bit samples; for 16x16 sub-PU size, this will be 800 16-bit samples
Gradient based correction needs to be done in a highly parallel manner for all 16 4x4s for the best timing
Horiz DCTIF
Vert DCTIF
DMVR Cost Evaluations
Finalize Integer delta MV +
obtain sub-pel deltaMV +
Decide DMVR vs BDOF
BDOF Flow vectors
Bi-pred with Gradient based Correction

## Slide 12: Results for Architecture-2
Even when only one of the refinements is applied adaptively at the sub-PU level, nearly 2/3rd of the BD-RATE gain is retained
  This run uses the 13-point rhombus shaped search proposed in JVET-M0148 and PR-MR-SAD as the cost function (which together had a 0.14% drop over CE9.2.1g)

## Slide 13: Conclusions
The timing diagrams for the CE9.2 architecture is studied and 2 new architectures for co-existence are proposed
CE9.2 architecture offers the best BDRATE gain among the options, but requires higher internal memory
Proposed architecture-1 foregoes some of the BDRATE gains (~0.15%) to improve the timing
Variant of architecture-1 further reduces the internal memory needs by eliminating the need for 2 different MCs
  If bilinear MC is used for extended region, the computations are also reduced
Proposed architecture-2 offers the best timing and the lowest internal memory requirement at the expense of an additional 0.32% BDRATE drop.
It should be noted that variant of Architecture-1 can also be considered when only DMVR is enabled and BDOF is disabled as it offers the least internal memory and the best timing
Gradient based correction has been extended to be applicable for DMVR in this contribution
It is requested that some of these elements be adopted into VTM or studied further in CE

## Slide 14: THANKS TO QUALCOMM FOR CROSS-CHECKING THE RESULTS!