## Slide 1: CE3-related: Chroma intra candidates modification based on non-directional DM
Reporter： MA Yanzhuo, WAN Shuai

## Slide 2: Proposed method
- If DM is non-directional (PLANAR/DC),
- use 3 fixed directional modes (mode 6, 40, 61) to replace VER_IDX, HOR_IDX and VDIA_IDX

## Slide 3: Proposed method
intra_chroma_pred_mode[ xCb ][ yCb ] | IntraPredModeY[ xCb + cbWidth / 2 ][ yCb + cbHeight / 2 ] |  |  |  | 
 | 0 | 50 | 18 | 1 | X ( 0 <= X <= 66 )
0 | 66 | 0 | 0 | 0 | 0
1 | 50 | 66 | 50 | 50 | 50
2 | 18 | 18 | 66 | 18 | 18
3 | 1 | 1 | 1 | 66 | 1
4 | 81 | 81 | 81 | 81 | 81
5 | 82 | 82 | 82 | 82 | 82
6 | 83 | 83 | 83 | 83 | 83
7 | 0 | 50 | 18 | 1 | X
Table 8‑3 – Specification of IntraPredModeC[ xCb ][ yCb ] depending on intra_chroma_pred_mode[ xCb ][ yCb ] and IntraPredModeY[ xCb + cbWidth / 2 ][ yCb + cbHeight / 2 ] when sps_cclm_enabled_flag is equal to 1
intra_chroma_pred_mode[ xCb ][ yCb ] | IntraPredModeY[ xCb + cbWidth / 2 ][ yCb + cbHeight / 2 ] |  |  |  | 
 | 0 | 50 | 18 | 1 | X ( 0 <= X <= 66 )
0 | 6 | 0 | 0 | 0 | 0
1 | 40 | 66 | 50 | 6 | 50
2 | 61 | 18 | 66 | 40 | 18
3 | 1 | 1 | 1 | 61 | 1
4 | 81 | 81 | 81 | 81 | 81
5 | 82 | 82 | 82 | 82 | 82
6 | 83 | 83 | 83 | 83 | 83
7 | 0 | 50 | 18 | 1 | X

## Slide 4: Results of the proposal
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.08% | 0.10% |  | 101%
Class A2 | -0.02% | 0.00% | 0.02% |  | 101%
Class B | -0.01% | 0.05% | -0.03% |  | 101%
Class C | -0.01% | -0.04% | -0.12% |  | 99%
Class E | -0.03% | -0.08% | -0.04% |  | 100%
Overall | -0.02% | -0.02% | -0.02% |  | 100%
Class D | -0.02% | 0.06% | -0.04% |  | 99%
Class F | -0.01% | 0.11% | 0.10% |  | 100%
Anchor: VTM-3.0
Tested: The proposed method

## Slide 5: Results of the proposal
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | -0.03% | -0.37% | -0.52% |  | 
Class E | -0.04% | -0.53% | -0.48% |  | 
Overall |  |  |  |  | 
Class D | -0.05% | -0.27% | -0.49% |  | 
Class F |  |  |  |  | 
Anchor: VTM-3.0
Tested: The proposed method combined with JVET-M0213.

## Slide 6
Thanks