## Slide 1: JVET-M0299 CE11: Deblocking for 4 x N, N x 4 and 8 x N and N x 8 block boundaries that not are aligned with 8x8 grid (test 11.2.1)
Kenneth Andersson, Zhi Zhang, Rickard Sjöberg (Ericsson)
Anand Meher Kotra, Jianle Chen, Semih Esenlik, Biao Wang, Han Gao (Huawei)
Chia-Ming Tsai, Chih-Wei Hsu, Tzu-Der Chuang, Ching-Yeh Chen Yu-Wen Huang, Shaw-Min Lei (MediaTek)
Presenter: Chia-Ming Tsai

## Slide 2: Overall Summary
Propose to support deblocking for 4xN, Nx4 and 8xN and Nx8 block boundaries that not are aligned with 8x8 grid by
  Enforce HEVC weak filtering with maximum one sample modification
Experimental results
  0.02%, -0.12%, -0.14%, and -0.18% luma BD-rates for AI, RA, LB, and LP in VTM-3.0
  -0.05%, -0.23%, -0.21%, and -0.36% luma BD-rates for AI, RA, LB, and LP in VTM-3.0 with ALF switched off
  Negligible encoding/decoding time change
X
X
X
X
X
X
X
X
X
X
8
4
4
Weak Filtering
Weak Filtering
X
Sample used in filtering
X
Sample modified by filter

## Slide 3: Example of Subjective Comparison
Johnny, POC #509, Low-delay P, QP 34, ALF off
8 x 16 CU not deblocked
Partitioning information
Depth information
8x8 sample grid missing the edge
8 x 16 CU also deblocked
Partitioning information
Depth information
4x4 sample grid enables deblocking

## Slide 4: Example of Subjective Comparison
Kimono, POC #236, Low-delay B, QP 34, ALF off
Deblocking on 8x8 sample grid
The edges filtered at 4x4 sample grid and not covered by 8x8 sample grid
Deblocking on 4x4 sample grid

## Slide 5: Example of Subjective Comparison
KristenAndSara, POC #302, Low-delay P, QP 37, ALF off
Deblocking on 8x8 sample grid
Deblocking on 4x4 sample grid

## Slide 6: Detailed Results
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 (ALF OFF) |  |  |  |  | Over VTM-3.0 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.01% | 0.00% | 99% | 99% | 0.03% | 0.00% | 0.00% | 99% | 99%
Class A2 | -0.03% | 0.00% | 0.00% | 99% | 99% | 0.03% | 0.00% | 0.00% | 99% | 99%
Class B | -0.02% | 0.00% | 0.00% | 99% | 99% | 0.05% | 0.00% | 0.00% | 99% | 99%
Class C | -0.03% | -0.01% | -0.01% | 99% | 99% | 0.02% | -0.02% | -0.01% | 98% | 99%
Class E | -0.20% | 0.00% | 0.00% | 99% | 99% | -0.04% | -0.01% | -0.01% | 99% | 99%
Overall | -0.05% | -0.01% | 0.00% | 99% | 99% | 0.02% | 0.00% | 0.00% | 99% | 99%
Class D | -0.03% | 0.00% | -0.01% | 99% | 99% | 0.02% | 0.00% | -0.01% | 99% | 99%
Class F | -0.05% | 0.00% | -0.01% | 100% | 101% | -0.01% | 0.01% | 0.00% | 100% | 100%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 (ALF OFF) |  |  |  |  | Over VTM-3.0 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.17% | 0.06% | -0.02% | 99% | 99% | -0.05% | 0.11% | 0.02% | 99% | 98%
Class A2 | -0.42% | -0.16% | -0.17% | 98% | 98% | -0.19% | 0.08% | 0.09% | 98% | 98%
Class B | -0.17% | 0.00% | -0.09% | 98% | 98% | -0.09% | 0.02% | -0.04% | 99% | 98%
Class C | -0.21% | -0.02% | 0.12% | 98% | 98% | -0.15% | 0.08% | 0.07% | 98% | 98%
Overall | -0.23% | -0.02% | -0.04% | 98% | 98% | -0.12% | 0.07% | 0.03% | 98% | 98%
Class D | -0.20% | -0.03% | 0.13% | 98% | 98% | -0.17% | -0.06% | -0.23% | 98% | 98%
Class F | -0.07% | -0.02% | -0.03% | 100% | 100% | -0.08% | -0.09% | -0.04% | 100% | 100%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 (ALF OFF) |  |  |  |  | Over VTM-3.0 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -0.15% | -0.10% | -0.13% | 98% | 98% | -0.11% | -0.31% | 0.15% | 98% | 98%
Class C | -0.28% | 0.01% | -0.18% | 97% | 97% | -0.14% | 0.09% | 0.24% | 97% | 97%
Class E | -0.23% | 0.30% | -0.45% | 98% | 98% | -0.18% | -0.27% | -0.63% | 98% | 99%
Overall | -0.21% | 0.04% | -0.23% | 98% | 98% | -0.14% | -0.17% | -0.01% | 98% | 98%
Class D | -0.20% | -0.30% | -0.52% | 97% | 98% | -0.14% | 0.13% | 0.11% | 97% | 97%
Class F | -0.15% | -0.06% | 0.00% | 100% | 101% | 0.01% | -0.31% | 0.30% | 100% | 100%
 | Low delay P Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0 (ALF OFF) |  |  |  |  | Over VTM-3.0 (ALF ON) |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class B | -0.30% | -0.03% | -0.33% | 98% | 99% | -0.12% | 0.27% | 0.15% | 98% | 98%
Class C | -0.31% | 0.15% | -0.08% | 97% | 97% | -0.19% | 0.14% | 0.06% | 97% | 98%
Class E | -0.53% | 0.41% | 0.01% | 98% | 99% | -0.27% | -0.85% | -1.14% | 98% | 99%
Overall | -0.36% | 0.14% | -0.16% | 97% | 98% | -0.18% | -0.06% | -0.20% | 98% | 98%
Class D | -0.26% | -0.59% | 0.12% | 97% | 97% | -0.16% | -0.61% | -0.21% | 97% | 97%
Class F | -0.23% | -0.01% | -0.23% | 100% | 99% | 0.01% | -0.07% | -0.15% | 100% | 100%

## Slide 7: Summary
Proposed to support deblocking for 4xN, Nx4 and 8xN and Nx8 block boundaries that not are aligned with 8x8 grid
  Only filter one sample adjacent to the block boundary at both sides using HEVC normal/weak filtering if any side of the blocks sharing the edge has a size of 4 samples
Some BD-rate improvement with negligible run-time change