## Slide 1
JVET-M0316
CE9-related: simplification of BDOF
Jingya Li, Ru-Ling Liao Chong Soon Lim

## Slide 2: Introduction
Simplification of bi-directional optical flow
Removing up to 98% multiplication operations of BDOF
Reduce 60% on chip buffer of BDOF
0.15% loss, 99% EncT, 95% DecT in RA

## Slide 3: Complexity of BDOF in VTM-3.0
Overall, 15% increase in multiplications
From pipeline point of view, 253% increase in multiplications in reconstruction stage

## Slide 4: Proposal’s complexity reduction
All 32-bit multiplications are removed
Up to 98% multiplications in BDOF are removed
removed

## Slide 5: Proposed algorithm
Proposed method
s3
s4
s1
s2
If S1 > th & s2 < th
  vx vy
Else If S2 > th & s2 < th
  vx 0, vy
Else
  vx vy

## Slide 6: BDOF on-chip buffer
VTM3.0:
M*N*5*32bit
Proposal:
M*N*4*16bit (60% reduction)
M*N is block size to store intermediate values

## Slide 7: Simulation results
0.15% B-D rate loss
5% DecT reduction
Random Access | Simplification of BDOF |  |  |  | 
Main 10 | Y | U | V | EncT | DecT
Class A1 | 0.07% | 0.04% | 0.02% | 99% | 96%
Class A2 | 0.15% | 0.09% | 0.07% | 99% | 95%
Class B | 0.19% | 0.16% | 0.09% | 99% | 94%
Class C | 0.14% | 0.12% | 0.15% | 99% | 96%
Overall | 0.15% | 0.11% | 0.08% | 99% | 95%
Class D | 0.24% | 0.17% | 0.20% | 99% | 97%
Class F | 0.03% | 0.00% | 0.03% | 99% | 97%

## Slide 8: Conclusions
Simplification of BDOF
Removing 98% multiplication operations of BDOF
Reduce 60% on-chip buffer
0.15% loss with 5% DecT reduction in RA
It is suggested to adopt this proposal to VVC

## Slide 9: Acknowledgments
Thank LG for cross-checking