## Slide 1: JVET-M0323 CE13-related: Adaptive QP to improve subjective quality for PHEC
Yule Sun, Xuchang Huangfu, Lu Yu
Zhejiang University

## Slide 2: Introduction
In-loop filters disabled across face discontinuities on PHEC with 2-pixel padding (M0322)
  The seam artifacts are still visible when coded QP is large (e.g. 37) near face row boundaries.
Enlarged seam artifacts of ChairLift

## Slide 3: Proposed method
Propose a geometry based adaptive QP method to use lower QP on area near the face row boundaries
  Implemented on coding tree unit (CTU) level

## Slide 4: Proposed method
Slice QP | Coded QP
0 - 31 | Slice QP
32 - 35 | 32
36 - 39 | 34
40 - 43 | 36
44 - 47 | 38
48 - 51 | 40
52 - 55 | 42
56 - 59 | 44
60 - 63 | 46
Table 1. Coded QP of boundary CTUs according to slice QP in current VTM.
Enabled on the slice with QP larger than 32
QP offsets of boundary CTUs are derived according to slice QP:

## Slide 5: Experimental results
Simulation setting
  Based on 360Lib-8.0 and VTM 3.0
  PHEC (3*2 layout, Face width is 1280)
Overall results
 | Anchor: PHEC |  |  | Anchor：CE test 1.1 (b) |  | 
 | Y | U | V | Y | U | V
SkateboardInLot | 2.77% | -0.75% | 0.25% | 2.63% | -0.26% | -0.13%
ChairLift | 2.32% | -2.80% | -2.15% | 2.39% | -2.69% | -2.06%
KiteFlite | 0.65% | -4.09% | -4.04% | 0.68% | -4.11% | -3.92%
Harbor | 1.32% | -5.09% | -4.71% | 1.42% | -4.79% | -4.64%
Trolley | 1.42% | -3.03% | -3.19% | 1.46% | -2.92% | -2.96%
GasLamp | 0.37% | -6.11% | -5.60% | 0.44% | -5.96% | -5.43%
Balboa | 3.80% | 1.81% | 2.65% | 3.75% | 2.26% | 2.56%
Broadway | 3.84% | 1.29% | 1.15% | 3.77% | 1.40% | 1.25%
Landing2 | 3.37% | -1.91% | 0.37% | 3.41% | -0.56% | 1.39%
BranCastle2 | 4.06% | 1.52% | 2.23% | 4.05% | 1.33% | 2.12%
Class S1 | 1.48% | -3.65% | -3.24% | 1.50% | -3.46% | -3.19%
Class S2 | 3.77% | 0.68% | 1.60% | 3.75% | 1.11% | 1.83%
Overall | 2.39% | -1.92% | -1.31% | 2.40% | -1.63% | -1.18%
Notes: 提及复杂度

## Slide 6: Experimental results
Enlarged seam artifacts (ChairLift; Frame=165)
Left: PHEC with 2-pixel padding (QP=37) Right: Adaptive method (QP=38)
Notes: 提及复杂度

## Slide 7: Conclusion
A geometry based adaptive QP method with in-loop filters disabled across face discontinuities and padding to improve subjective quality of PHEC is proposed.
The proposed method significantly improves subjective quality while it has 2.40% coding loss compared to PHEC with in-loop filters disabled across face discontinuities.
Further on CU level.

## Slide 8
Thank InterDigital for cross-checking!

## Slide 9
Thank you for your attention!