## Slide 1: Non-CE8: modification on SbTMVP process regarding with CPR (JVET-M0335)
Hyeongmun Jang (hm.jang@lge.com)

## Slide 2: Proposed method
Simply disallowing SbTMVP
  When fetched collocated center subblock L0 motion is CPR coded.
Simply disallowing TMVP
  When fetched collocated L0 motion is CPR coded.

## Slide 3: Motivation
In VTM-3.0 SbTMVP/TMVP is disallowed when fetched motion is CPR coded.
In VVC spec. (v7),
  It will be happen that coding unit is coded by PRED_BI with L0 referring current picture and L1 previous decoded picture as reference.
In VVC spec. (v9), disallowing this cases is guaranteed by conformance sentence.
  It is a requirement of bitstream conformance that when the current decoded picture is a reference picture for the current coding unit, inter_pred_idc[ x0 ][ y0 ] shall be equal to 0.
However CPR-inter multi hypothesis coding method could be suggested later.
  In this case, temporal motion prediction could be allowed based on L1 motion vector.

## Slide 4: Experimental results
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.08% | -0.10% | 0.06% | 126% | 101% | 0.00% | 0.00% | 0.00% | 99% | 100%
Class A2 | -0.47% | -0.50% | -0.55% | 128% | 101% | 0.00% | 0.00% | 0.00% | 100% | 101%
Class B | -0.30% | -0.39% | -0.36% | 135% | 100% | 0.00% | 0.00% | 0.00% | 100% | 99%
Class C | -0.09% | -0.24% | -0.25% | 140% | 101% | 0.00% | 0.00% | 0.00% | 100% | 101%
Class E | -0.64% | -0.81% | -0.59% | 139% | 101% | 0.00% | 0.00% | 0.00% | 100% | 101%
Overall | -0.27% | -0.40% | -0.33% | 134% | 101% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class D | -0.10% | -0.23% | 0.22% | 136% | 101% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class F (optional) | -12.09% | -12.04% | -12.10% | 155% | 98% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class SCC 1080p | -36.92% | -36.11% | -36.36% | 109% | 83% | 0.00% | 0.00% | 0.00% | 100% | 100%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.14% | -0.04% | 0.22% | 99% | 100% | 0.00% | 0.00% | 0.00% | 99% | 100%
Class A2 | 0.00% | 0.07% | 0.24% | 96% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class B | 0.02% | 0.00% | -0.21% | 99% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class C | 0.19% | -0.06% | 0.08% | 102% | 99% | 0.00% | 0.00% | 0.00% | 100% | 99%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.09% | -0.01% | 0.05% | 99% | 100% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class D | 0.15% | -0.28% | 0.16% | 102% | 99% | 0.00% | 0.00% | 0.00% | 100% | 99%
Class F (optional) | -9.89% | -9.92% | -9.95% | 106% | 99% | 0.00% | 0.00% | 0.00% | 100% | 100%
Class SCC 1080p | -22.03% | -21.58% | -22.11% | 103% | 98% | 0.00% | 0.00% | 0.00% | 100% | 101%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-3.0-CPR-off |  |  |  |  | Over VTM-3.0-CPR-on |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.07% | -0.32% | -0.13% | 106% | 99% | 0.00% | 0.00% | 0.00% | 100% | 98%
Class C | 0.13% | 0.39% | 0.33% | 108% | 98% | 0.00% | 0.00% | 0.00% | 99% | 98%
Class E | 0.28% | 1.07% | -0.19% | 105% | 99% | 0.00% | 0.00% | 0.00% | 99% | 98%
Overall | 0.14% | 0.26% | 0.01% | 106% | 99% | 0.00% | 0.00% | 0.00% | 99% | 98%
Class D | 0.13% | -0.15% | 0.70% | 111% | 98% | 0.00% | 0.00% | 0.00% | 100% | 97%
Class F (optional) | -5.14% | -5.38% | -5.48% | 107% | 99% | 0.00% | 0.00% | 0.00% | 99% | 99%
Class SCC 1080p | -13.08% | -13.36% | -13.58% | 108% | 95% | 0.02% | 0.07% | 0.06% | 100% | 98%

## Slide 5: Additional Suggestion
Add conformance sentence in order to disallow temporal mv prediction for picture which have only current picture as reference picture.
  slice_temporal_mvp_enabled_flag specifies whether temporal motion vector predictors can be used for inter prediction. If slice_temporal_mvp_enabled_flag is equal to 0, the syntax elements of the current picture shall be constrained such that no temporal motion vector predictor is used in decoding of the current picture. Otherwise (slice_temporal_mvp_enabled_flag is equal to 1), temporal motion vector predictors may be used in decoding of the current picture. When not present, the value of slice_temporal_mvp_enabled_flag is inferred to be equal to 0.
  It is a requirement of bitstream conformance that slice_temporal_mvp_enabled_flag should be 0 for P slices where the current picture is the only reference picture for the slice