## Slide 1: Non-Linear Adaptive Loop Filter (JVET-M0385)
Jonathan Taquet (jonathan.taquet@crf.canon.fr)
Christophe Gisquet
Guillaume Laroche Patrice Onno
Canon Research France

## Slide 2: Non-Linear Adaptive Loop Filter (JVET-M0385)
Jonathan Taquet (jonathan.taquet@crf.canon.fr), Christophe Gisquet, Guillaume Laroche, Patrice Onno
Canon Research France
09/01/2019

## Slide 3: Introduction

## Slide 4: Filtering in Adaptive Loop Filter (VTM3.0)
Filtering in Adaptive Loop Filter (in VTM3.0)
  Luma
    4x4 block of samples classified based on local gradients (25 classes)
    Each class associated to a filter index (N<25 filters, 7x7 diamond shape)
    1 flag to signal if ALF is applied or not per CTU
    For each filtered sample value
      The filter is selected from the class of the 4x4 block
      The filter is rotated/mirrored depending on gradient orientation (Transpose Index)
  Chroma
    1 filter for the two components (5x5 diamond shape)
    CTU, 1 flag per channel to signal if ALF is applied or not
    For each value
      Filter value (next slide) using Chroma filter
  Filter
    Output value is a linear combination of current value and neighbor values
    is determined based on such that
9
10
11
12
11
10
9
4
5
6
7
8
1
2
3
0
8
7
6
5
4
3
2
1
0
4
5
6
5
4
1
2
3
0
3
2
1
0

## Slide 5: Proposed Non-Linear filter

## Slide 6: Non-Linear Filter
Original filtering of a sample value in VTM3.0 (linear filter)
  a linear combination of current value and neighbor values :
  with =1-
Possible Reformulation (linear filter)
  a linear combination of current value and neighbor differences to current value :
  =1
Proposed modification (non-linear filter)
  a linear combination of current value and result of a non-linear function applied to neighbor differences to current value :
    with
    and clipping values optimized at encoder together with .

## Slide 7: Experiment

## Slide 8: Implementation in VTM3.0 (Key points)
VTM3.0 Linear filtering is replaced by non-linear filtering
As many clipping values are signaled as encoded filter coefficients
  12 clipping values per Luma filter
  6 clipping value for Chroma filter
A limited number of clipping values is allowed
  3 possible values on INTRA slices
  4 possible values on INTER slices
  Limit signaling cost (only value index is signaled)
  Limit encoder complexity
 | INTRA | INTER
LUMA | { 10, 102, 1024 } | { 6, 32, 181, 1024 }
CHROMA | { 4, 24, 1024 } | { 4, 25, 161, 1024 }

## Slide 9: Results
Encouraging BDR results
Decoder complexity:
  Non-linear ALF more often selected as active than VTM3 ALF
  Design could benefit of SIMD implementation (not the case here)
Recommendation: study the proposed modified ALF design in a CE

## Slide 10: Thanks to Sony for cross-checking Thanks for your attention

## Slide 11: Backup slide: Implementation in VTM3.0 (Encoder)
With
  the number of allowed clipping values, the number of coefficients of the filter, and the -th and -th allowed clipping value (), and the -th and -th coefficient indexes () associated to filter positions and
we compute matrices of size such that:
It allows to build, for fixed clipping values indexes , a “covariance” matrix similar to the “covariance” matrix that is used with linear ALF

## Slide 12: Backup slide: Implementation in VTM3.0 (Encoder)
Optimization of clipping values
  start with and with fixed clipping value indexes
  Estimate MSE of the corresponding Wiener filter (using matrix )
  Do
    For each
      increase if it improves MSE of the corresponding Wiener filter
      Or decrease if it improves MSE of the corresponding Wiener filter
  While improves MSE compared to