## Slide 1: Non-CE8: chroma block vector initialization for CPR in dual tree
JVET-M0393
Jan. 2019
T. Poirier

## Slide 2: Non-CE8: chroma interpolation for CPR results in VTM-3.0
  During last meeting, chroma interpolation has been removed for CPR
    But an encoder bug was present in VTM-2.0, in Dual Tree
    Valid block vector for Luma where rejected because corresponding chroma block vector was invalid

## Slide 3: Non-CE8: chroma interpolation Results
  In VTM-3.0
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.04% | -0.03% | 100% | 100%
Class A2 | -0.01% | -0.03% | 0.02% | 99% | 98%
Class B | 0.00% | 0.00% | 0.00% | 102% | 101%
Class C | 0.01% | -0.01% | 0.08% | 100% | 99%
Class E | 0.00% | 0.03% | 0.05% | 100% | 101%
Overall | 0.00% | -0.01% | 0.02% | 100% | 100%
Class D | -0.01% | 0.03% | 0.10% | 99% | 100%
Class F (optional) | -0.02% | 0.00% | -0.03% | 99% | 100%
TGM | -0.43% | -0.39% | -0.43% | 100% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.07% | 0.08% | 100% | 101%
Class A2 | 0.00% | -0.17% | -0.14% | 101% | 100%
Class B | 0.00% | 0.03% | -0.10% | 101% | 100%
Class C | 0.00% | 0.01% | 0.06% | 100% | 99%
Class E |  |  |  |  | 
Overall | 0.00% | -0.01% | -0.03% | 100% | 100%
Class D | 0.02% | 0.00% | 0.08% | 100% | 99%
Class F (optional) | -0.06% | -0.29% | -0.18% | 101% | 99%
TGM | -0.73% | -1.11% | -0.88% | 101% | 98%

## Slide 4: Non-CE8: chroma interpolation Results
  In VTM-3.0, no Dual Tree
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.07% | -0.03% | 102% | 99%
Class A2 | -0.24% | -0.50% | -0.42% | 101% | 100%
Class B | -0.02% | -0.14% | -0.09% | 103% | 101%
Class C | -0.07% | -0.03% | -0.11% | 102% | 102%
Class E | 0.02% | -0.19% | -0.36% | 103% | 102%
Overall | -0.06% | -0.17% | -0.18% | 102% | 101%
Class D | -0.02% | -0.15% | -0.06% | 101% | 100%
Class F (optional) | -0.36% | -0.61% | -0.84% | 102% | 101%
TGM | -1.91% | -2.07% | -1.82% | 103% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.10% | 0.02% | 100% | 99%
Class A2 | -0.07% | -0.45% | -0.21% | 99% | 101%
Class B | -0.01% | -0.09% | -0.17% | 98% | 96%
Class C | -0.04% | -0.22% | -0.20% | 95% | 90%
Class E |  |  |  |  | 
Overall | -0.02% | -0.20% | -0.15% | 98% | 96%
Class D | 0.03% | -0.19% | 0.08% | 95% | 93%
Class F (optional) | -0.39% | -0.57% | -0.63% | 96% | 92%
TGM | -1.16% | -1.30% | -1.06% | 96% | 96%

## Slide 5: Non-CE8: block vector initialization for Chroma in Dual Tree
  In VTM-3.0, Chroma uses CPR in Dual Tree only if all collocated luma blocks are CPR coded
    There is nothing to prevent signalling a chroma CPR CU when part or all of the collocated luma CU don’t use CPR

## Slide 6: Non-CE8: block vector initialization for Chroma in Dual Tree
  If current collocated luma sub-block don’t use CPR
    Merge with left BV
    if left subblock is outside current block merge with top BV
    If both left and top subblocks are ouside the current block, Initialize with default BV (-2*W, 0)

## Slide 7: Non-CE8: Proposed initialization vs chroma interpolation
  Proposed + chroma_interpolation vs VTM-3.0 + chroma_interpolation
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.01% | 0.04% | 100% | 99%
Class A2 | -0.02% | 0.05% | -0.03% | 99% | 99%
Class B | -0.01% | 0.01% | 0.04% | 99% | 98%
Class C | -0.02% | -0.02% | -0.05% | 100% | 100%
Class E | 0.00% | -0.02% | -0.05% | 101% | 99%
Overall | -0.01% | 0.00% | -0.01% | 100% | 99%
Class D | 0.01% | 0.03% | -0.13% | 100% | 99%
Class F (optional) | -0.05% | -0.14% | -0.08% | 101% | 100%
TGM | -0.30% | -0.40% | -0.40% | 102% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.04% | -0.05% | 100% | 102%
Class A2 | -0.04% | 0.07% | 0.02% | 99% | 99%
Class B | 0.00% | 0.06% | -0.10% | 100% | 100%
Class C | -0.01% | -0.17% | -0.03% | 100% | 100%
Class E |  |  |  |  | 
Overall | -0.01% | 0.00% | -0.05% | 100% | 100%
Class D | 0.00% | 0.08% | -0.06% | 99% | 100%
Class F (optional) | -0.10% | -0.08% | 0.02% | 99% | 101%
TGM | -0.30% | -0.13% | -0.21% | 99% | 102%

## Slide 8: Non-CE8: Proposed initialization + chroma interpolation
  Proposed + chroma_interpolation vs VTM-3.0
 | All Intra Main10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | 0.01% | 100% | 99%
Class A2 | -0.02% | 0.02% | -0.01% | 98% | 97%
Class B | -0.01% | 0.01% | 0.04% | 101% | 99%
Class C | -0.02% | -0.04% | 0.03% | 100% | 100%
Class E | 0.00% | 0.00% | 0.00% | 101% | 101%
Overall | -0.01% | -0.01% | 0.02% | 100% | 99%
Class D | 0.00% | 0.07% | -0.03% | 99% | 99%
Class F (optional) | -0.07% | -0.14% | -0.11% | 100% | 100%
TGM | -0.73% | -0.78% | -0.83% | 102% | 101%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-3.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.11% | 0.02% | 101% | 103%
Class A2 | -0.03% | -0.11% | -0.11% | 100% | 99%
Class B | 0.00% | 0.09% | -0.19% | 100% | 100%
Class C | -0.02% | -0.16% | 0.03% | 100% | 99%
Class E |  |  |  |  | 
Overall | -0.01% | -0.01% | -0.08% | 100% | 100%
Class D | 0.02% | 0.07% | 0.03% | 99% | 99%
Class F (optional) | -0.16% | -0.37% | -0.16% | 100% | 101%
TGM | -1.03% | -1.24% | -1.09% | 100% | 100%

## Slide 9: Non-CE8: block vector initialization for Chroma in Dual Tree
  Thanks Tencent for cross-checking the results
  This contribution proposes to establish CE tests on block vector initialization for Chroma in Dual Tree