## Slide 1: Non-CE8: CPR flag signaling at slice level (JVET-M0410)
X. Xu, X. Li, S. Liu (Tencent)
2019/01

## Slide 2: Summary
CPR mode is not enabled in VTM-3.0 CTC due to high encoder runtime with limited gain on natural contents
In this contribution, two aspects are proposed
  A slice level CPR flag
  An encoder algorithm based on hash key hit rate to adaptively switch CPR mode on/off at slice level
It is reported that with the proposed method:
  the runtime/BD rate changes for natural contents are negligible vs. CPR=0 case in VTM-3.0
  the runtime/BD rate changes for SCC contents are negligible vs. CPR=1 case in VTM-3.0

## Slide 3: Aspect #1
In current VTM, an sps flag sps_cpr_enabled_flag is used to control the used of CPR
It is proposed that a slice level flag slice_cpr_enabled_flag, is signaled in case that the sps flag is equal to 1
It is asserted that this provides more flexibility for CPR usage control (in case content switch)

## Slide 4: Aspect #2
With the presence of CPR slice level flag, it is proposed to turn CPR on/off based on the following facts:
  For natural contents, the hash hit rate is usually very low
  For screen contents, the hash hit rate is usually very high
An encoder algorithm is therefore proposed to turn CPR off for the next coded slice, if the overall hash key hit rate in current slice is below 3%
  Hash key hit is defined as a hash key value has more than 1 entry
  Hash key hit rate is defined as the percentage of hash key hits in hash table

## Slide 5: Simulation results
 | AI over VTM-3.0 |  |  |  | AI over VTM-3.0+CPR=1 |  |  | 
 | Y | U | V | Enc/Dec | Y | U | V | Enc/Dec Time
CTC | -0.01% | -0.02% | 0.00% | 103%/100% | 0.27% | 0.38% | 0.33% | 75%/99%
Class F | -11.96% | -11.90% | -11.97% | 151%/99% | 0.13% | 0.15% | 0.14% | 96%/100%
TGM | -36.92% | -36.11% | -36.36% | 141%/89% | 0.00% | 0.00% | 0.00% | 98%/100%
 | RA over VTM-3.0 |  |  |  | RA over VTM-3.0+CPR=1 |  |  | 
 | Y | U | V | Enc/Dec | Y | U | V | Enc/Dec Time
CTC | -0.01% | 0.04% | 0.08% | 101%/101% | -0.10% | 0.07% | 0.03% | 101%/101%
Class F | -9.81% | -9.87% | -9.96% | 107%/101% | 0.07% | 0.06% | 0.01% | 100%/102%
TGM | -22.22% | -21.92% | -22.42% | 104%/97% | 0.00% | 0.00% | 0.00% | 101%/102%
 | LB over VTM-3.0 |  |  |  | LB over VTM-3.0+CPR=1 |  |  | 
 | Y | U | V | Enc/Dec | Y | U | V | Enc/Dec Time
CTC | 0.13% | 0.15% | -0.08% | 103%/101% | 0.00% | -0.29% | -0.27% | 96%/101%
Class F | -5.16% | -5.37% | -5.30% | 107%/99% | 0.03% | 0.13% | 0.32% | 99%/100%
TGM | -13.20% | -13.59% | -13.80% | 110%/98% | 0.01% | 0.01% | 0.01% | 98%/100%

## Slide 6: Conclusion
In this contribution, two aspects are proposed
  A slice level CPR flag
  An encoder algorithm based on hash key hit rate to adaptively switch CPR mode on/off at slice level
It is reported that with the proposed method,
  the runtime/BD rate changes for natural contents are negligible vs. CPR=0 case in VTM-3.0
  the runtime/BD rate changes for SCC contents are negligible vs. CPR=1 case in VTM-3.0
It is recommended to adopt this proposal into next the VTM release
Thanks LGE for performing crosschecking!