## Slide 1: CE8-related: CPR mode signaling and interaction with inter coding tools
Wei-Jung Chien, Vadim Seregin, Marta Karczewicz

## Slide 2: Introduction
CPR in VTM3.0
  Bitstream conformance checks were added to disallow the inter tool combination between CPR and MMVD, Triangle partition, affine motion model, combined intra/inter prediction.
  Motion derivation process may treat CPR neighboring blocks as Inter blocks or intra blocks.
    MMVD – CPR is treated as intra mode
    Triangle partition – CPR is treated as intra mode
    Affine merge mode – CPR is treated as intra mode
    Pairwise average merge candidate can average two CPR merge canidate or two non-CPR merge candidate.
    CIIP – CPR is treated as inter mode

## Slide 3: Reference index signaling and bitstream conformance restrictions
Method 1: reference index signaling and bitstream conformance restrictions
  Remove all CPR dependency in MMVD, Trianglar, affine, ATMVP neighboring motion derivation.
Method 2: reference index signaling and bitstream conformance restrictions and disable pairwise merge candidate for CPR mode
  On top of Method 1, remove pairwise average from two CPR merge candidates.

## Slide 4: Block level flag signaling and independent CPR mode
Method 3: block level flag signaling and independent CPR mode
  Signal CPR as a third mode MODE_CPR, other than MODE_INTRA and MODE_INTER not through reference index signaling.
  Support skip_cpr, merge_cpr, inter_cpr, in I_SLICE
  Dual tree is enabled in I_SLICE only as in CTC.
  The derivation process of motion vectors for CPR mode excludes all neighboring blocks in inter mode and vice versa
  Separate HMVP buffer
  Allow pairwise average from two MODE_INTER, or two MODE_CPR.
  Currently, it disallows all other inter tools combined with CPR

## Slide 5: Simulation results – method 1
 | All Intra |  |  |  |  |  |  |  |  | 
 | Over VTM-3 |  |  |  |  | Over VTM-3 + CPR |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
CTC Overall | -0.27% | -0.40% | -0.33% | 133% | 102% | 0.00% | 0.00% | 0.00% | 99% | 100%
Class F | -12.09% | -12.04% | -12.10% | 150% | 99% | 0.00% | 0.00% | 0.00% | 97% | 99%
Class SCC 1080p | -36.92% | -36.11% | -36.36% | 139% | 91% | 0.00% | 0.00% | 0.00% | 98% | 99%
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM-3 |  |  |  |  | Over VTM-3 + CPR |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Overall | 0.09% | -0.01% | 0.04% | 99% | 100% | 0.00% | 0.00% | -0.01% | 100% | 100%
Class F | -9.93% | -9.98% | -9.98% | 102% | 96% | -0.03% | -0.02% | 0.01% | 97% | 99%
Class SCC 1080p | -22.02% | -21.58% | -22.12% | 101% | 97% | 0.00% | 0.00% | -0.03% | 98% | 99%
 | Low delay B |  |  |  |  |  |  |  |  | 
 | Over VTM-3 |  |  |  |  | Over VTM-3 + CPR |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Overall | 0.10% | 0.40% | 0.11% | 107% | 102% | -0.04% | 0.13% | 0.10% | 100% | 100%
Class F | -5.16% | -5.28% | -5.77% | 108% | 99% | -0.02% | 0.12% | -0.30% | 100% | 98%
Class SCC 1080p | -13.00% | -13.17% | -13.41% | 107% | 93% | 0.28% | 0.46% | 0.40% | 99% | 98%

## Slide 6: Simulation results – method 2
 | All Intra |  |  |  |  |  |  |  |  | 
 | Over VTM-3 |  |  |  |  | Over VTM-3 + CPR |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
CTC Overall | -0.26% | -0.38% | -0.32% | 132% | 102% | 0.01% | 0.02% | 0.02% | 98% | 100%
Class F | -12.05% | -12.06% | -11.92% | 152% | 102% | 0.05% | -0.02% | 0.20% | 98% | 102%
Class SCC 1080p | -36.87% | -36.07% | -36.33% | 139% | 91% | 0.08% | 0.07% | 0.04% | 98% | 101%
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM-3 |  |  |  |  | Over VTM-3 + CPR |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Overall | 0.07% | -0.07% | 0.05% | 99% | 100% | -0.02% | -0.06% | 0.00% | 100% | 100%
Class F | -9.85% | -9.89% | -10.03% | 104% | 98% | 0.06% | 0.09% | -0.03% | 100% | 102%
Class SCC 1080p | -21.95% | -21.56% | -22.05% | 103% | 98% | 0.09% | 0.03% | 0.06% | 100% | 101%
 | Low delay B |  |  |  |  |  |  |  |  | 
 | Over VTM-3 |  |  |  |  | Over VTM-3 + CPR |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Overall | 0.10% | 0.13% | 0.06% | 106% | 101% | -0.04% | -0.13% | 0.06% | 99% | 100%
Class F | -5.17% | -4.80% | -5.42% | 107% | 100% | -0.02% | 0.60% | 0.06% | 99% | 99%
Class SCC 1080p | -13.16% | -13.44% | -13.72% | 108% | 96% | 0.08% | 0.13% | 0.02% | 99% | 101%

## Slide 7: Simulation results – method 3
 | All Intra |  |  |  |  |  |  |  |  | 
 | Over VTM-3 |  |  |  |  | Over VTM-3 + CPR |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
CTC Overall | -0.39% | -0.42% | -0.42% | 139% | 98% | -0.12% | -0.03% | -0.09% | 103% | 96%
Class F | -12.25% | -12.18% | -12.12% | 157% | 100% | -0.19% | -0.17% | -0.05% | 101% | 100%
Class SCC 1080p | -37.14% | -36.30% | -36.56% | 142% | 87% | -0.37% | -0.31% | -0.35% | 100% | 100%
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM-3 |  |  |  |  | Over VTM-3 + CPR |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Overall | -0.05% | -0.27% | -0.35% | 101% | 96% | -0.14% | -0.26% | -0.39% | 101% | 96%
Class F | -10.09% | -10.07% | -10.10% | 107% | 95% | -0.22% | -0.13% | -0.13% | 103% | 99%
Class SCC 1080p | -22.90% | -22.56% | -23.06% | 108% | 94% | -1.08% | -1.19% | -1.18% | 104% | 97%
 | Low delay B |  |  |  |  |  |  |  |  | 
 | Over VTM-3 |  |  |  |  | Over VTM-3 + CPR |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Overall | -0.02% | -0.24% | -0.62% | 109% | 92% | -0.16% | -0.50% | -0.63% | 102% | 91%
Class F | -5.71% | -6.37% | -6.10% | 110% | 98% | -0.64% | -1.07% | -0.68% | 102% | 97%
Class SCC 1080p | -14.55% | -15.02% | -15.25% | 112% | 91% | -1.48% | -1.65% | -1.68% | 103% | 95%