## Slide 1
Reduced context models for transform coefficients coding (JVET-M0489)
Min Gao, Xiang Li, Xin Zhao, Shan Liu

## Slide 2
Syntax elements:
  Significant flag: sig_coeff_flag;
  Parity flag: par_level_flag;
  Greater flags: rem_abs_gt1_flag, rem_abs_gt2_flag
Contexts:
The Current Transform Coefficient Coding
d = x + y
sumAbs1 = sum of partially reconstructed absolute levels after first pass
numSig = number of transform coefficients with sig_coeff_flag == 1

## Slide 3
Context models for sig_coeff_flag:
  90 contexts ->60 contexts
The Proposed Method
Luma | 
Diagonal position | Context model index (sumAbs1)
d<2 | 12, 13, 14, 15, 16, 17
d<5 | 6, 7, 8, 9, 10, 11
d>=5 | 0, 1, 2, 3, 4, 5
Chroma | 
Diagonal position | Context model index (sumAbs1)
d<2 | 6, 7, 8, 9, 10, 11
d>=2 | 0, 1, 2, 3, 4, 5

## Slide 4
Contexts for parity flags and greater flags:
  96 contexts -> 72 contexts
The Proposed Method
Luma | 
Diagonal position | Context model index (sumAbs1 - numSig)
d=0 | 16, 17, 18, 19, 20
d<3 | 11, 12, 13, 14, 15
d<10 | 6, 7, 8, 9, 10
d>=10 | 1, 2, 3, 4, 5
Last non-zero coefficient | 0
Chroma | 
Diagonal position | Context model index (sumAbs1 - numSig)
d=0 | 6, 7, 8, 9, 10
d>0 | 1, 2, 3, 4, 5
Last non-zero coefficient | 0

## Slide 5
The proposed method vs Anchor VTM-3.0
Experimental Results:

## Slide 6
Share the context models among the transform coefficients to reduce the context models.
The proposed method can save 54 contexts (186->132) in total, at the cost of minor coding loss.
  The BD rate loss is 0.04%, 0.01%, 0.00% for AI, RA and LD configurations, respectively.
Conclusions:

## Slide 7
Thanks to Technicolor for cross-check!